#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2004/85

24 August 2004

# ORIGINAL: ENGLISH

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Twenty-sixth session, 29 November-3 December 2004

# Item 3(a) of the provisional agenda

OUTSTANDING ISSUES OR PROPOSALS OF AMENDMENTS TO THE RECOMMENDATIONS ON THE TRANSPORT OF DANGEROUS GOODS

Transport of gases

Proposal on low pressure Division 2.2 Gases

## Transmitted by the European Industrial Gases Association (EIGA)

Introduction

EIGA presented an informal paper at the twenty-fifth session to introduce a debate on the subject of the classification since it was concerned that classification of Division 2.2 is not applied uniformly in all the international agreements. As a result of that discussion, it was clear that a consensus for harmonisation was not yet available. However, as a small step forward, EIGA presents this formal proposal to make the classification more logical.  This proposal does not change the scope of application or effect of the Model Regulations.

Proposal

Amend Paragraph 2.2.2.1 (b) as follows (new words shown underlined).

(b)	Division 2.2	Non-flammable, non-toxic gases

Gases which are transported at a pressure not less than 280 kPa at 20 oC, or as a refrigerated liquids, and which:

- are asphyxiant – gases which dilute or replace the oxygen normally in the atmosphere; or

- are oxidising – gases which may, generally by providing oxygen, cause or contribute to the combustion or other material more than air does; or

- do not come under the other divisions;

NOTE:	Compressed, liquefied and dissolved gases which are transported at a pressure less than 280 kPa at 20 oC are not subject to these Regulations.

Justification

The process of assigning gases to one of three divisions is stated in 2.2.2.1 to be “based on the primary hazard of the gas during transport”. It is not a process of assessing the risk in transport. In the present text, the process of assigning a hazard division is mixed together with risk assessment. It is true that Division 2.2 gases at low pressure present a lower risk in transport than the same gases transported at higher pressure, but their hazards are not absent at low pressure.

As it stands the definition of Division 2.2 precludes any allocation of hazard to gases which happen to be at low pressure.  If, for example, nitrogen is packed at 200 kPa, it is impossible to classify it as UN 1066. This is equivalent to stating that nitrogen is not an asphyxiant when at low pressure.

The new formulation proposed above is more logical. Classification is completed in all cases and then it is made clear that low pressure Division 2.2 gases which are not refrigerated liquid are exempted from the Regulations. This is clearer and more transparent foundation for the regulation of Division 2.2.

##### Safety implications

None.

##### Feasibility

No problem.

##### Enforceability

Made easier by clarifying the status of low pressure gases.

_______________

# Text boxes

STSTE

Secretariat