ECONOMIC COMMISSION FOR EUROPE				INF.29

INLAND TRANSPORT COMMITTEE

Working Party on the transport of dangerous goods

Joint Meeting of the RID Safety Committee

and the Working Party on the Transport of

Dangerous Goods

(Geneva, 13-17 September 2004)

### Chapter 6.2; Stampmarking

##### Reinstatement of the note in paragraph 6.2.1.7.6

##### Transmitted by the European Industrial Gases Association (EIGA)

###### Introduction

Editions of the ADR/RID prior to 2005 contained a note which allowed pressure receptacles containing gases whose periods between inspections were 10 years or more to be stamped with the year of the periodic inspection only.  In harmonising the 2005 ADR/RID with the 13th Revision of the UN Model Regulations, this note has been lost.

###### Proposal

The Joint Meeting is requested to insert the following note at the end of paragraph 6.2.1.7.6.  This note was in previous editions of the ADR/RID and is reproduced below exactly as it appeared.  Furthermore, EIGA requests that this note should be published in a corrigendum to the 2005 editions of the ADR and RID.

NOTE: The month need not be indicated for gases for which the interval between periodic inspection is ten years or more (see 4.1.4.1 packing instructions P200 (9) and P203 (8)).

______________