Distr.
	GÉNÉRALE

ST/SG/AC.10/C.3/2005/34
	2 septembre 2005

FRANÇAIS
	Original: ANGLAIS

COMITÉ D’EXPERTS DU TRANSPORT DES MARCHANDISES
DANGEREUSES ET DU SYSTÈME GÉNÉRAL HARMONISÉ
DE CLASSIFICATION ET D’ÉTIQUETAGE
DES PRODUITS CHIMIQUES

Sous-Comité d’experts du transport des marchandises dangereuses

Vingt-huitième session, 28 novembre-7 décembre 2005
Point 5 de l’ordre du jour provisoire

INSCRIPTION, CLASSEMENT ET EMBALLAGE

Instructions de transport en citernes mobiles pour les numéros ONU 3129, 3148, 3131 et 2813

Transmis par l’expert des États-Unis d’Amérique

1.	Introduction

Actuellement, aucune instruction de transport en citernes mobiles n’est affectée aux liquides hydroréactifs, n.s.a, aux liquides hydroréactifs, corrosifs, n.s.a, ou aux rubriques du Groupe d’emballage 1 concernant les solides hydroréactifs, n.s.a, et les solides hydroréactifs, corrosifs, n.s.a. Il est proposé d’introduire des affectations conformes aux «Règles d’affectation de dispositions spéciales pour le transport en citernes mobiles aux matières des classes 3 à 9» (voir ST/SG/AC.10/25/Add.2). Ces affectations sont conformes aux rubriques classées de la même façon dans la Liste des marchandises dangereuses (voir l’annexe).

2.	Proposition

Ajouter de nouvelles instructions de transport en citernes mobiles et dispositions spéciales de transport en citernes mobiles aux rubriques suivantes de la Liste des marchandises dangereuses comme suit:

| No ONU | Nom et description | Groupe d’emballage | Citernes mobiles et conteneurs pour vrac |
| --- | --- | --- | --- |
|  |  |  | Instructions | Dispositions spéciales |
| 3129 | Liquide hydroréactif, corrosif, n.s.a. | I | T10 | TP2 TP9 |
|  |  | II | T7 | TP2 |
|  |  | III | T7 | TP1 |
| 3148 | Liquide hydroréactif, n.s.a. | I | T9 | TP2 TP9 |
|  |  | II | T7 | TP2 |
|  |  | III | T7 | TP1 |
| 3131 | Solide hydroréactif, corrosif, n.s.a. | I | T9 | TP33, TP9 |
| 2813 | Solide hydroréactif, n.s.a. | I | T9 | TP33, TP9 |

Annex (English only)

Current Tank Assignments for 4.3 Liquid and Solid Substances

| UN No | Name and Description | Class or Division | Subsi-diary risk | UN packing group | Special provisions | Tank Instruction | Tank Special Provision |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 3401 | ALKALI METAL AMALGAM, SOLID | 4.3 |  | I | 182 | T9 | TP7 TP33 |
| 1390 | ALKALI METAL AMIDES | 4.3 |  | II | 182 | T3 | TP33 |
| 1393 | ALKALINE EARTH METAL ALLOY, N.O.S. | 4.3 |  | II |  | T3 | TP33 |
| 3402 | ALKALINE EARTH METAL AMALGAM, SOLID | 4.3 |  | I | 183 | T9 | TP7 TP33 |
| 1394 | ALUMINIUM CARBIDE | 4.3 |  | II |  | T3 | TP33 |
| 1395 | ALUMINIUM FERROSILICON POWDER | 4.3 | 6.1 | II |  | T3 | TP33 |
| 1396 | ALUMINIUM POWDER, UNCOATED | 4.3 |  | II |  | T3 | TP33 |
| 1396 | ALUMINIUM POWDER, UNCOATED | 4.3 |  | III | 223 | T1 | TP33 |
| 1398 | ALUMINIUM SILICON POWDER, UNCOATED | 4.3 |  | III | 37 223 | T1 | TP33 |
| 3170 | ALUMINIUM SMELTING BY-PRODUCTS or ALUMINIUM REMELTING BY-PRODUCTS | 4.3 |  | II | 244 | T3 BK1 BK2 | TP33 |
| 3170 | ALUMINIUM SMELTING BY-PRODUCTS or ALUMINIUM REMELTING BY-PRODUCTS | 4.3 |  | III | 223 244 | T1 BK1 BK2 | TP33 |
| 1400 | BARIUM | 4.3 |  | II |  | T3 | TP33 |
| 2965 | BORON TRIFLUORIDE DIMETHYL ETHERATE | 4.3 | 3 8 | I |  | T10 | TP2 TP7 |
| 1401 | CALCIUM | 4.3 |  | II |  | T3 | TP33 |
| 1402 | CALCIUM CARBIDE | 4.3 |  | I |  | T9 | TP7 TP33 |
| 1402 | CALCIUM CARBIDE | 4.3 |  | II |  | T3 | TP33 |
| 1403 | CALCIUM CYANAMIDE with more than 0.1% calcium carbide | 4.3 |  | III | 38 | T1 | TP33 |
| 2844 | CALCIUM MANGANESE SILICON | 4.3 |  | III |  | T1 | TP33 |
| 1405 | CALCIUM SILICIDE | 4.3 |  | II |  | T3 | TP33 |
| 1405 | CALCIUM SILICIDE | 4.3 |  | III | 223 | T1 | TP33 |
| 3078 | CERIUM, turnings or gritty powder | 4.3 |  | II |  | T3 | TP33 |
| 2988 | CHLOROSILANES, WATER-REACTIVE, FLAMMABLE, CORROSIVE, N.O.S. | 4.3 | 3 8 | I |  | T10 | TP2 TP7 TP9 TP13 |
| 1183 | ETHYLDICHLOROSILANE | 4.3 | 3 8 | I |  | T10 | TP2 TP7 TP13 |
| 1408 | FERROSILICON with 30% or more but less than 90% silicon | 4.3 | 6.1 | III | 39 223 | T1 BK2 | TP33 |
| 2830 | LITHIUM FERROSILICON | 4.3 |  | II |  | T3 | TP33 |
| 2805 | LITHIUM HYDRIDE, FUSED SOLID | 4.3 |  | II |  | T3 | TP33 |
| 1417 | LITHIUM SILICON | 4.3 |  | II |  | T3 | TP33 |
| 2950 | MAGNESIUM GRANULES, COATED, particle size not less than 149 microns | 4.3 |  | III |  | T1 BK2 | TP33 |
| 1418 | MAGNESIUM POWDER or MAGNESIUM ALLOYS POWDER | 4.3 | 4.2 | II |  | T3 | TP33 |
| 1418 | MAGNESIUM POWDER or MAGNESIUM ALLOYS POWDER | 4.3 | 4.2 | III | 223 | T1 | TP33 |
| 2624 | MAGNESIUM SILICIDE | 4.3 |  | II |  | T3 | TP33 |
| 2968 | MANEB, STABILIZED or MANEB PREPARATION, STABILIZED against self-heating | 4.3 |  | III | 223 | T1 | TP33 |
| 1409 | METAL HYDRIDES, WATER-REACTIVE, N.O.S. | 4.3 |  | II | 274 | T3 | TP33 |
| 3208 | METALLIC SUBSTANCE, WATER-REACTIVE, N.O.S. | 4.3 |  | II | 274 | T3 | TP33 |
| 3208 | METALLIC SUBSTANCE, WATER-REACTIVE, N.O.S. | 4.3 |  | III | 223 274 | T1 | TP33 |
| 3209 | METALLIC SUBSTANCE, WATER-REACTIVE, SELF-HEATING, N.O.S. | 4.3 | 4.2 | II | 274 | T3 | TP33 |
| 3209 | METALLIC SUBSTANCE, WATER-REACTIVE, SELF-HEATING, N.O.S. | 4.3 | 4.2 | III | 223 274 | T1 | TP33 |
| 1242 | METHYLDI-CHLOROSILANE | 4.3 | 3 8 | I |  | T10 | TP2 TP7 TP13 |
| 3398 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER-REACTIVE | 4.3 |  | I | 274 | T13 | TP2 TP7 |
| 3398 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER-REACTIVE | 4.3 |  | II | 274 | T7 | TP2 TP7 |
| 3398 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER-REACTIVE | 4.3 |  | III | 223 274 | T7 | TP2 TP7 |
| 3399 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER-REACTIVE, FLAMMABLE | 4.3 | 3 | I | 274 | T13 | TP2 TP7 |
| 3399 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER-REACTIVE, FLAMMABLE | 4.3 | 3 | II | 274 | T7 | TP2 TP7 |
| 3399 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER-REACTIVE, FLAMMABLE | 4.3 | 3 | III | 223 274 | T7 | TP2 TP7 |
| 3395 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER-REACTIVE | 4.3 |  | I | 274 | T9 | TP7 TP33 |
| 3395 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER-REACTIVE | 4.3 |  | II | 274 | T3 | TP33 |
| 3395 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER-REACTIVE | 4.3 |  | III | 223 274 | T1 | TP33 |
| 3396 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER-REACTIVE, FLAMMABLE | 4.3 | 4.1 | I | 274 | T9 | TP7 TP33 |
| 3396 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER-REACTIVE, FLAMMABLE | 4.3 | 4.1 | II | 274 | T3 | TP33 |
| 3396 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER-REACTIVE, FLAMMABLE | 4.3 | 4.1 | III | 223 274 | T1 | TP33 |
| 3397 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER-REACTIVE, SELF-HEATING | 4.3 | 4.2 | I | 274 | T9 | TP7 TP33 |
| 3397 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER-REACTIVE, SELF-HEATING | 4.3 | 4.2 | II | 274 | T3 | TP33 |
| 3397 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER-REACTIVE, SELF-HEATING | 4.3 | 4.2 | III | 223 274 | T1 | TP33 |
| 1340 | PHOSPHORUS PENTASULPHIDE, free from yellow and white phosphorus | 4.3 | 4.1 | II |  | T3 | TP33 |
| 2257 | POTASSIUM | 4.3 |  | I |  | T9 | TP7 TP33 |
| 3403 | POTASSIUM METAL ALLOYS, SOLID | 4.3 |  | I |  | T9 | TP7 TP33 |
| 1422 | POTASSIUM SODIUM ALLOYS, LIQUID | 4.3 |  | I |  | T9 | TP3 TP7 TP31 |
| 3404 | POTASSIUM SODIUM ALLOYS, SOLID | 4.3 |  | I |  | T9 | TP7 TP33 |
| 1428 | SODIUM | 4.3 |  | I |  | T9 | TP7 TP33 |
| 2835 | SODIUM ALUMINIUM HYDRIDE | 4.3 |  | II |  | T3 | TP33 |
| 1295 | TRICHLOROSILANE | 4.3 | 3 8 | I |  | T14 | TP2 TP7 TP13 |
| 3131 | WATER-REACTIVE SOLID, CORROSIVE, N.O.S. | 4.3 | 8 | II | 274 | T3 | TP33 |
| 3131 | WATER-REACTIVE SOLID, CORROSIVE, N.O.S. | 4.3 | 8 | III | 223 274 | T1 | TP33 |
| 3132 | WATER-REACTIVE SOLID, FLAMMABLE, N.O.S. | 4.3 | 4.1 | II | 274 | T3 | TP33 |
| 3132 | WATER-REACTIVE SOLID, FLAMMABLE, N.O.S. | 4.3 | 4.1 | III | 223 274 | T1 | TP33 |
| 2813 | WATER-REACTIVE SOLID, N.O.S. | 4.3 |  | II | 274 | T3 | TP33 |
| 2813 | WATER-REACTIVE SOLID, N.O.S. | 4.3 |  | III | 223 274 | T1 | TP33 |
| 3135 | WATER-REACTIVE SOLID, SELF-HEATING, N.O.S. | 4.3 | 4.2 | II | 274 | T3 | TP33 |
| 3135 | WATER-REACTIVE SOLID, SELF-HEATING, N.O.S. | 4.3 | 4.2 | III | 223 274 | T1 | TP33 |
| 3134 | WATER-REACTIVE SOLID, TOXIC, N.O.S. | 4.3 | 6.1 | II | 274 | T3 | TP33 |
| 3134 | WATER-REACTIVE SOLID, TOXIC, N.O.S. | 4.3 | 6.1 | III | 223 274 | T1 | TP33 |
| 1435 | ZINC ASHES | 4.3 |  | III | 223 | T1 | TP33 |
| 1436 | ZINC POWDER or ZINC DUST | 4.3 | 4.2 | II |  | T3 | TP33 |
| 1436 | ZINC POWDER or ZINC DUST | 4.3 | 4.2 | III | 223 | T1 | TP33 |

-----

# Text boxes

NATIONS UNIES

Secrétariat

ST