# UN/SCETDG/27/INF.7

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the

Transport of Dangerous Goods

Twenty-seventh session

Geneva, 4-8 July 2005

Item 3 (a) of the provisional agenda

# EXPLOSIVES, SELF-REACTIVE SUBSTANCES AND ORGANIC PEROXIDES

# Test series 8

# Comments on documents ST/SG/AC.10/C.3/2005/11 and ST/SG/AC.10/C.3/2005/14

##### Transmitted by the expert from Sweden

# Introduction

After the informal Working Group Meeting on Ammonium Nitrate Emulsions (ANE), Suspensions and Gels and Test Series 8 in February 2005, a series of tests on different ANE-formulations were made using the modified vented pipe test (MVPT) proposed as Test Series 8d.

These tests were made in Finland, 18 – 22 April 2005. The different ANEs came from the companies Orica Mining Services, Kimit AB, Forcit OY and Dyno Nobel ASA. Personnel from these companies were also present during the tests.

# Test results

A total of twelve tests were made. In one test (FEM5) the ANE was out of specification and this test is thereby discarded. Of the remaining eleven tests 6 tests were made by two formulations (i.e. 3 tests per formulation), these were FEM1, 2 and 12 in one group and FEM3, 6 and 7 in another group.

In two of the tests detonations occurred, i.e. those ANEs did not pass the test. However a number of those that passed the test were very close to failure.

Two interesting observations can be made from these tests:

(1) 	Viscosity seems to be a vital parameter, formulations with low viscosity passes the test easier than those with high viscosity.

(2)	Identical samples (i.e. from the same formulation) can behave differently as shown by both event time and observation of test 3, 6 and 7. The event time had values between 83 and 107 minutes!

A summary of the tests is shown in table 1, annex A.

Conclusions

Sweden still believes that a large-scale 8d test is necessary. However in view of the latest test results we doubt that the MVPT is correct for this purpose.

Proposal

Sweden therefore proposes that the MVPT is not accepted as the 8d test.

| Table 1 |
| --- |
| Test | Code of emulsion / composition | Viscosity (Pa*s) | Vent (mm) | Heating rate (C/min) | Observations | Event time (min) | Vessel state | Pictures / plot |
| 1 | FEM1; AN (76-79), water (16-18), Oil (4.5-5.5), emulsifier (1.0-2.0) | 370 | 90 | 3.4 | Fuming vigorously and venting | 94 | Undamaged | 10 |
| 2 | FEM2; Same as 1 | 370 | 87 | 3.4 | Fuming vigorously and venting | 85 | Undamaged | 11 |
| 3 | FEM3; AN (68-72), SN (8-11), water (13-17), Oil (4.0-5.5), emulsifier (1.0-2.0) | 355 | 87 | 3.4 | Fuming vigorously - material ejected in chunks | 83 | Undamaged | 14 |
| 4 | FEM4 AN (66-69), SN (13-16), water (11-13), Oil (4.8-5.2), emulsifier (1.6-2.3) | 900 | 90 |  | Material out of specification |  |  |  |
| 5 | FEM5; AN (61-65), SN (10-14), water (14-16), Oil (3.2-4.1), emulsifier (1.05-1.5) | 450 | 87 | 3.3 | Detonation | 98 | Fragmented | 18 |
| 6 | FEM6; Same as 3 | 355 | 87 | 3.5 | Vented - frost on propane bottles | 107 | Undamaged | 15 |
| 7 | FEM7; Same as 3 | 355 | 87 | 3.5 | Vented | 97 | Undamaged | 16 |
| 8 | FEM8; AN (61-65%), SN (10-14), water (14-16), Oil (3.2-4.1), emulsifier (1.05-1.5) | 1270 | 87 | 3.5 | Detonation - strong fuming, MB* Sensitised | 78 | Fragmented | 19 |
| 9 | FEM9; AN (61-65), SN (10-14), water (14-16), Oil (3.2-4.1), emulsifier (1.05-1.5) | 670 | 87 | 3.5 | Fumes and fire – aluminised product | 88 | Undamaged | 20 |
| 10 | FEM10; AN (73-76), water (17-19), Oil (5.05-5.5), emulsifier (1.5-2.5) | 280 | 100 | 3.5 | Strong venting - red fumes | 95 | Undamaged | 13 |
| 11 | FEM11; AN (66-70), SN (3-6); water (16-20), Oil (4.5-5.5), emulsifier (0.9-1.5) | 460 | 100 | 3.5 | Strong fuming, then venting and noise | 69 | Undamaged | 17 |
| 12 | FEM12; Same as 1 | 370 | 87 | 3.5 | Just strong fuming for 10 minutes | 82 | Undamaged | 12 |

Viscosity was measured with Helipath spindle D @1.0 rpm, MB*. - Microballoons