# UN/SCETDG/27/INF.11

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the

Transport of Dangerous Goods

Twenty-seventh session

Geneva, 4-8 July 2005

Item 7 of the provisional agenda

MISCELLANEOUS PROPOSALS OF AMENDMENTS TO THE Model regulations

ON THE TRANSPORT OF DANGEROUS GOODS

### Viscosity and flash point in accordance with the table in 32.3.1.7

Transmitted by the expert from Austria

#### Introduction

Existing text:

“32.3.1.7 Viscous flammable liquids such as paints, enamels, varnishes, adhesives and polishes with a flash point of less than 23 °C are included in packing group III provided that:

………

(c) 	The viscosity and flash point are in accordance with the following table:

| Flow-time | Jet diameter | Flash point |
| --- | --- | --- |
| t (s) | (mm) | ( °C) |
| 20 < t 60 | 4 | above 17 |
| 60 < t 100 | 4 | above 10 |
| 20 < t 32 | 6 | above 5 |
| 32 < t 44 | 6 | above -1 |
| 44 < t 100 | 6 | above -5 |
| 100 < t | 6 | -5 and below |

(d) 	The capacity of the receptacle used does not exceed 450 litres.”

#### Proposal

Eliminate the entry “-5 and below” and insert “no limit”.

| Flow-time | Jet diameter | Flash point |
| --- | --- | --- |
| t (s) | (mm) | ( °C) |
| 20 < t 60 | 4 | above 17 |
| 60 < t 100 | 4 | above 10 |
| 20 < t 32 | 6 | above 5 |
| 32 < t 44 | 6 | above -1 |
| 44 < t 100 | 6 | above -5 |
| 100 < t | 6 | no limit |

#### Justification

The table gives a relation between the viscosity and the flashpoint of a liquid for shifting the classification from PG II to PG III. A substance with a high viscosity is less dangerous and may therefore have a lower flash point. So one would expect the last line should be something like “above –10°C”.

The current version means that a substance with a flow time greater 100 seconds and a flash point above –5 °C (which is less dangerous than substances with a flashpoint below –5 °C) is not covered by this table and therefore PG II instead of PG III does apply.

______________