# UN/SCETDG/27/INF.23

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the

Transport of Dangerous Goods

Twenty-seventh session

Geneva, 4-8 July 2005

# Item 11 of the provisional agenda

GUIDING PRINCIPLES FOR THE MODEL REGULATIONS

Transmitted by the expert from the United States of America

1.	The expert from the United States of America has undertaken a review of the portable tank special provisions (TP notes) in order to establish a rationalized approach that can be incorporated into the Guiding Principles for the Model Regulations.  This guidance will be useful when new substances are added to the UN Model Regulations and as a basis for reviewing the current assignments to ensure that they have been consistently and appropriately applied to existing substances.  During a review of the TP notes proposals for improving the notes were developed.  On this basis, the Sub-Committee is invited to consider a number of amendments to the existing special provisions.  A proposed TP note rationalized approach is provided in the annex to this paper.

Proposals:

2.	It is proposed that the Sub-Committee adopt the annexed rationalized approach for the assignment of portable tank special provisions, and that it be incorporated into the Guiding Principles document within the Guidelines for Assigning Portable Tank Requirements to Substances in Classes 3 to 9.

3.	It is proposed that the following changes be made to the existing portable tank special provisions:

- Delete TP6.  This provision is not necessary. Pressure-relief devices are already required for all substances and these requirements are referenced within the Portable Tank Instructions and in Chapter 6.7 (see 6.7.2.7.1). TP6 repeats what is already stated in Chapter 6.7.

- Consider the deletion of TP9.  This TP note is unnecessary and burdensome to both consignors and competent authorities because it mandates that a competent authority approval be issued.  The entries assigned TP9 are n.o.s. entries that already have tank instructions and special provisions indicated in the Dangerous Goods List.  Over the last several years, the competent authority of the United States of America has issued numerous TP9 approvals for the transport of substances assigned TP9, and in every case the approval authorization has been identical to that authorized by the tank instructions and Special Provisions shown in the Dangerous Goods List. It is recommended that TP9 be deleted. A list of substances assigned TP9 is attached as Annex 2.

Annex 1

Part III

Guidelines for assigning portable tank special provisions (TP notes) to individual substances:

Portable tank special provisions must be considered on an individual basis depending on the characteristics of the substances.  The following guidance shall be used:

TP1	The degree of filling prescribed in 4.2.1.9.2 shall not be exceeded

TP1 applies to liquid materials with a vapor pressure of not more than 175 kPa (1.75 bar) having a primary or subsidiary hazard of:

Class 3, PG II

Class 3, PG III

Division 5.1 PG II

Division 6.1 PG III

Class 8 PG III

TP2 	The degree of filling prescribed in 4.2.1.9.3 shall not be exceeded

TP2 applies to liquid materials with a vapor pressure of not more than 175 kPa (1.75 bar) and also to materials having a primary or subsidiary hazard of:

Class 3, PG I

Class 3 PG II (with a vapor pressure greater than 175 kPa (1.75 bar))

Division 4.2 PG I

Division 4.3 (all PG)

Division 5.1 PG I

Division 6.1 PG I or PG II

Class 8 PG I and II

TP3 		The maximum degree of filling (in %) for solids transported above their melting points and for elevated temperature liquids shall be determined in accordance with 4.2.1.9.5.

TP3 applies to solids transported above their melting point and to elevated temperature liquids.

TP4 	The degree of filling shall not exceed 90% or, alternatively, any other value approved by the competent authority (see 4.2.1.15.2).

TP4 applies to low specific activity radioactive materials authorized for transport in portable tanks, and to stabilized sulphur trioxide.

TP5 	The degree of filling prescribed in 4.2.3.6 shall be met.

TP5 applies to materials transported as refrigerated liquids.

TP6 	To prevent the tank bursting in any event, including fire engulfment, it shall be provided with pressure-relief devices which are adequate in relation to the capacity of the tank and to the nature of the substance transported. The device shall also be compatible with the substance.

Propose to delete.  The applicable tank instructions and provisions of Chapter 6.7 already establish adequate pressure relief requirements.

TP7 	Air shall be eliminated from the vapour space by nitrogen or other means.

TP7 applies to pyrophoric or water reactive materials.

TP8 	The test pressure for the portable tank may be reduced to 1.5 bar when the flash point of the substances transported is greater than 0 °C.

TP8 applies to certain flammable liquids with a flash point greater than 0 °C.

TP9 	A substance under this description shall only be transported in a portable tank under an approval granted by the competent authority.

Propose to delete.

TP10 	A lead lining, not less than 5 mm thick, which shall be tested annually, or another suitable lining material approved by the competent authority is required.

TP10 applies to bromine or bromine solutions.

TP12 	This substance is highly corrosive to steel.

TP12 applies to all substances which are highly corrosive to steel .

TP13 	Self-contained breathing apparatus shall be provided when this substance is transported.

TP13 applies to substances which are toxic by inhalation.

TP16 	The tank shall be fitted with a special device to prevent under-pressure and excess pressure during normal transport conditions. This device shall be approved by the competent authority. Pressure-relief requirements are as indicated in 6.7.2.8.3 to prevent crystallization of the product in the pressure-relief valve.

TP16 is applies to ammonium nitrate, liquid (hot concentrated solution).

TP17	Only inorganic non-combustible materials shall be used for thermal insulation of the tank.

TP17 applies to blasting explosives and blasting agents of types B or E, ammonium nitrate, liquid (hot concentrated solution), and to ammonium nitrate emulsions, suspensions, or gels.

TP18 	Temperature shall be maintained between 18 °C and 40 °C. Portable tanks containing solidified methacrylic acid shall not be reheated during transport.

TP18 applies to stabilized methacrylic acid.

TP19 	The calculated shell thickness shall be increased by 3 mm. Shell thickness shall be verified ultrasonically at intervals midway between periodic hydraulic tests.

TP19 applies to sulphur dioxide and chlorine.

TP20 	This substance shall only be transported in insulated tanks under a nitrogen blanket.

TP20 applies to ethylene oxide, or ethylene oxide with nitrogen, up to a total pressure of 1 MPa (10 bar) at 50 (C.

TP21 	The shell thickness shall be not less than 8 mm. Tanks shall be hydraulically tested and internally inspected at intervals not exceeding 2.5 years.

TP21 applies to dinitrogen tetroxide and trifluoroacetyl chloride.

TP22 	Lubricant for joints or other devices shall be oxygen compatible.

TP22 applies to refrigerated liquids containing oxygen.

TP23 	Transport permitted under special conditions prescribed by the competent authorities.

TP23 applies to hydrogen, refrigerated liquid.

TP24	The portable tank may be fitted with a device located under maximum filling conditions in the vapour space of the shell to prevent the build up of excess pressure due to the slow decomposition of the substance transported. This device shall also prevent an unacceptable amount of leakage of liquid in the case of overturning or entry of foreign matter into the tank. This device shall be approved by the competent authority or its authorized body.

TP24 applies to substances liable to build up excess pressure due to decomposition.

TP25	Sulphur trioxide 99.95% pure and above may be transported in tanks without an inhibitor provided that it is maintained at a temperature equal to or above 32.5 °C.

TP25 applies to stabilized sulphur trioxide.

TP26	When transported under heated conditions, the heating device shall be fitted outside the shell. For UN 3176 this requirement only applies when the substance reacts dangerously with water.

TP26 applies to materials transported in a molten state which react dangerously with water.

TP27	A portable tank having a minimum test pressure of 4 bar may be used if it is shown that a test pressure of 4 bar or less is acceptable according to the test pressure definition in 6.7.2.1.

TP27 applies when a higher test pressure has been assigned to a substance on the basis of its generic nomenclature, but it can be shown that a test pressure of 4 bar or less is acceptable according to the test pressure definition in 6.7.2.1 for the particular substance transported.

TP28	A portable tank having a minimum test pressure of 2.65 bar may be used if it is shown that a test pressure of 2.65 bar or less is acceptable according to the test pressure definition in 6.7.2.1.

TP28 applies when a higher test pressure has been assigned to a substance on the basis of its generic nomenclature, but it can be shown that a test pressure of 2.65 bar or less is acceptable according to the test pressure definition in 6.7.2.1 for the particular substance transported.

TP29 	A portable tank having a minimum test pressure of 1.5 bar may be used if it is shown that a test pressure of 1.5 bar or less is acceptable according to the test pressure definition in 6.7.2.1.

TP3 applies when a higher test pressure has been assigned to a substance on the basis of its generic nomenclature, but it can be shown that a test pressure of 1.5 bar or less is acceptable according to the test pressure definition in 6.7.2.1 for the particular substance transported.

TP30	This substance shall be transported in insulated tanks.

TP30 applies to stabilized methacrylic acid.

TP31 	This substance may only be transported in tanks in the solid state.

TP31 applies to certain materials whose proper shipping name authorizes a solid and a liquid state but whose portable tank instruction and special provisions only apply to the solid state.

TP32 	For UN Nos. 0331, 0332 and 3375, portable tanks may be used subject to the following conditions:

(a)	To avoid unnecessary confinement, each portable tank constructed of metal shall be fitted with a pressure-relief device that may be of the reclosing spring-loaded type, a frangible disc or a fusible element.  The set to discharge or burst pressure, as applicable, shall not be greater than 2.65 bar for portable tanks with minimum test pressures greater than 4 bar;

(b)	The suitability for transport in tanks shall be demonstrated.  One method to evaluate this suitability is test 8 (d) in Test Series 8 (see "Manual of Tests and Criteria", Part 1, sub-section 18.7).

(c)	Substances shall not be allowed to remain in the portable tank for any period that could result in caking.  Appropriate measures shall be taken to avoid accumulation and packing of substances in the tank (e.g. cleaning, etc).

TP32 applies to blasting explosives and blasting agents of types B or E, ammonium nitrate, liquid (hot concentrated solution), and to ammonium nitrate emulsions, suspensions, or gels.

TP33 	The portable tank instruction assigned for this substance applies for granular and powdered solids and for solids which are filled and discharged at temperatures above their melting point which are cooled and transported as a solid mass. For solids which are transported above their melting point see 4.2.1.18.

TP33 applies to certain granular and powdered solids and to certain solids which are filled and discharged at temperatures above their melting point which are cooled and transported as a solid mass.

TP34 	Portable tanks need not be subjected to the impact test in 6.7.4.14.1 if the portable tank is marked "NOT FOR RAIL TRANSPORT" on the plate specified in 6.7.4.15.1 and also in letters of at least 10 cm high on both sides of the outer jacket.

TP34 applies to hydrogen, refrigerated liquid and helium, refrigerated liquid.

Annex 2

Substances assigned TP9 in the UN Model Regulations 13th revised edition

| UN | Name | Portable Tank SP | Class | PG | Sub-Risk | SP | TI |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1993 | FLAMMABLE LIQUID, N.O.S. | TP1 TP9 TP27 | 3 | I |  | 274 | T11 |
| 3295 | HYDROCARBONS, LIQUID, N.O.S. | TP1 TP8 TP9 TP28 | 3 | I |  |  | T11 |
| 1989 | ALDEHYDES, N.O.S. | TP1 TP9 TP27 | 3 | I |  | 274 | T11 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. or PETROLEUM PRODUCTS, N.O.S. | TP1 TP8 TP9 | 3 | I |  |  | T11 |
| 1992 | FLAMMABLE LIQUID, TOXIC, N.O.S. | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 3021 | PESTICIDE, LIQUID,FLAMMABLE, TOXIC, N.O.S., flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 3273 | NITRILES, FLAMMABLE, TOXIC, N.O.S. | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 2776 | COPPER BASED PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 2758 | CARBAMATE PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 3346 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 1986 | ALCOHOLS, FLAMMABLE, TOXIC, N.O.S. | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 2760 | ARSENICAL PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 3350 | PYRETHROID PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 1988 | ALDEHYDES, FLAMMABLE, TOXIC, N.O.S. | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 2772 | THIOCARBAMATE PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 2778 | MERCURY BASED PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 2782 | BIPYRIDILIUM PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 2762 | ORGANOCHLORINE PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 2784 | ORGANOPHOSPHORUS PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 3024 | COUMARIN DERIVATIVE PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 2764 | TRIAZINE PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 2780 | SUBSTITUTED NITROPHENOL PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 2787 | ORGANOTIN PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 3286 | FLAMMABLE LIQUID, TOXIC, CORROSIVE, N.O.S. | TP2 TP9 TP13 TP27 | 3 | I | 6.1 8 | 274 | T14 |
| 2924 | FLAMMABLE LIQUID, CORROSIVE, N.O.S. | TP2 TP9 | 3 | I | 8 | 274 | T14 |
| 2733 | AMINES, FLAMMABLE, CORROSIVE, N.O.S. or POLYAMINES, FLAMMABLE, CORROSIVE, N.O.S. | TP1 TP9 TP27 | 3 | I | 8 | 274 | T14 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. or PETROLEUM PRODUCTS, N.O.S. | TP1 TP8 TP9 TP28 | 3 | II |  |  | T7 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. or PETROLEUM PRODUCTS, N.O.S. | TP1 TP9 TP29 | 3 | III |  | 223 | T4 |
| 3200 | PYROPHORIC SOLID, INORGANIC, N.O.S. | TP7 TP9 TP33 | 4.2 | I |  | 274 | T21 |
| 1383 | PYROPHORIC METAL, N.O.S. or PYROPHORIC ALLOY, N.O.S. | TP7 TP9 TP33 | 4.2 | I |  | 274 | T21 |
| 2845 | PYROPHORIC LIQUID, ORGANIC, N.O.S. | TP2 TP7 TP9 | 4.2 | I |  | 274 | T22 |
| 3051 | ALUMINIUM ALKYLS | TP2 TP7 TP9 | 4.2 | I | 4.3 | 320 | T21 |
| 3052 | ALUMINIUM ALKYL HALIDES, LIQUID | TP2 TP7 TP9 | 4.2 | I | 4.3 | 320 | T21 |
| 2988 | CHLOROSILANES, WATER-REACTIVE, FLAMMABLE, CORROSIVE, N.O.S. | TP2 TP7 TP9 TP13 | 4.3 | I | 3 8 |  | T10 |
| 3375 | AMMONIUM NITRATE EMULSION or SUSPENSION or GEL, intermediate for blasting explosives | TP1 TP9 TP17 TP32 | 5.1 | II |  | 309 | T1 T2 |
| 1935 | CYANIDE SOLUTION, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I |  |  | T14 |
| 3440 | SELENIUM COMPOUND, LIQUID, N.O.S. | TP2 TP9 TP27 | 6.1 | I |  |  | T14 |
| 3020 | ORGANOTIN PESTICIDE, LIQUID, TOXIC | TP2 TP9 TP13 TP27 | 6.1 | I |  | 61 274 | T14 |
| 3026 | COUMARIN DERIVATIVE PESTICIDE, LIQUID, TOXIC | TP2 TP9 TP13 TP27 | 6.1 | I |  | 61 274 | T14 |
| 2788 | ORGANOTIN COMPOUND, LIQUID, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I |  | 43 274 | T14 |
| 2902 | PESTICIDE, LIQUID, TOXIC, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I |  | 61 274 | T14 |
| 3018 | ORGANOPHOSPHORUS PESTICIDE, LIQUID, TOXIC | TP2 TP9 TP13 TP27 | 6.1 | I |  | 61 274 | T14 |
| 3352 | PYRETHROID PESTICIDE, LIQUID, TOXIC | TP2 TP9 TP13 TP27 | 6.1 | I |  | 61 274 | T14 |
| 2998 | TRIAZINE PESTICIDE, LIQUID, TOXIC | TP2 TP9 TP13 TP27 | 6.1 | I |  | 61 274 | T14 |
| 3348 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, LIQUID, TOXIC | TP2 TP9 TP13 TP27 | 6.1 | I |  | 61 274 | T14 |
| 3016 | BIPYRIDILIUM PESTICIDE, LIQUID, TOXIC | TP2 TP9 TP13 TP27 | 6.1 | I |  | 61 274 | T14 |
| 3014 | SUBSTITUTED NITROPHENOL PESTICIDE, LIQUID, TOXIC | TP2 TP9 TP13 TP27 | 6.1 | I |  | 61 274 | T14 |
| 3012 | MERCURY BASED PESTICIDE, LIQUID, TOXIC | TP2 TP9 TP13 TP27 | 6.1 | I |  | 61 274 | T14 |
| 3010 | COPPER BASED PESTICIDE, LIQUID, TOXIC | TP2 TP9 TP13 TP27 | 6.1 | I |  | 61 274 | T14 |
| 1556 | ARSENIC COMPOUND, LIQUID, N.O.S., inorganic, including: Arsenates, n.o.s., Arsenites, n.o.s.; and Arsenic sulphides, n.o.s. | TP2 TP9 TP13 TP27 | 6.1 | I |  | 43 | T14 |
| 2996 | ORGANOCHLORINE PESTICIDE, LIQUID, TOXIC | TP2 TP9 TP13 TP27 | 6.1 | I |  | 61 274 | T14 |
| 3006 | THIOCARBAMATE PESTICIDE, LIQUID, TOXIC | TP2 TP9 TP13 | 6.1 | I |  | 61 274 | T14 |
| 3276 | NITRILES, TOXIC, LIQUID, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I |  | 274 315 | T14 |
| 3278 | ORGANOPHOSPHORUS COMPOUND, TOXIC, LIQUID, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I |  | 43 274 315 | T14 |
| 3281 | METAL CARBONYLS, LIQUID, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I |  | 274 315 | T14 |
| 3280 | ORGANOARSENIC COMPOUND, LIQUID, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I |  | 274 315 | T14 |
| 3282 | ORGANOMETALLIC COMPOUND, TOXIC, LIQUID, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I |  | 274 | T14 |
| 3287 | TOXIC LIQUID, INORGANIC, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I |  | 274 315 | T14 |
| 2810 | TOXIC LIQUID, ORGANIC, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I |  | 274 315 | T14 |
| 2992 | CARBAMATE PESTICIDE, LIQUID, TOXIC | TP2 TP9 TP13 TP27 | 6.1 | I |  | 61 274 | T14 |
| 2994 | ARSENICAL PESTICIDE, LIQUID, TOXIC | TP2 TP9 TP13 TP27 | 6.1 | I |  | 61 274 | T14 |
| 3382 | TOXIC BY INHALATION LIQUID, N.O.S. with an inhalation toxicity lower than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50 | TP2 TP9 TP13 | 6.1 | I |  | 274 | T20 |
| 3381 | TOXIC BY INHALATION LIQUID, N.O.S. with an inhalation toxicity lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50 | TP2 TP9 TP13 | 6.1 | I |  | 274 | T22 |
| 2588 | PESTICIDE, SOLID, TOXIC, N.O.S. | TP9 TP33 | 6.1 | I |  | 61 274 | T6 |
| 2026 | PHENYLMERCURIC COMPOUND, N.O.S. | TP9 TP33 | 6.1 | I |  | 43 | T6 |
| 3467 | ORGANOMETALLIC COMPOUND, TOXIC, SOLID, N.O.S. | TP9 TP33 | 6.1 | I |  | 274 | T6 |
| 2811 | TOXIC SOLID, ORGANIC, N.O.S. | TP9 TP33 | 6.1 | I |  | 274 | T6 |
| 3284 | TELLURIUM COMPOUND, N.O.S. | TP9 TP33 | 6.1 | I |  |  | T6 |
| 3466 | METAL CARBONYLS, SOLID, N.O.S. | TP9 TP33 | 6.1 | I |  | 274 | T6 |
| 3465 | ORGANOARSENIC COMPOUND, SOLID, N.O.S. | TP9 TP33 | 6.1 | I |  | 274 | T6 |
| 3464 | ORGANOPHOSPHORUS COMPOUND, TOXIC, SOLID, N.O.S. | TP9 TP33 | 6.1 | I |  | 43 274 | T6 |
| 3462 | TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. | TP9 TP33 | 6.1 | I |  | 210 274 | T6 |
| 3448 | TEAR GAS SUBSTANCE, SOLID, N.O.S. | TP9 TP33 | 6.1 | I |  | 274 | T6 |
| 3439 | NITRILES, TOXIC, SOLID, N.O.S. | TP9 TP33 | 6.1 | I |  | 274 | T6 |
| 3349 | PYRETHROID PESTICIDE, SOLID, TOXIC | TP9 TP33 | 6.1 | I |  | 61 274 | T6 |
| 3345 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, SOLID, TOXIC | TP9 TP33 | 6.1 | I |  | 61 274 | T6 |
| 1544 | ALKALOIDS, SOLID, N.O.S. or ALKALOID SALTS, SOLID, N.O.S. | TP9 TP33 | 6.1 | I |  | 43 274 | T6 |
| 3288 | TOXIC SOLID, INORGANIC, N.O.S. | TP9 TP33 | 6.1 | I |  | 274 | T6 |
| 3285 | VANADIUM COMPOUND, N.O.S. | TP9 TP33 | 6.1 | I |  |  | T6 |
| 3283 | SELENIUM COMPOUND, SOLID, N.O.S. | TP9 TP33 | 6.1 | I |  |  | T6 |
| 1655 | NICOTINE COMPOUND, SOLID, N.O.S. or NICOTINE PREPARATION, SOLID, N.O.S. | TP9 TP33 | 6.1 | I |  | 43 | T6 |
| 2025 | MERCURY COMPOUND, SOLID, N.O.S. | TP9 TP33 | 6.1 | I |  | 43 66 | T6 |
| 3143 | DYE, SOLID, TOXIC, N.O.S. or DYE INTERMEDIATE, SOLID, TOXIC, N.O.S. | TP9 TP33 | 6.1 | I |  | 274 | T6 |
| 3146 | ORGANOTIN COMPOUND, SOLID, N.O.S. | TP9 TP33 | 6.1 | I |  | 43 274 | T6 |
| 1588 | CYANIDES, INORGANIC, SOLID, N.O.S. | TP9 TP33 | 6.1 | I |  | 47 274 | T6 |
| 1557 | ARSENIC COMPOUND, SOLID, N.O.S., inorganic, including: Arsenates, n.o.s.; Arsenites, n.o.s.; and Arsenic sulphides, n.o.s. | TP9 TP33 | 6.1 | I |  | 43 | T6 |
| 1601 | DISINFECTANT, SOLID, TOXIC, N.O.S. | TP9 TP33 | 6.1 | I |  | 274 | T6 |
| 3019 | ORGANOTIN PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash point not less than 23 °C | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 61 274 | T14 |
| 3017 | ORGANOPHOSPHORUS PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash point not less than 23 °C | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 61 274 | T14 |
| 2903 | PESTICIDE, LIQUID, TOXIC, FLAMMABLE, N.O.S., flash point not less than 23 °C | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 61 274 | T14 |
| 3351 | PYRETHROID PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash point not less than 23 °C | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 61 274 | T14 |
| 2997 | TRIAZINE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash point not less than 23 °C | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 61 274 | T14 |
| 3015 | BIPYRIDILIUM PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash point not less than 23 °C | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 61 274 | T14 |
| 2929 | TOXIC LIQUID, FLAMMABLE, ORGANIC, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 274 315 | T14 |
| 2993 | ARSENICAL PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash point not less than 23 °C | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 61 274 | T14 |
| 3013 | SUBSTITUTED NITROPHENOL PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash point not less than 23 °C | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 61 274 | T14 |
| 3009 | COPPER BASED PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash point not less than 23 °C | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 61 274 | T14 |
| 3025 | COUMARIN DERIVATIVE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash point not less than 23 °C | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 61 274 | T14 |
| 2991 | CARBAMATE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash point not less than 23 °C | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 61 274 | T14 |
| 3011 | MERCURY BASED PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash point not less than 23 °C | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 61 274 | T14 |
| 2995 | ORGANOCHLORINE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash point not less than 23 °C | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 61 274 | T14 |
| 3279 | ORGANOPHOSPHORUS COMPOUND, TOXIC, FLAMMABLE, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 43 274 315 | T14 |
| 3347 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash point not less than 23 °C | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 61 274 | T14 |
| 3005 | THIOCARBAMATE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash point not less than 23 °C | TP2 TP9 TP13 | 6.1 | I | 3 | 61 274 | T14 |
| 3275 | NITRILES, TOXIC, FLAMMABLE, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 274 315 | T14 |
| 3384 | TOXIC BY INHALATION LIQUID, FLAMMABLE, N.O.S. with an inhalation toxicity lower than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50 | TP2 TP9 TP13 | 6.1 | I | 3 | 274 | T20 |
| 3383 | TOXIC BY INHALATION LIQUID, FLAMMABLE, N.O.S. with an inhalation toxicity lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50 | TP2 TP9 TP13 | 6.1 | I | 3 | 274 | T22 |
| 2930 | TOXIC SOLID, FLAMMABLE, ORGANIC, N.O.S. | TP9 TP33 | 6.1 | I | 4.1 | 274 | T6 |
| 3124 | TOXIC SOLID, SELF-HEATING, N.O.S. | TP9 TP33 | 6.1 | I | 4.2 | 274 | T6 |
| 3386 | TOXIC BY INHALATION LIQUID, WATER-REACTIVE, N.O.S. with an inhalation toxicity lower than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50 | TP2 TP9 TP13 | 6.1 | I | 4.3 | 274 | T20 |
| 3385 | TOXIC BY INHALATION LIQUID, WATER-REACTIVE, N.O.S. with an inhalation toxicity lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50 | TP2 TP9 TP13 | 6.1 | I | 4.3 | 274 | T22 |
| 3125 | TOXIC SOLID, WATER-REACTIVE, N.O.S. | TP9 TP33 | 6.1 | I | 4.3 | 274 | T6 |
| 3388 | TOXIC BY INHALATION LIQUID, OXIDIZING, N.O.S. with an inhalation toxicity lower than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50 | TP2 TP9 TP13 | 6.1 | I | 5.1 | 274 | T20 |
| 3387 | TOXIC BY INHALATION LIQUID, OXIDIZING, N.O.S. with an inhalation toxicity lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50 | TP2 TP9 TP13 | 6.1 | I | 5.1 | 274 | T22 |
| 3086 | TOXIC SOLID, OXIDIZING, N.O.S. | TP9 TP33 | 6.1 | I | 5.1 | 274 | T6 |
| 3289 | TOXIC LIQUID, CORROSIVE, INORGANIC, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I | 8 | 274 315 | T14 |
| 2927 | TOXIC LIQUID, CORROSIVE, ORGANIC, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I | 8 | 274 315 | T14 |
| 3390 | TOXIC BY INHALATION LIQUID, CORROSIVE, N.O.S. with an inhalation toxicity lower than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50 | TP2 TP9 TP13 | 6.1 | I | 8 | 274 | T20 |
| 3389 | TOXIC BY INHALATION LIQUID, CORROSIVE, N.O.S. with an inhalation toxicity lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50 | TP2 TP9 TP13 | 6.1 | I | 8 | 274 | T22 |
| 2928 | TOXIC SOLID, CORROSIVE, ORGANIC, N.O.S. | TP9 TP33 | 6.1 | I | 8 | 274 | T6 |
| 3290 | TOXIC SOLID, CORROSIVE, INORGANIC, N.O.S. | TP9 TP33 | 6.1 | I | 8 | 274 | T6 |
| 2735 | AMINES, LIQUID, CORROSIVE, N.O.S. or POLYAMINES, LIQUID, CORROSIVE, N.O.S. | TP2 TP9 TP27 | 8 | I |  | 274 | T14 |
| 3267 | CORROSIVE LIQUID, BASIC, ORGANIC, N.O.S. | TP2 TP9 TP27 | 8 | I |  | 274 | T14 |
| 1760 | CORROSIVE LIQUID, N.O.S. | TP2 TP9 TP27 | 8 | I |  | 274 | T14 |
| 3265 | CORROSIVE LIQUID, ACIDIC, ORGANIC, N.O.S. | TP2 TP9 TP27 | 8 | I |  | 274 | T14 |
| 3264 | CORROSIVE LIQUID, ACIDIC, INORGANIC, N.O.S. | TP2 TP9 TP27 | 8 | I |  | 274 | T14 |
| 3145 | ALKYLPHENOLS, LIQUID, N.O.S. (including C2-C12 homologues) | TP2 TP9 | 8 | I |  |  | T14 |
| 2801 | DYE, LIQUID, CORROSIVE, N.O.S. or DYE INTERMEDIATE, LIQUID, CORROSIVE, N.O.S. | TP2 TP9 TP27 | 8 | I |  | 274 | T14 |
| 3266 | CORROSIVE LIQUID, BASIC, INORGANIC, N.O.S. | TP2 TP9 TP27 | 8 | I |  | 274 | T14 |
| 3147 | DYE, SOLID, CORROSIVE, N.O.S. or DYE INTERMEDIATE, SOLID, CORROSIVE, N.O.S. | TP9 TP33 | 8 | I |  | 274 | T6 |
| 3263 | CORROSIVE SOLID, BASIC, ORGANIC, N.O.S. | TP9 TP33 | 8 | I |  | 274 | T6 |
| 1759 | CORROSIVE SOLID, N.O.S. | TP9 TP33 | 8 | I |  | 274 | T6 |
| 3262 | CORROSIVE SOLID, BASIC, INORGANIC, N.O.S. | TP9 TP33 | 8 | I |  | 274 | T6 |
| 3261 | CORROSIVE SOLID, ACIDIC, ORGANIC, N.O.S. | TP9 TP33 | 8 | I |  | 274 | T6 |
| 3259 | AMINES, SOLID, CORROSIVE, N.O.S. or POLYAMINES, SOLID, CORROSIVE, N.O.S. | TP9 TP33 | 8 | I |  | 274 | T6 |
| 2430 | ALKYLPHENOLS, SOLID, N.O.S. (including C2-C12 homologues) | TP9 TP33 | 8 | I |  |  | T6 |
| 3260 | CORROSIVE SOLID, ACIDIC, INORGANIC, N.O.S. | TP9 TP33 | 8 | I |  | 274 | T6 |
| 2734 | AMINES, LIQUID, CORROSIVE, FLAMMABLE, N.O.S. or POLYAMINES, LIQUID, CORROSIVE, FLAMMABLE, N.O.S. | TP2 TP9 TP27 | 8 | I | 3 | 274 | T14 |
| 2920 | CORROSIVE LIQUID, FLAMMABLE, N.O.S. | TP2 TP9 TP27 | 8 | I | 3 | 274 | T14 |
| 2921 | CORROSIVE SOLID, FLAMMABLE, N.O.S. | TP9 TP33 | 8 | I | 4.1 | 274 | T6 |
| 3095 | CORROSIVE SOLID, SELF-HEATING, N.O.S. | TP9 TP33 | 8 | I | 4.2 | 274 | T6 |
| 3096 | CORROSIVE SOLID, WATER-REACTIVE, N.O.S. | TP9 TP33 | 8 | I | 4.3 | 274 | T6 |
| 3084 | CORROSIVE SOLID, OXIDIZING, N.O.S. | TP9 TP33 | 8 | I | 5.1 | 274 | T6 |
| 2922 | CORROSIVE LIQUID, TOXIC, N.O.S. | TP2 TP9 TP13 TP27 | 8 | I | 6.1 | 274 | T14 |
| 2923 | CORROSIVE SOLID, TOXIC, N.O.S. | TP9 TP33 | 8 | I | 6.1 | 274 | T6 |

________________