# UN/SCETDG/28/INF.17

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the

Transport of Dangerous Goods

Twenty-eighth session

Geneva, 28 November – 7 December 2005

Item 5 of the provisional agenda

LISTING, CLASSIFICATION AND PACKING

Comments on ST/SG/AC.10/C.3/2005/27

Transmitted by the International Council of Chemical Associations (ICCA)

Introduction

In its proposal ST/SG/AC.10/C.3/2005/27, the expert from Germany rightfully draws the attention to an inconsistency in the second entry of Nitric acid as UN 2031 i.e. Nitric acid, with not more than 70% nitric acid.

Indeed according to the UN Manual of Tests and Criteria (34.4.2.4.2), Nitric acid with a concentration higher than 65% of nitric acid should be assigned a (sub)risk 5.1. Therefore ICCA agrees that Nitric acid, with a concentration of between 65% and 70% of nitric acid, should be assigned a subsidiary risk 5.1.

Nitric acid in this concentration range is being transported in big quantities in IBC’s. As a consequence of the amendments proposed by Germany, which actually reduces the cut-off value between PG I and PG II from 70% to 65%, Nitric acid in this concentration range would now be assigned to PG I. This would mean that Nitric acid in this concentration range would no longer be allowed to be transported in IBC’s.

However, Nitric acid belongs to class 8 (not division 5.1) and ICCA is not aware of any new evidence on the corrosivity of Nitric acid in the concentration range 65-70%. Therefore ICCA is of the opinion that there is no scientific basis to justify this “upgrade” from PG II into PG I for Nitric acid in the concentration range between 65 and 70%.

Proposal

ICCA is therefore proposing the following amendments in the Dangerous Goods List:

- amend the description in column 2 of the entry for UN 2031, PG II from “NITRIC ACID, other than red fuming, with not more than 70% nitric acid” into “NITRIC ACID, other than red fuming, with at least 65%, but not more than 70% nitric acid” and add 5.1 as subsidiary risk (column 4)

- create a separate entry for “NITRIC ACID, other than red fuming, with less than 65% nitric acid”, PG II, without a subsidiary risk, but with all other provisions identical to those for UN 2031, PG II, subsidiary risk 5.1

See table below

ICCA proposal

| UN No. | Name and description | Class or division | Subsi-diary risk | UN packing group | Special provi-sions | Limited quantities | Packagings and IBCs | Portable tanks and bulk containers |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | Packing instruction | Special packing provisions | Instruc-tions | Special provisions |
| 2031 | NITRIC ACID, other than red fuming, with more than 70% nitric acid | 8 | 5.1 | I |  | NONE | P001 | PP81 | T10 | TP2 TP12 TP13 |
|  | NITRIC ACID, other than red fuming, with at least 65%, but not more than 70% nitric acid | 8 | 5.1 | II |  | 1 L | P001 IBC02 | PP81 | T8 | TP2 TP12 |
|  | NITRIC ACID, other than red fuming, with less than 65% nitric acid | 8 |  | II |  | 1 L | P001 IBC02 | PP81 | T8 | TP2 TP12 |

In order to facilitate the comparison with the current provisions, the current entries for UN 2031 have been reproduced below:

Current provisions for UN 2031 (14th revised edition of the UN Model Regulations)

| UN No. | Name and description | Class or division | Subsi-diary risk | UN packing group | Special provi-sions | Limited quantities | Packagings and IBCs | Portable tanks and bulk containers |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | Packing instruction | Special packing provisions | Instruc-tions | Special provisions |
| 2031 | NITRIC ACID, other than red fuming, with more than 70% nitric acid | 8 | 5.1 | I |  | NONE | P001 | PP81 | T10 | TP2 TP12 TP13 |
|  | NITRIC ACID, other than red fuming, with not more than 70% nitric acid | 8 |  | II |  | 1 L | P001 IBC02 | PP81 | T8 | TP2 TP12 |

_____________