| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL TRANS/WP.15/AC.2/2005/3 23 September 2004 ENGLISH Original: FRENCH |

### ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

Working Party on the Transport of Dangerous Goods

Joint Meeting of Experts on the Regulations annexed to the
European Agreement concerning the International Carriage
of Dangerous Goods by Inland Waterways (ADN)*
(Ninth session, Geneva, 24-28 January 2005,
agenda item 4)

# PROPOSALS FOR AMENDMENTS TO THE REGULATIONS
ANNEXED TO ADN**

## Table C

## Transmitted by the Central Commission for the Navigation of the Rhine (CCNR)

The Central Commission for the Navigation of the Rhine (CCNR) proposes the following amendments to table C of the Regulations annexed to ADN 2005.

3.2.3	Amend as follows:

Column (9)

Amend as follows:

“1.	(no change)

2.	Possibility of heating the cargo

3.	(no change)

4.	Cargo heating system on board”

Column (20)

Remark 6:

Replace the first two paragraphs by the following:

“6.	When external temperatures are below or equal to that indicated in column (20), the substance may only be carried in tank vessels equipped with a cargo heating system.”

(remainder unchanged)

Remark 34:

Beginning, amend to read:

“34.	For type N carriage, the flanges …” (remainder unchanged)

Add the following new remarks:

“35.	A direct system for the cargo heating system is not permitted for this substance.

36.	Only an indirect system for the cargo heating system is permitted for this substance.

37.	For this substance, the cargo tank system shall be capable of resisting the vapour pressure of the cargo at higher ambient temperatures whatever the system adopted for the boil-off gas.

38.	When the initial melting point of these mixtures in accordance with standard ASTM D86-01 is above 60° C, the transport requirements for packing group II are applicable.”

Note by the UNECE secretariat:

The UNECE secretariat notes that there is a difference between ADN and ADNR in the use of upper-case letters in column (2) of table C and suggests that ADN should be brought into line with ADNR.

Amend the entries of table C as follows:

| UN number | Column | Amendment |
| --- | --- | --- |
| 1010 3rd position* | 2 | Read: BUTADIENE, STABILIZED or MIXTURES OF BUTADIENE AND HYDROCARBONS, STABILIZED, having a vapour pressure at 70° C not exceeding 1.1 MPa (11 bar) and a density at 50° C not lower than 0.525 kg/l |
| 1170 1st position | 12 | Delete: “- 0.87” |
| 1202 1st position | 2 | Add: “(flash-point not more than 61° C)” |
|  | 12 | Insert: “< 0.85” |
| 1307 1st position | 4 | Replace “II” by “III” |
|  | 19 | Replace “1” by “0” |
| 1307 3rd position | 9 | Insert “2” |
| 1578 1st position | 2 | Read: “CHLORONITROBENZENES, SOLID, MOLTEN (p-CHLORONITROBENZENE)” |
| 1578 2nd position | 2 | Read: “CHLORONITROBENZENES, SOLID, MOLTEN (p-CHLORONITROBENZENE)” |
|  | 9 | Replace “2” by “4” |
| 1662 1st position | 20 | Insert: “6:+10° C” |
| 1662 2nd position |  | Delete |
| 1663 2nd position | 9 | Replace “2” by “4” |
| 1708 3rd and 4th positions |  | Delete |
| 1750 2nd position | 8 | Replace “2” by “1” |
|  | 9 | Replace “2” by “4” |
|  | 20 | Add: “26” |
| 1805 1st position | 2 | Read: “PHOSPHORIC ACID, SOLUTION, WITH MORE THAN 80% (VOLUME) ACID” |
|  | 12 | Insert: “> 1.6” |
| 1805 2nd position | 2 | Read: “PHOSPHORIC ACID, SOLUTION, WITH 80% (VOLUME) ACID, OR LESS” |
| 1823 | 9 | Replace “2” by “4” |
| 1987 6th and 7th positions | 2 | End, add: “(CYCLOHEXANOL)” |
| 1987 7th position | 9 | Replace “2” by “4” |
| 1999 | 2 | Does not concern the French version |
| 2045 | 20 | Delete: “7” Insert: “15; 23” |
| 2078 2nd position | 8 | Replace “2” by “1” |
|  | 9 | Replace “2” by “4” |
|  | 20 | Add: “26” |
| 2206 | 9 | Replace “2” by “4” |
| 2215 2nd position | 9 | Replace “2” by “4” |
| 2218 | 9 | Insert: “4” |
| 2280 2nd position | 9 | Replace “2” by “4” |
| 2303 | 20 | Delete: “16” |
| 2312 both positions | 9 | Replace “2” by “4” |
| 2321 | 9 | Replace “2” by “4” |
| 2430 2nd position | 8 | Replace “3” by “1” |
|  | 9 | Replace “2” by “4” |
| 2448 | 9 | Replace “2” by “4” |
| 2531 | 9 | Replace “2” by “4” |
| 2811 2nd and 4th positions | 9 | Replace “2” by “4” |
| 3175 | 9 | Replace “2” by “4” |
| 3257 both positions | 9 | Replace “2” by “4” |
| 3446 2nd position | 9 | Replace “2” by “4” |
| 3451 2nd position | 9 | Replace “2” by “4” |
| 3455 2nd position | 9 | Replace “2” by “4” |
| 9001 | 2 | Read: “SUBSTANCES WITH A FLASH-POINT ABOVE 61° C handed over for carriage or carried at a TEMPERATURE WITHIN A RANGE OF 15 K BELOW THEIR FLASH-POINT or SUBSTANCES WITH A FLASH-POINT > 61° C, HEATED TO LESS THAN 15 K FROM THE FLASH-POINT” |
| 9003 all positions | 2 | After “100° C”, insert “or SUBSTANCES WHERE 61° C < flash-point ≤ 100° C” |
| 9004 | 9 | Replace “2” by “4” |

*  Note by the UNECE secretariat:  The description in lower case should be deleted in the first two positions.

Insert as appropriate:

| UN No. or substance identification No. | Name and description | Class | Classification code | Packing group | Labels | Type of tank vessel | Cargo tank design | Cargo tank type | Cargo tank equipment | Opening pressure of the high-velocity vent valve in kPa | Maximum degree of filling in % | Relative density at 20° C | Type of sampling device | Pump room below deck permitted | Temperature class | Explosion group | Anti-explosion protection required | Equipment required | Number of cones/blue lights | Additional requirements/remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| (1) | (2) | 3 (a) | 3 (b) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) | (12) | (13) | (14) | (15) | (16) | (17) | (18) | (19) | (20) |
| 1202 | DIESEL FUEL in accordance with standard EN 590:1993 or GAS OIL or HEATING OIL (LIGHT) with a flash-point defined in standard EN 590:1993 | 3 | F1 | III | 3 | N | 4 | 2 |  |  | 97 | 0.82-0.85 | 3 | Yes |  |  | No | PP | 0 |  |
| 1202 | DIESEL FUEL or GAS OIL or HEATING OIL (LIGHT) (flash-point between 61° C and 100° C) | 3 | F1 | III | 3 | N | 4 | 2 |  |  | 97 | < 1.1 | 3 | Yes |  |  | No | PP | 0 |  |
| 1267 | PETROLEUM CRUDE OIL vp 50 ≤ 110 kPa | 3 | F1 | I | 3 | N | 2 | 2 |  | 10 | 97 |  | 3 | Yes | T43 | II B4 | Yes | PP, EX, A | 1 | 14; 29 |
| 1267 | PETROLEUM CRUDE OIL WITH MORE THAN 10% BENZENE vp 50 ≤ 110 kPa BOILING POINT ≤ 60° C | 3 | F1 | I | 3 | C | 1 | 1 |  |  | 95 |  | 1 | Yes | T43 | II B4 | Yes | PP, EX, A | 1 | 29 |
| 1267 | PETROLEUM CRUDE OIL WITH MORE THAN 10% BENZENE vp 50 ≤ 110 kPa BOILING POINT ≤ 60° C | 3 | F1 | I | 3 | C | 2 | 2 | 3 | 50 | 95 |  | 1 | Yes | T43 | II B4 | Yes | PP, EX, A | 1 | 23; 29 |
| 1267 | PETROLEUM CRUDE OIL WITH MORE THAN 10% BENZENE vp 50 ≤ 110 kPa BOILING POINT ≤ 60° C | 3 | F1 | II | 3 | C | 2 | 2 | 3 | 50 | 95 |  | 1 | Yes | T43 | II B4 | Yes | PP, EX, A | 1 | 23; 29; 38 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. or PETROLEUM PRODUCTS, N.O.S. 110 kPa < vp 50 ≤ 175 kPa | 3 | F1 | I | 3 | N | 2 | 2 |  | 50 | 97 |  | 3 | Yes | T43 | II B4 | Yes | PP, EX, A | 1 | 14; 27; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. OR PETROLEUM PRODUCTS, N.O.S. 110 kPa < vp 50 ≤ 150 kPa | 3 | F1 | I | 3 | N | 2 | 2 | 3 | 10 | 97 |  | 3 | Yes | T43 | II B4 | Yes | PP, EX, A | 1 | 14; 27; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. or PETROLEUM PRODUCTS, N.O.S. vp 50 ≤ 110 kPa | 3 | F1 | I | 3 | N | 2 | 2 |  | 10 | 97 |  | 3 | Yes | T43 | II B4 | Yes | PP, EX, A | 1 | 14; 27; 29 |
| 1268 | PETROLEUM DISTILLATES, WITH MORE THAN 10% BENZENE or PETROLEUM PRODUCTS, N.O.S. WITH MORE THAN 10% BENZENE vp 50 ≤ 110 kPa BOILING POINT < 60° C | 3 | F1 | I | 3 | C | 1 | 1 |  |  | 95 |  | 1 | Yes | T43 | II B4 | Yes | PP, EX, A | 1 | 27; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. WITH MORE THAN 10% BENZENE or PETROLEUM PRODUCTS, N.O.S. WITH MORE THAN 10% BENZENE vp 50 ≤ 110 kPa BOILING POINT ≤ 60° C | 3 | F1 | I | 3 | C | 2 | 2 | 3 | 50 | 95 |  | 1 | Yes | T43 | II B4 | Yes | PP, EX, A | 1 | 23; 27; 29 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. WITH MORE THAN 10% BENZENE or PETROLEUM PRODUCTS, N.O.S. WITH MORE THAN 10 % BENZENE vp 50 ≤ 110 kPa BOILING POINT ≤ 60° C | 3 | F1 | II | 3 | C | 2 | 2 | 3 | 50 | 95 |  | 1 | Yes | T43 | II B4 | Yes | PP, EX, A | 1 | 23; 27; 29; 38 |
| 2381 | DIMENTHYL DISULPHIDE | 3 | F1 | II | 3 | C | 2 | 2 |  | 40 | 95 | 1.063 | 2 | Yes | T2 | II B | Yes | PP, EX, A | 1 |  |
| 2582 | FERRIC CHLORIDE SOLUTION | 8 | C1 | III | 8 | N | 4 | 3 |  |  | 97 | 1.45 | 3 | Yes |  |  | No | PP, EP | 0 | 22; 30; 34 |
| 2785 | 4-THIAPENTANAL (3-METHYL MERCAPTO- PROPIONALDEHYDE) | 6.1 | T1 | III | 6.1 | C | 2 | 2 |  | 25 | 95 | 1.04 | 2 | No |  |  | No | PP, EP, TOX, A | 0 |  |
| 3295 | HYDROCARBONS, LIQUID, N.O.S. (… WITH MORE THAN 10% BENZENE) vp 50 < 110 kPa BOILING POINT < 60° C | 3 | F1 | II | 3 | C | 2 | 2 | 3 | 50 | 95 |  | 1 | Yes | T43 | II B4 | Yes | PP, EX, A | 1 | 23; 27; 29; 38 |

# Footnotes

*  This meeting is organized jointly by the Economic Commission for Europe and the Central Commission for the Navigation of the Rhine.

**  Distributed in German by the Central Commission for the Navigation of the Rhine under the symbol CCNR/ZKR/ADN/WP.15/AC.2/2005/3.

GE.04-23703  (E)    081104    101104

# Text boxes

-----