Comment to TRANS/WP.29/GRE/2005/21 (Draft amendments to Regulation No. 45)

Japanese comments are marked in bold, italic and red coloured characters.

A.	PROPOSAL

Paragraph 7.1., the diagram of measuring points on a screen, replace the existing diagram by:

"

"

Paragraphs 7.3.1. and 7.3.2., amend to read:

"7.3.1.	for headlamps approved in respect of the passing beam only, the measuring points are shown on the sketches in paragraph 7.2. 7.1.  5　4/

Measuring points:

Regulation No. 98 Class D or Regulation No. 112 Class A and B;  50 R(L) and 50V  4/

Regulation No. 98 Class E or Regulation No. 112 Class C;  Test point 1 and 2  4/

7.3.2.	for headlamps approved in respect of the passing beam and the driving beam, the measuring points are shown on the sketches in paragraph 7.2. 7.1

Measuring points:

Regulation No. 98 Class D or Regulation No. 112 Class A and B;  50 R(L)  4/

Regulation No. 98 Class E or Regulation No. 112 Class C;  Test point 1  4/

(the points 50/V and No. 2 are measured if in the same headlamps, different optic systems for the driving lamp and the passing lamp are provided)."

Footnote 5 4/, amend to read:

"5 4/	R refers to right-hand traffic (RHT).

L refers to left-hand traffic (LHT)."

B.	JUSTIFICATION

In order to clarify the measuring points, we added the specific measuring points according to the manner of the current sentence in paragraphs 7.3.1. and 7.3.2., as shown in the above.

- - - - -