#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2006/11

24 March 2006

Original: ENGLISH

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Twenty-ninth session

# Geneva, 3-12 (a.m.) July 2006

# Item 6 of the provisional agenda

LISTING, CLASSIFICATION AND PACKING

Amendments to provisions for chlorosilanes

Transmitted by the International Council of Chemical Associations (ICCA)

1.	Background

Chlorosilanes are intermediates used to manufacture siloxanes and silanes, the building blocks for many silicone products. Chlorosilanes are therefore not found in final applications. All chlorosilanes react readily with water to form corrosive and toxic hydrogen chloride gas and hydrochloric acid. These substances therefore need to be handled and transported with care by producers and customers.

In order to further enhance the safe transport of chlorosilanes, the silicone manufacturers of Europe (CES: Centre Européen des Silicones), of North-America (SEHSC: Silicones Environmental, Health and Safety Council) and of Japan (SIAJ: Silicone Industry Association of Japan) are of the opinion that a number of provisions related to chlorosilanes should be revisited.

2.	Discussion

The list of substances concerned can be found in Annex 1.

2.1 	Packing group (Column 5)

Whereas all chlorosilanes of class 3 are classified as Class 3, subsidiary risk 8, PG II, there are currently two chlorosilanes, Methyltrichlorosilane (UN1250) and Vinyltrichlorosilane (UN 1305), which are classified as Class 3, subsidiary risk 8, PG I.

Their flammability properties (flashpoint respectively 3 °C and 13 °C, and boiling point respectively 66 °C and 92 °C) put them in PG II.

There is further no evidence that these 2 chlorosilanes are more corrosive than all the other chlorosilanes of class 3 i.e. UN 1162, 1196, 1298 and 2985. Indeed all these substances release hydrogen chloride in contact with water and form hydrochloric acid through hydrolysis. Hydrochloric acid (UN 1789) itself is PG II or III.

In view of this and in accordance with the table of precedence of hazards (2.0.3.3) the 2 chlorosilanes (UN 1250 and UN 1305) should be classified as Class 3, subsidiary risk 8, PG II (see Annex 3 and Annex 4 for the completed Data Sheets).

2.2	Limited Quantities (Column 7)

Whereas all other entries in the list of Annex 1 have “NONE” as entry in column 7 of the Dangerous Goods List, Silicon tetrachloride (UN 1818) has an entry of “1 L”.

No reason can be found why this substance should be allowed for transport as limited quantity, in particular because of the less demanding requirements for the packagings.

Therefore the entry in column 7 for UN 1818 should be aligned to those of the other chlorosilanes and be amended into “NONE”

2.3 	Packing instructions for packagings except IBC’s (Column 8)

Chlorosilanes of classes 3, 6.1 and 8 have been assigned packing instruction P001. However this packing instruction shows a very broad variety of types of packagings. Many of these packagings are in the opinion of the chemical industry not recommended for the transport of chlorosilanes e.g. steel drums with removable head (1A2), aluminium drums with non-removable head (1B1) or with removable head (1B2), plastic drums with non-removable head (1H1) or with removable head (1H2)

It is therefore proposed to create a new specific packing instruction Pxxx, limiting the number of suitable types of packagings, and to put it in column 8 of the entries for chlorosilanes of classes 3, 6.1 and 8 in Annex 1.

It is further proposed to prohibit the use of plastics inner packagings and to reduce the maximum content of glass inner packagings from 10 l to 1 l.

The current assignment of packing instruction P401 to the other chlorosilanes i.e. the chlorosilanes belonging to division 4.3, is considered as being adequate.

2.4 	Packing instructions for IBC’s (Column 8)

Chlorosilanes of classes 3 and 8 have been assigned packing instruction IBC02 whereas chlorosilanes of division 6.1 have been assigned packing instruction IBC01. The chemical industry is concerned about the risk of accidents during the transport of chlorosilanes for a number of reasons: IBC’s have bottom discharge connections, they have no flange connections and are equipped with screw caps (plastic IBC’s) or lift-up lids with clamp screws (metal IBC’s). An overturn of an IBC (metal) may lead to an opening of the lift-up lid and the sudden release of 1,000 litres of chlorosilanes, which would constitute a major disaster

It is therefore proposed to remove current packing instructions IBC01 and IBC02 from column 8 for the entries of classes 3, 6.1 and 8 in Annex 1

The chlorosilanes of division 4.3 have not been assigned an IBC packing instruction and this should be maintained.

2.5 	Portable tank instructions (Column 10)

For most of the chlorosilanes bottom discharge openings are currently allowed (portable tank instruction T7 in column 10 of the dangerous goods list). As part of a voluntary initiative to enhance safety, the silicone manufacturers agreed to use only portable tanks without bottom discharge connections. Furthermore they recommend the general use of bursting disks preceding a pressure-relief valve (as described in 6.7.2.8.3).

In line with these recommendations, it is therefore proposed to replace portable tank instruction T7, where present in column 10 of Annex 1, by portable tank instruction T10. This concerns the entries for classes 3 and 8, with the exception of the n.o.s. entries of these classes.

This also means that, if the proposed change from PG I into PG II is adopted for UN 1250 and UN 1305, T10, instead of T11, should be assigned to both substances.

For the entries of division 4.3 and the n.o.s. entries for classes 3, 6.1 and 8, the silicone manufacturers propose the general assignment of portable tank instruction T14 rather than T10 or T11, as is already the case for UN 1295 and UN 2987.

2.6 	Portable tank special provisions (Column 11)

With respect to the proposal made under 2.5, it is proposed to assign portable tank special provision TP27 (allowing a test pressure of 4 bar instead of 6 bar if acceptable according to the test pressure definition in 6.7.2.1) to all chlorosilanes of classes 3, 6.1 and 8 with portable tank instruction T14 i.e. the respective n.o.s. entries.

As is already currently the case this portable tank special provision TP27 should not be assigned to entries for division 4.3 because of the higher risk of a possible release of a flammable gas.

There is currently no consistent assignment of portable tank special provision TP7 (air shall be eliminated from the vapour space by nitrogen or other means), which the silicone manufacturers consider to be essential for chlorosilanes. It is therefore proposed to enter TP7 in column 11 to all entries in Annex 1, if not already present.

At the same time it is proposed to allocate TP13 (need for self-contained breathing apparatus) consistently to all chlorosilanes.

3.	Proposal

- The following changes in the Dangerous Goods List in Chapter 3.2 are proposed:

3.1	Column 5 (Packing Group):

- replace PG I by PG II for UN 1250 and UN 1305

3.2 	Column 7 (Limited Quantities):

- replace “1 L” by “NONE” for UN 1818

3.3 	Column 8 (Packing instructions):

- replace 	P001 by Pxxx for UN 1162-1196-1250-1298-1305-1724-1728-1747-1753-1762-1763-1766-1767-1769-1771-1781-1784-1799-1800-1801-1804-1816-1818-2434-2435-2437-2985-2986-2987-3361-3362

3.4 	Column 8 (Packing instructions – IBC’s):

- remove 	IBC02 for UN 1162-1196-1298-1724-1728-1747-1753-1762-1763-1766-1767-1769-1771-1781-1784-1799-1800-1801-1804-1816-1818-2434-2435-2437-2985-2986-2987

- remove 	IBC01 from UN 3361-3362

3.5 	Column 10 (Portable tank instructions):

- replace 	T7 by T10 for UN 1162-1196-1298-1724-1728-1747-1753-1762-1763-1766-1767-1769-1771-1781-1784-1799-1800-1801-1804-1816-1818-2434-2435-2437

- replace 	T11 by T10 for UN 1250-1305

- replace 	T10 by T14 for UN 1183-1242-2988

- replace 	T11 by T14 for UN 2985-2986-3361-3362

3.6 	Column 11 (Portable tank special provisions)

- add 	TP27 to UN 3361-3362

- add 	TP7 to UN 1162-1196-1250-1298-1305-1724-1728-1747-1753-1762-1763-1766-1767-1769-1771-1781-1784-1799-1800-1801-1804-1816-2434-2435-2437-2985-2986-2987-3361-3362

- add 	TP13 to UN 1781-1804-1818-2986-2987

See Annex 2 where all changes have been highlighted.

Insert the following new packing instruction Pxxx in 4.1.4.1:

Note that if the proposal to reclassify UN 1250 and 1305 as PG II is adopted, the column with values for PG I could be deleted.

| PXXX | PACKING INSTRUCTION | PXXX |
| --- | --- | --- |
| The following packagings are authorized provided the general provisions of 4.1.1 and 4.1.3 are met: |
| Combination packagings | Maximum capacity / Net mass (see 4.1.3.3) |
| Inner packagings | Outer packagings | Packing group I | Packing group II |
| Glass 1 l Steel 40 l | Drums steel (1A2) plastics (1H2) plywood (1D) fibre (1G) | 250 kg 250 kg 150 kg 75 kg | 400 kg 400 kg 400 kg 400 kg |
|  | Boxes steel (4A) natural wood (4C1, 4 C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) expanded plastics (4H1) solid plastics (4H2) | 250 kg 150 kg 150 kg 75 kg 75 kg 60 kg 150 kg | 400 kg 400 kg 400 kg 400 kg 400 kg 60 kg 400 kg |
| Single packagings |
| Drums steel, non-removable head (1A1) | 250 l | 450 l |
| Jerricans steel, non-removable head (3A1) | 60 l | 60 l |
| Composite packagings plastics receptacle in steel drum (6HA1) | 250 l | 250 l |

- Justification

The chemical industry is of the opinion that these changes will increase the level of safety for the transport of chlorosilanes for the reasons given above.

*  *  *

Annex 1 ( in ENGLISH ONLY)

List of chlorosilanes (current provisions of UN Model Regulations 14th revised edition)

| UN No. | Name and descripton | Class or division | Subsi-diary risk | UN packing group | Special provisions | Limited quantities | Packagings and IBCs | Portable tanks and bulk containers |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | Packing instruction | Special packing provisions | Instruc-tions | Special provisions |
| (1) | (2) | (3) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) |
| 1162 | DIMETHYLDICHLOROSILANE | 3 | 8 | II |  | NONE | P001 IBC02 |  | T7 | TP2 TP13 |
| 1183 | ETHYLDICHLOROSILANE | 4.3 | 3 8 | I |  | NONE | P401 |  | T10 | TP2 TP7 TP13 |
| 1196 | ETHYLTRICHLOROSILANE | 3 | 8 | II |  | NONE | P001 IBC02 |  | T7 | TP2 TP13 |
| 1242 | METHYLDICHLOROSILANE | 4.3 | 3 8 | I |  | NONE | P401 |  | T10 | TP2 TP7 TP13 |
| 1250 | METHYLTRICHLOROSILANE | 3 | 8 | I |  | NONE | P001 |  | T11 | TP2 TP13 |
| 1295 | TRICHLOROSILANE | 4.3 | 3 8 | I |  | NONE | P401 |  | T14 | TP2 TP7 TP13 |
| 1298 | TRIMETHYLCHLOROSILANE | 3 | 8 | II |  | NONE | P001 IBC02 |  | T7 | TP2 TP13 |
| 1305 | VINYLTRICHLOROSILANE | 3 | 8 | I |  | NONE | P001 |  | T11 | TP2 TP13 |
| 1724 | ALLYLTRICHLOROSILANE, STABILIZED | 8 | 3 | II |  | NONE | P001 IBC02 |  | T7 | TP2 TP13 |
| 1728 | AMYLTRICHLOROSILANE | 8 |  | II |  | NONE | P001 IBC02 |  | T7 | TP2 TP13 |
| 1747 | BUTYLTRICHLOROSILANE | 8 | 3 | II |  | NONE | P001 IBC02 |  | T7 | TP2 TP13 |
| 1753 | CHLOROPHENYLTRICHLORO-SILANE | 8 |  | II |  | NONE | P001 IBC02 |  | T7 | TP2 |
| 1762 | CYCLOHEXENYL-TRICHLOROSILANE | 8 |  | II |  | NONE | P001 IBC02 |  | T7 | TP2 TP13 |
| 1763 | CYCLOHEXYL-TRICHLOROSILANE | 8 |  | II |  | NONE | P001 IBC02 |  | T7 | TP2 TP13 |
| 1766 | DICHLOROPHENYL-TRICHLOROSILANE | 8 |  | II |  | NONE | P001 IBC02 |  | T7 | TP2 TP13 |
| 1767 | DIETHYLDICHLOROSILANE | 8 | 3 | II |  | NONE | P001 IBC02 |  | T7 | TP2 TP13 |
| 1769 | DIPHENYLDICHLOROSILANE | 8 |  | II |  | NONE | P001 IBC02 |  | T7 | TP2 TP13 |
| 1771 | DODECYLTRICHLOROSILANE | 8 |  | II |  | NONE | P001 IBC02 |  | T7 | TP2 TP13 |
| 1781 | HEXADECYL-TRICHLOROSILANE | 8 |  | II |  | NONE | P001 IBC02 |  | T7 | TP2 |
| 1784 | HEXYLTRICHLOROSILANE | 8 |  | II |  | NONE | P001 IBC02 |  | T7 | TP2 TP13 |
| 1799 | NONYLTRICHLOROSILANE | 8 |  | II |  | NONE | P001 IBC02 |  | T7 | TP2 TP13 |
| 1800 | OCTADECYLTRICHLORO-SILANE | 8 |  | II |  | NONE | P001 IBC02 |  | T7 | TP2 TP13 |
| 1801 | OCTYLTRICHLOROSILANE | 8 |  | II |  | NONE | P001 IBC02 |  | T7 | TP2 TP13 |
| 1804 | PHENYLTRICHLOROSILANE | 8 |  | II |  | NONE | P001 IBC02 |  | T7 | TP2 |
| 1816 | PROPYLTRICHLOROSILANE | 8 | 3 | II |  | NONE | P001 IBC02 |  | T7 | TP2 TP13 |
| 1818 | SILICON TETRACHLORIDE | 8 |  | II |  | 1 L | P001 IBC02 |  | T7 | TP2 TP7 |
| 2434 | DIBENZYLDICHLOROSILANE | 8 |  | II |  | NONE | P001 IBC02 |  | T7 | TP2 TP13 |
| 2435 | ETHYLPHENYLDICHLORO-SILANE | 8 |  | II |  | NONE | P001 IBC02 |  | T7 | TP2 TP13 |
| 2437 | METHYLPHENYL- DICHLOROSILANE | 8 |  | II |  | NONE | P001 IBC02 |  | T7 | TP2 TP13 |
| 2985 | CHLOROSILANES, FLAMMABLE, CORROSIVE, N.O.S. | 3 | 8 | II |  | NONE | P001 IBC02 |  | T11 | TP2 TP13 TP27 |
| 2986 | CHLOROSILANES, CORROSIVE, FLAMMABLE, N.O.S. | 8 | 3 | II |  | NONE | P001 IBC02 |  | T11 | TP2 TP27 |
| 2987 | CHLOROSILANES, CORROSIVE, N.O.S. | 8 |  | II |  | NONE | P001 IBC02 |  | T14 | TP2 TP27 |
| 2988 | CHLOROSILANES, WATER-REACTIVE, FLAMMABLE, CORROSIVE, N.O.S. | 4.3 | 3 8 | I |  | NONE | P401 |  | T10 | TP2 TP7 TP9 TP13 |
| 3361 | CHLOROSILANES, TOXIC, CORROSIVE, N.O.S. | 6.1 | 8 | II |  | NONE | P001 IBC01 |  | T11 | TP2 TP13 |
| 3362 | CHLOROSILANES, TOXIC, CORROSIVE, FLAMMABLE, N.O.S. | 6.1 | 3 8 | II |  | NONE | P001 IBC01 |  | T11 | TP2 TP13 |

Annex 2 ( in ENGLISH ONLY)

List of chlorosilanes: proposed amendments either struck through or indicated in bold and underlined

| UN No. | Name and descripton | Class or division | Subsi-diary risk | UN packing group | Special provisions | Limited quantities | Packagings and IBCs | Portable tanks and bulk containers |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | Packing instruction | Special packing provisions | Instruc-tions | Special provisions |
| (1) | (2) | (3) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) |
| 1162 | DIMETHYLDICHLOROSILANE | 3 | 8 | II |  | NONE | P001 IBC02 Pxxx |  | T7 T10 | TP2 TP7 TP13 |
| 1183 | ETHYLDICHLOROSILANE | 4.3 | 3 8 | I |  | NONE | P401 |  | T10 T14 | TP2 TP7 TP13 |
| 1196 | ETHYLTRICHLOROSILANE | 3 | 8 | II |  | NONE | P001 IBC02 Pxxx |  | T7 T10 | TP2 TP7 TP13 |
| 1242 | METHYLDICHLOROSILANE | 4.3 | 3 8 | I |  | NONE | P401 |  | T10 T14 | TP2 TP7 TP13 |
| 1250 | METHYLTRICHLOROSILANE | 3 | 8 | I II |  | NONE | P001 Pxxx |  | T11 T10 | TP2 TP7 TP13 |
| 1295 | TRICHLOROSILANE | 4.3 | 3 8 | I |  | NONE | P401 |  | T14 | TP2 TP7 TP13 |
| 1298 | TRIMETHYLCHLOROSILANE | 3 | 8 | II |  | NONE | P001 IBC02 Pxxx |  | T7 T10 | TP2 TP7 TP13 |
| 1305 | VINYLTRICHLOROSILANE | 3 | 8 | I II |  | NONE | P001 Pxxx |  | T11 T10 | TP2 TP7 TP13 |
| 1724 | ALLYLTRICHLOROSILANE, STABILIZED | 8 | 3 | II |  | NONE | P001 IBC02 Pxxx |  | T7 T10 | TP2 TP7 TP13 |
| 1728 | AMYLTRICHLOROSILANE | 8 |  | II |  | NONE | P001 IBC02 Pxxx |  | T7 T10 | TP2 TP7 TP13 |
| 1747 | BUTYLTRICHLOROSILANE | 8 | 3 | II |  | NONE | P001 IBC02 Pxxx |  | T7 T10 | TP2 TP7 TP13 |
| 1753 | CHLOROPHENYLTRICHLORO-SILANE | 8 |  | II |  | NONE | P001 IBC02 Pxxx |  | T7 T10 | TP2 TP7 |
| 1762 | CYCLOHEXENYL-TRICHLOROSILANE | 8 |  | II |  | NONE | P001 IBC02 Pxxx |  | T7 T10 | TP2 TP7 TP13 |
| 1763 | CYCLOHEXYL-TRICHLOROSILANE | 8 |  | II |  | NONE | P001 IBC02 Pxxx |  | T7 T10 | TP2 TP7 TP13 |
| 1766 | DICHLOROPHENYL-TRICHLOROSILANE | 8 |  | II |  | NONE | P001 IBC02 Pxxx |  | T7 T10 | TP2 TP7 TP13 |
| 1767 | DIETHYLDICHLOROSILANE | 8 | 3 | II |  | NONE | P001 IBC02 Pxxx |  | T7 T10 | TP2 TP7 TP13 |
| 1769 | DIPHENYLDICHLOROSILANE | 8 |  | II |  | NONE | P001 IBC02 Pxxx |  | T7 T10 | TP2 TP7 TP13 |
| 1771 | DODECYLTRICHLOROSILANE | 8 |  | II |  | NONE | P001 IBC02 Pxxx |  | T7 T10 | TP2 TP7 TP13 |
| 1781 | HEXADECYL-TRICHLOROSILANE | 8 |  | II |  | NONE | P001 IBC02 Pxxx |  | T7 T10 | TP2 TP7 TP13 |
| 1784 | HEXYLTRICHLOROSILANE | 8 |  | II |  | NONE | P001 IBC02 Pxxx |  | T7 T10 | TP2 TP7 TP13 |
| 1799 | NONYLTRICHLOROSILANE | 8 |  | II |  | NONE | P001 IBC02 Pxxx |  | T7 T10 | TP2 TP7 TP13 |
| 1800 | OCTADECYLTRICHLORO-SILANE | 8 |  | II |  | NONE | P001 IBC02 Pxxx |  | T7 T10 | TP2 TP7 TP13 |
| 1801 | OCTYLTRICHLOROSILANE | 8 |  | II |  | NONE | P001 IBC02 Pxxx |  | T7 T10 | TP2 TP7 TP13 |
| 1804 | PHENYLTRICHLOROSILANE | 8 |  | II |  | NONE | P001 IBC02 Pxxx |  | T7 T10 | TP2 TP7 TP13 |
| 1816 | PROPYLTRICHLOROSILANE | 8 | 3 | II |  | NONE | P001 IBC02 Pxxx |  | T7 T10 | TP2 TP7 TP13 |
| 1818 | SILICON TETRACHLORIDE | 8 |  | II |  | 1 L NONE | P001 IBC02 Pxxx |  | T7 T10 | TP2 TP7 TP13 |
| 2434 | DIBENZYLDICHLOROSILANE | 8 |  | II |  | NONE | P001 IBC02 Pxxx |  | T7 T10 | TP2 TP7 TP13 |
| 2435 | ETHYLPHENYLDICHLORO-SILANE | 8 |  | II |  | NONE | P001 IBC02 Pxxx |  | T7 T10 | TP2 TP7 TP13 |
| 2437 | METHYLPHENYL- DICHLOROSILANE | 8 |  | II |  | NONE | P001 IBC02 Pxxx |  | T7 T10 | TP2 TP7 TP13 |
| 2985 | CHLOROSILANES, FLAMMABLE, CORROSIVE, N.O.S. | 3 | 8 | II |  | NONE | P001 IBC02 Pxxx |  | T11 T14 | TP2 TP7 TP13 TP27 |
| 2986 | CHLOROSILANES, CORROSIVE, FLAMMABLE, N.O.S. | 8 | 3 | II |  | NONE | P001 IBC02 Pxxx |  | T11 T14 | TP2 TP7 TP13 TP27 |
| 2987 | CHLOROSILANES, CORROSIVE, N.O.S. | 8 |  | II |  | NONE | P001 IBC02 Pxxx |  | T14 | TP2 TP7 TP13 TP27 |
| 2988 | CHLOROSILANES, WATER-REACTIVE, FLAMMABLE, CORROSIVE, N.O.S. | 4.3 | 3 8 | I |  | NONE | P401 |  | T10 T14 | TP2 TP7 TP9 TP13 |
| 3361 | CHLOROSILANES, TOXIC, CORROSIVE, N.O.S. | 6.1 | 8 | II |  | NONE | P001 IBC01 Pxxx |  | T11 T14 | TP2 TP7 TP13 TP27 |
| 3362 | CHLOROSILANES, TOXIC, CORROSIVE, FLAMMABLE, N.O.S. | 6.1 | 3 8 | II |  | NONE | P001 IBC01 Pxxx |  | T11 T14 | TP2 TP7 TP13 TP27 |

### Annex 3 ( in ENGLISH ONLY)

### Data Sheet for Methyltrichlorosilane

DATA SHEET TO BE SUBMITTED TO THE UNITED NATIONS

FOR NEW OR AMENDED CLASSIFICATION OF SUBSTANCES

Submitted by	CES	Date 	 January 2006

Supply all relevant information including sources of basic classification data. Data should relate to the product in the form to be transported. State test methods. Answer all questions - if necessary state "not known" or "not applicable" - If data is not available in the form requested, provide what is available with details. Delete inappropriate words.

Section 1. SUBSTANCE IDENTITY

1.1	Chemical name:	 Methyltrichlorosilane

1.2	Chemical formula :	 CH3SiCl3

1.3	Other names/synonyms : Trichloro(methyl)silane

1.4.1	UN number 	.....1250	1.4.2	CAS number 	75-79-6

1.5	Proposed classification for the Recommendations

1.5.1	proper shipping name (3.1.2)	Methyltrichlorosilane

1.5.2	class/division   ...3	subsidiary risk(s)   ....8

packing group 	 ....II (according to proposal)

1.5.3	proposed special provisions, if any

1.5.4	proposed packing instruction(s) .....Pxxx (according to proposal)

Section 2. PHYSICAL PROPERTIES

2.1	Melting point or range –77 °C

2.2	Boiling point or range	   66 °C (101.3kPa)

2.3	Relative density at :

2.3.1	15 °C	 1.283 g/cm3

2.3.2	20 °C	 1.275 g/cm3

2.3.3	50 °C	 1.223 g/cm3

2.4	Vapour pressure at :

2.4.1	50 °C	 59.02 kPa

2.4.2	65 °C	 96.56 kPa

2.5     Viscosity at 20 °C 	0.4 x 10-6 m2/s

2.6	Solubility in water at 20 °C	reacts violently with water	g/100 ml

2.7	Physical state at 20°C (2.2.1.11)		solid/liquid/gas2

2.8	Appearance at normal transport temperatures, including colour and odour

colourless liquid, pungent odour

2.9	Other relevant physical properties  	.....highly flammable; release of hydrogen chloride gas in contact with humidity, formation of  hydrochloric acid vapours; reacts violently with water, alcohols, protic solvents

Section 3. FLAMMABILITY

3.1	Flammable vapour

3.1.1	Flash point (2.3.31) ....  3 °C oc/cc

3.1.2	Is combustion sustained? (2.3.1.31)		yes/no

3.2	Auto-ignition temperature .... 460 °C

3.3	Flammability range (LEL/UEL)	 ....4.5 – 43.0 % (Vol.)

3.4	Is the substance a flammable solid? (2.4.21)		yes/no

3.4.1	If yes, give details

Section 4. CHEMICAL PROPERTIES

4.1	Does the substance require inhibition/stabilization or other treatment such as nitrogen blanket to prevent hazardous reactivity ?			yes/no

If yes, state:

4.1.1	Inhibitor/stabilizer used  ............nitrogen blanket to exclude humidity

4.1.2	Alternative method

4.1.3	Time effective at 55 °C

4.1.4	Conditions rendering it ineffective

4.2	Is the substance an explosive according to paragraph 2.1.1.1? (2.11)	yes/no

4.2.1	If yes, give details

4.3	Is the substance a desensitized explosive? (2.4.2.41) 		yes/no

4.3.1	If yes, give details

4.4	Is the substance a self-reactive substance? (2.4.11) 		yes/no

If yes, state:

4.4.1	exit box of flow chart

What is the self-accelerating decomposition temperature (SADT) for a 50 kg package?	°C

Is the temperature control required? (2.4.2.3.41)	yes/no

4.4.2	proposed control temperature for a 50 kg package	°C

4.4.3	proposed emergency temperature for a 50 kg package	°C

4.5	Is the substance pyrophoric? (2.4.31) 		yes/no

4.5.1	If yes, give details

4.6	Is the substance liable to self-heating? (2.4.31) 	yes/no

4.6.1	If yes, give details

4.7	Is the substance an organic peroxide (2.5.11) 		yes/no

If yes state:

4.7.1	exit box of flow chart

What is the self accelerating decomposition temperature (SADT) for a 50 kg package?	°C

Is temperature control required? (2.5.3.4.11) 		yes/no

4.7.2	proposed control temperature for a 50 kg package	°C

4.7.3	proposed emergency temperature for a 50 kg package	°C

4.8	Does the substance in contact with water emit flammable gases? (2.4.41) 		yes/no

4.8.1	If yes, give details

4.9	Does the substance have oxidizing properties (2.5.11)		yes/no

4.9.1	If yes, give details

4.10	Corrosivity (2.81) to:

4.10.1	mild steel  0.0075 mm/year 		 at  50 °C

4.10.2	aluminium	mm/year  	at	°C

4.10.3	other packaging materials (specify)

mm/year   at	°C

mm/year   at	°C

4.11	Other relevant chemical properties

Section 5. HARMFUL BIOLOGICAL EFFECTS

5.1	LD50, oral (2.6.2.1.11) ....300 – 1000 	mg/kg	Animal species  ...................rat

5.2	LD50, dermal (2.6.2.1.21) .not known   mg/kg	Animal species

5.3	LC50, inhalation (2.6.2.1.31) ....8.48	mg/litre	Exposure time .....................1	 hours

or		ml/m3	Animal species ...................rat........

5.4	Saturated vapour concentration at 20 °C (2.6.2.2.4.31)	   .(18 kPa).....................177690	ml/m3

5.5	Skin exposure (2.81) results	Exposure time 	 hours/minutes

Animal species

5.6	Other data

5.7	Human experience 	.......corrosive to skin, causes severe burns to the skin and to the eyes

Section 6. SUPPLEMENTARY INFORMATION

6.1	Recommended emergency action

6.1.1	Fire (include suitable and unsuitable extinguishing agents)

medium expansion foam, no water, no halones

6.1.2	Spillage	.......soak up with inert absorbent material (e.g. dry sand)

6.2	Is it proposed to transport the substance in:

6.2.1	Bulk Containers (6.81)			yes/no

6.2.2	Intermediate Bulk Containers (6.51)?		yes/no

6.2.3	Portable tanks (6.71)?			yes/no

If yes, give details in Sections 7, 8 and/or 9.

Section 7. BULK CONTAINERS (only complete if yes in 6.2.1)

7.1	Proposed type(s)

Section 8. INTERMEDIATE BULK CONTAINERS (IBCs) (only complete if yes in 6.2.2)

8.1	Proposed type(s)

Section 9. MULTIMODAL TANK TRANSPORT (only complete if yes in 6.2.3)

9.1	Description of proposed tank (including IMO tank type if known) .....T10; IMO1

9.2	Minimum test pressure  ....4 bars

9.3	Minimum shell thickness  ....6 mm (mild steel)

9.4	Details of bottom openings, if any  .....not allowed

9.5	Pressure relief arrangements  .......pressure-relief valve preceded by a frangible disc

9.6	Degree of filling 	 .......TP2;  95/(1+( (tr – tf))

9.7	Unsuitable construction materials	 ........aluminium, non-ferrous metals

### Annex 4 ( in ENGLISH ONLY)

### Data Sheet for Vinyltrichlorosilane

##### DATA SHEET TO BE SUBMITTED TO THE UNITED NATIONS

FOR NEW OR AMENDED CLASSIFICATION OF SUBSTANCES

Submitted by	CES	Date 	 January 2006

Supply all relevant information including sources of basic classification data. Data should relate to the product in the form to be transported. State test methods. Answer all questions - if necessary state "not known" or "not applicable" - If data is not available in the form requested, provide what is available with details. Delete inappropriate words.

Section 1. SUBSTANCE IDENTITY

1.1	Chemical name			Vinyltrichlorosilane

1.2	Chemical formula 		CH2=CH-SiCl3

1.3	Other names/synonyms	Ethenyltrichlorosilane

1.4.1	UN number 	 .....1305	1.4.2	CAS number 	75-94-5

1.5	Proposed classification for the Recommendations

1.5.1	proper shipping name (3.1.2) .......Vinyltrichlorosilane

1.5.2	class/division  ......3	subsidiary risk(s)  ...8

packing group 	 ...II  (according to proposal)

1.5.3	proposed special provisions, if any

1.5.4	proposed packing instruction(s) ........Pxxx (according to proposal)

Section 2. PHYSICAL PROPERTIES

2.1	Melting point or range  < - 78 °C

2.2	Boiling point or range	       92  °C (101.3 kPa)

2.3	Relative density at :

2.3.1	15 °C

2.3.2	20 °C	    1.27 g/cm3

2.3.3	50 °C

2.4	Vapour pressure at :

2.4.1	50 °C	 ....23.5	 kPa

2.4.2	65 °C		 kPa

2.5	Viscosity at 20 °C 	 0.5 x 10-6	 m2/s

2.6	Solubility in water at 20 °C	reacts violently with water 	g/100 ml

2.7	Physical state at 20°C (2.2.1.11)		solid/liquid/gas2

2.8	Appearance at normal transport temperatures, including colour and odour

colourless liquid, pungent odour

2.9	Other relevant physical properties  	........highly flammable; release of hydrogen chloride gas in contact with humidity, formation of  hydrochloric acid vapours; reacts violently with water, alcohols, protic solvents

Section 3. FLAMMABILITY

3.1	Flammable vapour

3.1.1	Flash point (2.3.31)  13°C oc/cc

3.1.2	Is combustion sustained? (2.3.1.31)		yes/no

3.2	Autoignition temperature ..270	°C

3.3	Flammability range (LEL/UEL)	..3.17 – 49.2  % (Vol.)

3.4	Is the substance a flammable solid? (2.4.21)		yes/no

3.4.1	If yes, give details

Section 4. CHEMICAL PROPERTIES

4.1	Does the substance require inhibition/stabilization or other treatment such as nitrogen blanket to prevent hazardous reactivity ?			yes/no

If yes, state:

4.1.1	Inhibitor/stabilizer used 	nitrogen blanket to exclude humidity

4.1.2	Alternative method

4.1.3	Time effective at 55 °C

4.1.4	Conditions rendering it ineffective

4.2	Is the substance an explosive according to paragraph 2.1.1.1? (2.1)	yes/no

4.2.1	If yes, give details

4.3	Is the substance a desensitized explosive? (2.4.2.41) 		yes/no

4.3.1	If yes, give details

4.4	Is the substance a self-reactive substance? (2.4.11) 		yes/no

If yes, state:

4.4.1	exit box of flow chart

What is the self-accelerating decomposition temperature (SADT) for a 50 kg package?	°C

Is the temperature control required? (2.4.2.3.41)	yes/no

4.4.2	proposed control temperature for a 50 kg package	°C

4.4.3	proposed emergency temperature for a 50 kg package	°C

4.5	Is the substance pyrophoric? (2.4.31) 		yes/no

4.5.1	If yes, give details

4.6	Is the substance liable to self-heating? (2.4.31) 	yes/no

4.6.1	If yes, give details

4.7	Is the substance an organic peroxide (2.5.11) 		yes/no

If yes state:

4.7.1	exit box of flow chart

What is the self accelerating decomposition temperature (SADT) for a 50 kg package?	°C

Is temperature control required? (2.5.3.4.11) 		yes/no

4.7.2	proposed control temperature for a 50 kg package	°C

4.7.3	proposed emergency temperature for a 50 kg package	°C

4.8	Does the substance in contact with water emit flammable gases? (2.4.41) 		yes/no

4.8.1	If yes, give details

4.9	Does the substance have oxidizing properties (2.5.11)		yes/no

4.9.1	If yes, give details

4.10	Corrosivity (2.81) to:

4.10.1	mild steel .0.0075	mm/year 		 at .................50	°C

4.10.2	aluminium	mm/year  	at	°C

4.10.3	other packaging materials (specify)

mm/year   at	°C

mm/year   at	°C

4.11	Other relevant chemical properties

Section 5. HARMFUL BIOLOGICAL EFFECTS

5.1	LD50, oral (2.6.2.1.11)	 1280…mg/kg	Animal species                rat

5.2	LD50, dermal (2.6.2.1.21).. 857…mg/kg	Animal species                rabbit

5.3	LC50, inhalation (2.6.2.1.31)	 10.8	mg/litre	Exposure time..................1	 hours

or		ml/m3	Animal species ...............rat

5.4	Saturated vapour concentration at 20 °C (2.6.2.2.4.31)	..(6.2 kPa)...................61204	ml/m3

5.5	Skin exposure (2.81) results	Exposure time 	 hours/minutes

Animal species

5.6	Other data

5.7	Human experience 	.......corrosive to skin, causes severe burns to the skin and to the eyes

Section 6. SUPPLEMENTARY INFORMATION

6.1	Recommended emergency action

6.1.1	Fire (include suitable and unsuitable extinguishing agents)

................medium expansion foam; no water; no halones

6.1.2	Spillage	........ soak up with inert absorbent material (e.g. dry sand)

6.2	Is it proposed to transport the substance in:

6.2.1	Bulk Containers (6.8)			yes/no

6.2.2	Intermediate Bulk Containers (6.51)?		yes/no

6.2.3	Portable tanks (6.71)?			yes/no

If yes, give details in Sections 7, 8 and/or 9.

Section 7. BULK CONTAINERS (only complete if yes in 6.2.1)

7.1	Proposed type(s)

Section 8. INTERMEDIATE BULK CONTAINERS (IBCs) (only complete if yes in 6.2.2)

8.1	Proposed type(s)

Section 9. MULTIMODAL TANK TRANSPORT (only complete if yes in 6.2.3)

9.1	Description of proposed tank (including IMO tank type if known).......T10; IMO1

9.2	Minimum test pressure ..........4 bars

9.3	Minimum shell thickness .......6 mm (mild steel)

9.4	Details of bottom openings, if any :...not allowed

9.5	Pressure relief arrangements         ......pressure-relief valve preceded by a frangible disc

9.6	Degree of filling 	.........TP2;  95/(1+( (tr – tf))

9.7	Unsuitable construction materials	...........aluminium; non-ferrous metals

# Footnotes

This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

See definition of "liquid" in 1.2.1 of the Model Regulations on the Transport of Dangerous Goods.

1 	This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

1	This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

1 	This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

1	This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

1	This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

2 	See definition of "liquid" in 1.2.1 of the Model Regulations on the Transport of Dangerous Goods.

1	This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

1	This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

1	This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

# Text boxes

STSTE

Secretariat