#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2006/12

28 March 2006

Original: ENGLISH

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Twenty-ninth session

# Geneva, 3-12 (a.m.) July 2006

# Item 6 of the provisional agenda

LISTING, CLASSIFICATION AND PACKING

Organic peroxides

New formulations to be listed in 2.5.3.2.4, IBC 520 and T23

Transmitted by the International Council of Chemical Associations (ICCA)

1.	Introduction

Since several new peroxides and formulations have become commercially available, there is a need to update 2.5.3.2.4, IBC 520 and T23. A list of new products, proposed classification, the accompanying competent authority approvals and a summary of the supporting test data are given in the annex to this proposal.

2.	Proposals

ICCA proposes to include a number of new or amended entries in 2.5.3.2.4, list of currently assigned organic peroxides, as indicated in 2.1. Further, ICCA proposes to include a number of new entries or change one entry in packaging IBC520, as indicated in 2.2. In addition for one organic peroxide formulation an additional type of diluent is proposed for inclusion in portable tank instruction T23.

2.1	Proposed amendments to 2.5.3.2.4 List of currently assigned organic peroxides:

| ORGANIC PEROXIDE | Concen-tration (%) | Diluent type A (%) | Diluent type B 1) (%) | Inert solid (%) | Water | Packing Method | Control temperature (°C) | Emergency temperature (°C) | Number (Generic entry) | Subsidiary risks and remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ADD: |  |  |  |  |  |  |  |  |  |  |
| tert-AMYL PEROXYNEODECANOATE | ≤47 | ≥ 53 |  |  |  | OP8 | 0 | +10 | 3119 |  |
| tert-BUTYL PEROXY 3,5,5-TRIMETHYLHEXANOATE | ≤42 |  |  | ≥48 |  | OP7 |  |  | 3106 |  |
| CUMYL PEROXYNEODECANOATE | ≤ 87 | ≥ 13 |  |  |  | OP7 | -10 | 0 | 3115 |  |
| 2,2-DI-(tert-AMYLPEROXY)BUTANE | ≤ 57 | ≥ 43 |  |  |  | OP7 |  |  | 3105 |  |
| 1,1-DI-(tert-BUTYLPEROXY)CYCLOHEXANE | ≤ 72 |  | ≥ 28 |  |  | OP5 |  |  | 3103 | 30) |
| 1,1-DI-(tert-BUTYLPEROXY) CYCLOHEXANE + tert-BUTYLPEROXY-2-ETHYLHEXANOATE | ≤43+≤16 | ≥ 41 |  |  |  | OP 7 |  |  | 3105 |  |
| 1,1-DI-(tert-BUTYLPEROXY)-3,3,5-TRIMETHYLCYCLOHEXANE | ≤ 90 |  | ≥ 10 |  |  | OP5 |  |  | 3103 | 30) |
| DI-2,4-DICHLOROBENZOYL PEROXIDE | ≤ 52 as a paste |  |  |  |  | OP8 | +20 | +25 | 3118 |  |
| 3-HYDROXY-1,1-DIMETHYLBUTYL PEROXYNEODECANOATE | ≤77 | ≥ 23 |  |  |  | OP 7 | -5 | +5 | 3115 |  |
| 3-HYDROXY-1,1-DIMETHYL BUTYLPEROXYNEODECANOATE | ≤52 as a stable dispersion in water |  |  |  |  | OP 8 | -5 | +5 | 3119 |  |
| 3-HYDROXY-1,1-DIMETHYLBUTYL PEROXYNEODECANOATE | ≤52 | ≥ 48 |  |  |  | OP 8 | -5 | +5 | 3117 |  |
| METHYL ISOPROPYL KETONE PEROXIDE(S) | See remark 31) | ≥ 70 |  |  |  | OP8 |  |  | 3109 | 31) |
| 3,3,5,7,7-PENTAMETHYL-1,2,4-TRIOXEPANE | ≤100 |  |  |  |  | OP8 |  |  | 3107 |  |
| CHANGE: |  |  |  |  |  |  |  |  |  |  |
| DI-(2-ETHYLHEXYL) PEROXYDICARBONATE | ≤ 62 as a stable dispersion in water |  |  |  |  | OP8 | -15 | -5 | change 3117 to 3119 |  |
| tert-AMYLPEROXY-3,5,5-TRIMETHYLHEXANOATE | ≤100 |  |  |  |  | Change OP5 to OP7 |  |  | Change 3101 to 3105 |  |
| DICUMYL PEROXIDE | >52-100 |  |  | Delete≤ 57 |  | OP8 |  |  | 3110 | 12) |
| DELETE: |  |  |  |  |  |  |  |  |  |  |
| DI-(2-ETHYLHEXYL) PEROXYDICARBONATE | ≤ 52 as a stable dispersion in water |  |  |  |  | OP8 | -15 | -5 | 3119 |  |
| Add new notes: Note 30) Diluent type B with a boiling point >130°C Note 31) Active oxygen ≤ 6.7 % |  |  |  |  |  |  |  |  |  |  |

2.2	Proposed amendments to packing instruction IBC520:

| UN No. | Organic peroxide | Type of IBC | Maximum quantity (litres) | Control temperature | Emergency Temperature |
| --- | --- | --- | --- | --- | --- |
| 3109 | ORGANIC PEROXIDE TYPE F, LIQUID |  |  |  |  |
|  | ADD: |  |  |  |  |
|  | tert-Butyl peroxybenzoate, not more than 32% in diluent type A | 31A | 1250 |  |  |
|  | 1,1-Di-(tert-Butylperoxy)cyclohexane, not more than 47% in diluent type A, | 31A | 1250 |  |  |
|  | CHANGE: |  |  |  |  |
|  | Change: tert-Butyl peroxy-3,5,5-trimethylhexanoate, not more than 32% in diluent type A To: tert-Butyl peroxy-3,5,5-trimethylhexanoate, not more than 37% in diluent type A | 31A 31HA1 | 1250 1000 |  |  |
| 3119 | ORGANIC PEROXIDE TYPE F, LIQUID, TEMPERATURE CONTROLLED |  |  |  |  |
|  | ADD: |  |  |  |  |
|  | tert-Amyl peroxypivalate, not more than 32% in diluent type A | 31A | 1250 | +10 | +15 |
|  | tert-Butyl peroxyneodecanoate, not more than 52%, stable dispersion, in water | 31A | 1250 | -5 | +5 |
|  | Di-(2-neodecanoylperoxyisopropyl)-benzene, not more than 42%, stable dispersion, in water | 31A | 1250 | -15 | -5 |
|  | 3-Hydroxy-1,1-dimethylbutylperoxyneodecanoate, not more than 52%, stable dispersion, in water | 31A | 1250 | -15 | -5 |
|  | CHANGE: |  |  |  |  |
|  | Di-(2-ethylhexyl) peroxydicarbonate, not more than 52%, stable dispersion in water | 31A | 1250 | -20 | -10 |
|  | INTO: |  |  |  |  |
|  | Di-(2-ethylhexyl) peroxydicarbonate, not more than 62%, stable dispersion in water | 31A | 1250 | -20 | -10 |

2.3	Proposed amendments to portable tank instruction T23:

| UN No. | Substance | Min. test pressure (bar) | Min. shell thickness (mm-reference steel) | Bottom openings requirem-ents | Pressure-relief require-ments | Degree of filling | Control temp. | Emer-gency temp. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 3119 | ORGANIC PEROXIDE TYPE F, LIQUID, TEMPERATURE CONTROLLED | 4 | See 6.7.2.4.2 | See 6.7.2.6.3 | See 6.7.2.8.2 4.2.1.13.6 4.2.1.13.7 4.2.1.13.8 | See 4.2.1.13.13 | c | c |
|  | ADD: |  |  |  |  |  |  |  |
|  | Tert-Amyl peroxyneodecanoate, not more than 47% in diluent type A |  |  |  |  |  | -10 | -5 |
|  | CHANGE: |  |  |  |  |  |  |  |
|  | Di-(3,5,5-trimethyl-hexanoyl)peroxide, not more than 38% in diluent type B |  |  |  |  |  | 0 °C | +5°C |
|  | IN: |  |  |  |  |  |  |  |
|  | Di-(3,5,5-trimethyl-hexanoyl)peroxide, not more than 38% in diluent type A or type B |  |  |  |  |  | 0 °C | +5°C |

##### Annex (IN ENGLISH ONLY)

##### TEST RESULTS OF NEW ORGANIC PEROXIDES AND FORMULATIONS TO BE ADDED TO 2.5.3.2.4 or IBC520 or T23

|  |  |  |  |  | Test results |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| no | Product | packaging | UN | Koenen/ E.1 | DPVT/ E.2 | P/T / C.1 | Deflagration / C.2 | SADT (1000ml) | Trauzl/ F.3 | Detonation/ A.1 cav. | approval number |
| 1 | tert-Amylperoxypivalate, 32% - diluent type A | IBC/31A/ 1250l | 3119 | <1,0mm ("0") | 1,2mm(10g) | <2170kPa | < 0,35 mm/s | 25 °C | 7,0 ml/10g (no) | No propagation | BAM/ Tgb.-Nr.II.2-792/98 |
| 2 | tert-Butylperoxybenzoate, 32% -diluent type A | IBC/31A/ 1250l | 3109 | <1,0mm ("0") | 1,0mm (50g) | <2170kPa | < 0,35 mm/s | > 60 °C | 5,5 ml/10g (no) | No propagation | BAM/ Tgb.-Nr.II.2-1182/01 |
| 3 | tert-Butylperoxy-3,5,5-trimethylhexanoate, 37% - diluent type A | IBC/31A/ 1250l | 3109 | <1,0mm ("0") | 1,0mm (50g) | yes, slowly | <0,35 mm/s | > 60 °C | 6,0 ml/10g (no) | No propagation | BAM/ Tgb.-Nr.II.2-1506/01 |
| 4 | tert-Butylperoxyneodecanoate, 52% as a stable dispersion in water | IBC/31A/ 1250l | 3119 | <1,0mm ("0") | 1,0mm (50g) | <2170kPa | < 0,35 mm/s | 15 °C | 10,0ml/10g (low) | No propagation | BAM/ Tgb.-Nr.II.2-1510/01 and BAM/Tgb:-Nr. II.2-861/02 |
| 5 | Cumylperoxyneodecanoate, 87% - diluent type A | OP7 | 3115 | 1.0 mm | 8.0 mm (10g) | 293 ms, yes, slowly | <0,35 mm/s | 10 °C (400ml) | n.a. | No propagation | TNO 05DV3/0741 |
| 6 | 2,2-Di-(tert-amylperoxy)butane, 57% in diluent type A | OP7 | 3105 | 1.5 mm | 2.0 mm (10g) | <2170kPa | <0,35 mm/s | 70°C (400ml) | n.a. | Partial propagation UN A.6 | TNO 05DV3/0855 |
| 7 | 1,1-Di-(tert-butylperoxy)cyclohexane, 72% - diluent type B** | OP5 | 3103 | 2,0 mm | 6,0mm (50g) | - | <0,35 mm/s | 70 °C (400ml) | n.a. | No propagation (borderline) | BAM/ Tgb.-Nr.II.2-420/04 |
| 8 | 1,1-Di-(tert-butylperoxy)-3,3,5-trimethylcyclohexane, 90% - diluent type B** | OP5 | 3103 | 2,5 mm | 9.0 mm (10g, technically pure) | 800 ms (technically pure) | 0.48 mm/s (technically pure) | 70 °C (400ml) | n.a. | No propagation (technically pure) | BAM/ Tgb.-Nr. II.2- 442/04 |
| 9 | Di-(2,4-dichlorobenzoyl) peroxide, 52% as a paste | OP8 | 3118 | <1,0mm ("0") | 1,0mm (50g) | <2170kPa | <0,35 mm/s | 35°C (400ml) | n.a. | No propagation (77%) | TNO 03D2/0570 |
|  |  |  |  |  | Test results |  |  |  |  |  |  |
| no | Product | packaging | UN | Koenen/ E.1 | DPVT/ E.2 | P/T / C.1 | Deflagration / C.2 | SADT (1000ml) | Trauzl/ F.3 | Detonation/ A.1 cav. | approval number |
| 10 | Di-(2-ethylhexyl)peroxydicarbonate, 62% as a stable dispersion in water | OP8 IBC/31A 1250l | 3119 | <1,0mm ("A") | 1,0mm (50g) | <2170kPa | <0,35 mm/s | 5° C (400 ml) 0 °C (1000ml) | 0.4 ml/Modified Trauzl F.4 (no) | Partial propagation UN A.6 | TNO 02D2/0086 NO 02D2/0155 |
| 11 | Di-(3,5,5-trimethylhexanoyl)peroxide, 38% - diluent type B | T23 | 3119 | <1,0mm ("A") | <1,0mm(10g) | <2170kPa | <0,35 mm/s | 10 °C (Test H.3) | 7.2 ml/Modified Trauzl F.4 (low) | No propagation | TNO 02D2/0115 |
| 12 | Di-(2-neodecanoylperoxyisopropyl)-benzene, 42% as a stable dispersion in water | IBC/31A/ 1250l | 3119 | <1,0mm ("0") | 1,0mm (50g) | yes, slowly | <0,35 mm/s | 5 °C | No | No propagation | BAM/ Tgb.-Nr.II.2-484/02 |
| 13 | 3,3,5,7,7-Pentamethyl-1,2,4-trioxepane, technically pure | OP8 | 3107 | <1,0mm ("0") | 1.5 mm (10g) | <2170kPa | <0,35 mm/s | 120 °C (400 ml) | 6.4 ml/Modified Trauzl F.4 (low) | No propagation, UN A.6 | TNO 05DV3/0728 |
| 14 | Methyl isopropyl ketoneperoxide(s), 27% in diluent type A (active oxygen 6.5%) | OP8 | 3109 | <1,0mm ("A") | 2.0 mm (10g) | >30 ms | <0,35 mm/s | 50°C (400ml) | 3.1 ml/Modified Trauzl F.4 (low) | No propagation | TNO 02D/0087-rev.1 |
| 15 | Tert-Amyl peroxyneodecanoate, not more than 47 % in diluent typeA | OP8/ T23 | 3119 | <1,0mm (“0”) | 2,5 mm (10g) | <2170kPa* | 0,07 mm/s | 20°C (500ml) 0°C (3000ml) | 7 ml/Modified Trauzl F.4 (No) | No propagation | BAM/Tgb.-Nr. II.2-370/03 und II.2-354/04 |
| 16 | Tert-Amylperoxy-3,5,5-trimethylhexanoate, technically pure | OP7 | 3105 | 1,5 mm(“F”) | 8 mm (10g) | <2070kPa | 1,09 mm/s | 55°C | n.a. | No propagation | BAM/Tgb.-Nr. II.2-178/04 |
| 17 | 3-Hydroxy-1,1-dimethylbutylperoxyneodecanoate, not more than 77 % in diluent type A | OP7 | 3115 | < 1,0mm(“0”) | 3,5 mm (10g) | Yes,slowly | 0,12 mm/s | ≥ 15 °C | 9 ml/Modified Trauzl (No) | No propagation | BAM/Tgb.-Nr. II.2-55/04 und II.2-1109/00 |
| 18 | 3-Hydroxy-1,1-dimethylbutylperoxyneodecanoate, not more than 52%, as a stable dispersion in water | OP8/ IBC/31A/1250l | 3119 | <1,0 mm | 1,0 mm (50g) | <2170kPa | 0,115 mm/s | 15°C (500 ml) 5°C (1000 ml) | 7 ml/modified Trauzl F.3 | No propagation | BAM/Tgb.-Nr. 4-1660/90 und II.2-92/00 |
| 19 | 3-Hydroxy-1,1-dimethylbutylperoxyneodecanoate, not more than 52 % in diluent type A | OP8 | 3117 | <1,0 mm | 1,5 mm (10g) | <2170kPa | 0,115 mm/s | 15°C | 7 ml/modified Trauzl F.3 | No propagation *** | BAM/Tgb.-Nr. 4-1660/90 |

|  |  |  |  |  | Test results |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| no | Product | packaging | UN | Koenen/ E.1 | DPVT/ E.2 | P/T / C.1 | Deflagration / C.2 | SADT (1000ml) | Trauzl/ F.3 | Detonation/ A.1 cav. | approval number |
| 20 | (1,1-Di-(tert-Butylperoxy)cyclohexane 43% + tert-Butylperoxy-2-ethylhexanoate 16%) in diluent type A | OP7 | 3105 | 1 mm (“F”) | 8 mm (10g) | 766 ms | 0,401 mm/s | 60°C | 7 ml/modified Trauzl F.3 | No propagation | BAM/Tgb.-Nr. 4/3367/89 |
| 21 | 1,1-Di-(tert-Butylperoxy)cyclohexane, not more than 47% in diluent Type A | IBC/31A/1250l | 3109 | <1mm | 1,0 mm (50g) | < 2170kPa | 0,229 mm/s | >60°C | No | No propagation | BAM/Tgb-Nr. II.2-374/03 und 4-394/93 |
| 22 | tert-Butyl Peroxy -3,5,5-trimethylhexanoate, 42% with inert solid | OP7 | 3106 | <1.0mm (“0”) | 1.0 (50g) | 1375ms* | 0.27mm/s* | 55°C* (400 ml) | 2.9ml(no) | No propagation* | CA2002100015 |

* 	Results from DATATOP, data base on test results of organic peroxides, issued by TNO, The Netherlands

**  	Diluent type B with a boiling point >130°C

*** 	According BAM/Tgb. II.2-1109/00

# Text boxes

STSTE

Secretariat