| UNITED NATIONS |  | ST |
| --- | --- | --- |
|  | Secretariat | Distr. GENERAL ST/SG/AC.10/C.3/2006/59 13 April 2006 ENGLISH Original: FRENCH |

###### COMMITTEE OF EXPERTS ON THE TRANSPORT OF
DANGEROUS GOODS AND ON THE GLOBALLY 
HARMONIZED SYSTEM OF CLASSIFICATION
AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the
Transport of Dangerous Goods

Twenty-ninth session, 3-12 July 2006
Item 4 (a) of the provisional agenda

# PACKAGINGS

## Packaging performance

## Drop test

## Transmitted by the expert from France

### Introduction

1.	During the consideration of questions relating to IBCs, and in the Working Group that met in Paris earlier, it was noted that the characteristics of the target used in the drop test were not clearly defined and that different results could be obtained depending on the target used (see ST/SG/AC.10/C.3/56, paras. 42 to 44).  The expert from France said that he would submit a proposal on this matter.

2.	There is a standard that clearly defines the characteristics of the impact surface, namely ISO 2248 (para. 4.4).

3.	It is proposed to refer to this standard in order to clearly define the characteristics of the target used in the drop test.  This will enhance the reliability of the test and the quality of packagings.

GE.06-22454  (E)    090606    130606

4.	Given that the same issue arises for other packagings, an identical amendment is proposed in chapters 6.1, 6.2 and 6.6.

### Proposals

1.	In 6.5.6.9.3, add “in conformity with the requirements of standard ISO 2248” after “flat and horizontal surface”.

2.	In 6.1.5.3.4, add “in conformity with the requirements of standard ISO 2248” at the end of the sentence.

3.	In 6.3.2.5 (a), add “in conformity with the requirements of standard ISO 2248” at the end of the first sentence.

4.	In 6.6.5.3.4.3, add “in conformity with the requirements of standard ISO 2248” after “flat and horizontal surface”.

-----