#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2006/93

10 September 2006

Original: ENGLISH

## COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Thirtieth session

# Geneva, 4-12 (a.m.) December 2006

# Item 2(a) of the provisional agenda

PROPOSALS OF AMENDMENTS TO THE RECOMMENDATIONS

ON THE TRANSPORT OF DANGEROUS GOODS

Model Regulations on the Transport of Dangerous Goods

Portable tank assignments for toxic by inhalation liquids

Transmitted by the expert from the United States of America

Introduction

1.  	At its previous session the Sub-Committee considered portable tank instructions for UN1569, Bromoacetone (see ST/SG/AC.10/C.3/2006/57).  The Sub-Committee agreed that portable tank instruction T20 and portable tank special provisions TP2 and TP13 were appropriate based on Bromoacetone’s toxicity and vapour pressure.  The assignment agreed to for Bromoacetone is in accordance with Part II of the Guiding Principles for the UN Model Regulations which addresses portable tank assignments and special provisions.  The Guiding Principles specify that T20 shall be assigned to substances with an inhalation toxicity less than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50, and that T22 shall be assigned to substances with an inhalation toxicity less than or equal to 200 ml/m3 and a saturated vapour concentration greater than or equal to 500 LC50.

2.  	The expert from the United States has undertaken a review of liquids considered to be toxic by inhalation and proposes that appropriate portable tank instructions be assigned based on each substance’s vapour pressure and toxicity.

Proposals

3.  	Amend the portable tank instructions and special provisions as noted for the listed substances in annex.

* * * * *

Annex (ENGLISH ONLY)

Proposed Portable Tank Instructions for Toxic by Inhalation Liquids

|  |  |  |  |  | Current | Proposed |
| --- | --- | --- | --- | --- | --- | --- |
| UN # | Name | Class | SubRisk | PG | Instruction | Special Provisions | Instruction | Special Provisions |
| Liquids with an inhalation toxicity lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50: |
| 1092 | ACROLEIN, STABILIZED | 6.1 | 3 | I | T14 | TP2 TP7 TP13 | T22 | TP2, TP7, TP13 |
| 1185 | ETHYLENEIMINE, STABILIZED | 6.1 | 3 | I |  |  | T22 | TP2, TP13 |
| 1238 | METHYL CHLOROFORMATE | 6.1 | 3 8 | I | T14 | TP2 TP13 | T22 | TP2, TP13 |
| 1239 | METHYL CHLOROMETHYL ETHER | 6.1 | 3 | I | T14 | TP2 | T22 | TP2 |
| 1244 | METHYLHYDRAZINE | 6.1 | 3 8 | I | T14 | TP2 TP13 | T22 | TP2, TP13 |
| 1251 | METHYL VINYL KETONE, STABILIZED | 6.1 | 3 8 | I | T14 | TP2 TP13 | T22 | TP2, TP13 |
| 1834 | SULPHURYL CHLORIDE | 8 |  | I | T20 | TP2 TP12 | T22 | TP2, TP12 |
| 1994 | IRON PENTACARBONYL | 6.1 | 3 | I |  |  | T22 | TP2, TP13 |
| 2480 | METHYL ISOCYANATE | 6.1 | 3 | I |  |  | T22 | TP2, TP13 |
| 2481 | ETHYL ISOCYANATE | 3 | 6.1 | I | T14 | TP2 TP13 | T22 | TP2, TP13 |
| 2482 | n-PROPYL ISOCYANATE | 6.1 | 3 | I | T14 | TP2 TP13 | T22 | TP2, TP13 |
| 2483 | ISOPROPYL ISOCYANATE | 3 | 6.1 | I | T14 | TP2 TP13 | T22 | TP2, TP13 |
| 2484 | tert-BUTYL ISOCYANATE | 6.1 | 3 | I | T14 | TP2 TP13 | T22 | TP2, TP13 |
| 2486 | ISOBUTYL ISOCYANATE | 3 | 6.1 | II | T8 | TP2 TP13 | T22 | TP2, TP13, TP27 |
| 2605 | METHOXYMETHYL ISOCYANATE | 3 | 6.1 | I | T14 | TP2 TP13 | T22 | TP2, TP13 |
|  |  |  |  |  | Current | Proposed |
| UN # | Name | Class | SubRisk | PG | Instruction | Special Provisions | Instruction | Special Provisions |
| Liquids with an inhalation toxicity lower than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50 |
| 1098 | ALLYL ALCOHOL | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1135 | ETHYLENE CHLOROHYDRIN | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1143 | CROTONALDEHYDE or CROTONALDEHYDE, STABILIZED | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1163 | DIMETHYLHYDRAZINE, UNSYMMETRICAL | 6.1 | 3 8 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1182 | ETHYL CHLOROFORMATE | 6.1 | 3 8 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1510 | TETRANITROMETHANE | 5.1 | 6.1 | I |  |  | T20 | TP2, TP13 |
| 1541 | ACETONE CYANOHYDRIN, STABILIZED | 6.1 |  | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1560 | ARSENIC TRICHLORIDE | 6.1 |  | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1569 | BROMOACETONE | 6.1 | 3 | II | T3 | TP33 | T20 | TP2, TP13 |
| 1580 | CHLOROPICRIN | 6.1 |  | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1595 | DIMETHYL SULPHATE | 6.1 | 8 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1605 | ETHYLENE DIBROMIDE | 6.1 |  | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1613 | HYDROCYANIC ACID, AQUEOUS SOLUTION (HYDROGEN CYANIDE, AQUEOUS SOLUTION) with not more than 20% hydrogen cyanide | 6.1 |  | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1647 | METHYL BROMIDE AND ETHYLENE DIBROMIDE MIXTURE, LIQUID | 6.1 |  | I |  |  | T20 | TP2, TP13 |
| 1670 | PERCHLOROMETHYL MERCAPTAN | 6.1 |  | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1672 | PHENYLCARBYLAMINE CHLORIDE | 6.1 |  | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1695 | CHLOROACETONE, STABILIZED | 6.1 | 3 8 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1722 | ALLYL CHLOROFORMATE | 6.1 | 3 8 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1746 | BROMINE TRIFLUORIDE | 5.1 | 6.1 8 | I | T22 | TP2 TP12 TP13 | T20 | TP2, TP12, TP13 |
| 1752 | CHLOROACETYL CHLORIDE | 6.1 | 8 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1809 | PHOSPHORUS TRICHLORIDE | 6.1 | 8 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1810 | PHOSPHORUS OXYCHLORIDE | 8 |  | II | T7 | TP2 | T20 | TP2 |
|  |  |  |  |  | Current | Proposed |
| UN # | Name | Class | SubRisk | PG | Instruction | Special Provisions | Instruction | Special Provisions |
| 1838 | TITANIUM TETRACHLORIDE | 8 |  | II | T10 | TP2 TP13 | T20 | TP2, TP13 |
| 1892 | ETHYLDICHLOROARSINE | 6.1 |  | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 2232 | 2-CHLOROETHANAL | 6.1 |  | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 2334 | ALLYLAMINE | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 2337 | PHENYL MERCAPTAN | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 2382 | DIMETHYLHYDRAZINE, SYMMETRICAL | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 2407 | ISOPROPYL CHLOROFORMATE | 6.1 | 3 8 | I |  |  | T20 | TP2, TP13 |
| 2438 | TRIMETHYL-ACETYL CHLORIDE | 6.1 | 3 8 | I | T14 |  | T20 | TP2, TP13 |
| 2442 | TRICHLORO-ACETYL CHLORIDE | 8 |  | II | T7 | TP2 | T20 | TP2 |
| 2474 | THIOPHOSGENE | 6.1 |  | II | T7 |  | T20 | TP2 |
| 2477 | METHYL ISOTHIOCYANATE | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 2485 | n-BUTYL ISOCYANATE | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 2487 | PHENYL ISOCYANATE | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 2488 | CYCLOHEXYL ISOCYANATE | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 2521 | DIKETENE, STABILIZED | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 2606 | METHYL ORTHOSILICATE | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 2644 | METHYL IODIDE | 6.1 |  | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 2646 | HEXACHLOROCYCLO-PENTADIENE | 6.1 |  | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 2668 | CHLOROACETONITRILE | 6.1 | 3 | II | T7 | TP2 | T20 | TP2 |
| 2826 | ETHYL CHLOROTHIOFORMATE | 8 | 3 | II | T7 | TP2 | T20 | TP2 |
| 3023 | 2-METHYL-2-HEPTANETHIOL | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 3079 | METHACRYLONITRILE, STABILIZED | 3 | 6.1 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 3246 | METHANESULPHONYL CHLORIDE | 6.1 | 8 | I | T14 | TP2 TP12 TP13 | T20 | TP2, TP12, TP13 |
| 3294 | HYDROGEN CYANIDE, SOLUTION IN ALCOHOL with not more than 45% hydrogen cyanide | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |

# Text boxes

STSTE

Secretariat