#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2006/99

11 September 2006

Original: ENGLISH

## COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Thirtieth session

# Geneva, 4-12 (a.m.) December 2006

# Item 2(a) of the provisional agenda

PROPOSALS OF AMENDMENTS TO THE RECOMMENDATIONS

ON THE TRANSPORT OF DANGEROUS GOODS

Model Regulations on the Transport of Dangerous Goods

P200 Filling Ratio Amendments

Transmitted by the expert from the United States of America

Background

- Based on a proposal by the United States of America (ST/SG/AC.10/C.3/2006/41), the Sub-Committee at its twenty-ninth session agreed to amend the filling ratio values for certain gases in P200.  The result of this amendment was to increase the filling ratio value for six gases, and to reconsider the value for Germane based on the technical information submitted to the experts. The technical justification for this amendment was based on an independent study performed by the U.S. National Institute of Standards and Technology (NIST).  This study was designed to verify that the listed P200 filling ratio values provided an adequate level of safety.  The NIST study has been reviewed by members of the gases working group at previous Sub-Committee sessions.  During the 25th session of the Sub-Committee, the report of the gases working group (UN/SCETDG/25/INF.98) identified that experts from Germany and the US agreed to collaborate on proposed changes to the filling ratios listed in P200 based on the NIST calculations.   The same NIST study indicated higher filling ratio values for several additional gases but it was agreed that the values should be further reviewed.  Subsequently, experts from Germany (BAM and PRB), the US DOT, industry and NIST met in July 2005 and reviewed each liquefied gas separately for the purpose of refining the filling ratio data that is currently included in the NIST final report.

During the Sub-Committee’s 29th session, representatives from Germany (BAM), EIGA and the United States agreed to propose to amend the filling ratios of all the liquefied gases of P200 with the final values that were calculated and confirmed by NIST with an uncertainty of less than 1%.  In support of this proposal the following documents are provided as Annexes to this paper (reproduced in informal document UN/SCETDG/30/INF.4).

Annex 1: NIST Final Report: Calculation and Verification of Filling Ratios for Liquified Gases

Annex 2: New Filling Conditions according to NIST Report DTRS 56-02-X-0049 November 2002.  This document is a supplement to the original NIST Final Report that provides revised values based on the experts review during the July 2005 meeting.

A separate informal proposal will be submitted considering related changes to the filling densities used in Portable Tank Instruction T50.

Proposal

- Amend the P200 filling ratio values as identified in Table 1 below.

Table 1 – Amended filling ratios for P200

| UN No | Name | Tc (oC) | Ptest(bar) | Filling ratio | Percentage Difference | Proposed minimum Ptest (bar) gauge | Uncertainty | Checked by |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Amended Filling Ratio Value | UN vs. NIST |  |  |  |
|  |  |  |  |  |  | See Note |  |  |  |
|  |  |  | UN, gauge | UN |  |  |  | class | NIST |
| 1982 | Tetrafluoromethane (R14) | -45.64 | 200 | 0.62 | 0.71 | 14.5 | No Change | 1 | Confirmed |
| 2451 | Nitrogen trifluoride | -39.15 | 200 | 0.5 | 0.63 | 26.0 | No Change | 1 | Confirmed |
| 2451 | Nitrogen trifluoride | -39.15 | 300 | 0.75 | 0.82 | 9.3 | No Change | 1 | Confirmed |
| 1962 | Ethylene | 9.2 | 225 | 0.34 | 0.34 | 0.0 | No Change | 1 | Confirmed |
| 1962 | Ethylene | 9.2 | 300 | 0.37 | 0.38 | 2.7 | No Change | 1 | Confirmed |
| 2036 | Xenon | 16.584 | 130 | 1.24 | 1.28 | 3.2 | No Change | 1 | Confirmed |
| 2599 | R503 | 18.595 | 31 | 0.11 | 0.12 | 9.1 | No Change | 1 | Confirmed |
| 2193 | Hexafluoroethane (R116) | 19.88 | 200 | 1.1 | 1.13 | 2.7 | No Change | 1 | Confirmed |
| 1984 | Trifluoromethane (R23) | 26.143 | 190 | 0.87 | 0.88 | 1.1 | No Change | 1 | Confirmed |
| 1984 | Trifluoromethane (R23) | 26.143 | 250 | 0.95 | 0.96 | 1.1 | No Change | 1 | Confirmed |
| 1022 | Chlorotrifluoromethane (R13) | 28.85 | 120 | 0.9 | 0.90 | 0.0 | No Change | 1 | Confirmed |
| 1022 | Chlorotrifluoromethane (R13) | 28.85 | 190 | 1.04 | 1.04 | 0.0 | No Change | 1 | Confirmed |
| 1022 | Chlorotrifluoromethane (R13) | 28.85 | 250 | 1.1 | 1.11 | 0.9 | No Change | 1 | Confirmed |
| 1013 | Carbon dioxide | 30.978 | 190 | 0.66 | 0.68 | 3.0 | No Change | 1 | Confirmed |
| 1013 | Carbon dioxide | 30.978 | 250 | 0.75 | 0.76 | 1.3 | No Change | 1 | Confirmed |
| 1035 | Ethane | 32.18 | 95 | 0.25 | 0.25 | 0.0 | No Change | 1 | Confirmed |
| 1035 | Ethane | 32.18 | 120 | 0.29 | 0.30 | 3.4 | No Change | 1 | Confirmed |
| 1035 | Ethane | 32.18 | 300 | 0.39 | 0.40 | 2.6 | No Change | 1 | Confirmed |
| 1080 | Sulphur hexafluoride | 45.583 | 70 | 1.04 | 1.06 | 1.9 | No Change | 1 | Confirmed |
| 1080 | Sulphur hexafluoride | 45.583 | 140 | 1.33 | 1.34 | 0.8 | No Change | 1 | Confirmed |
| 1080 | Sulphur hexafluoride | 45.583 | 160 | 1.37 | 1.38 | 0.7 | No Change | 1 | Confirmed |
| 2454 | Methyl fluoride (R41) | 44.13 | 300 | 0.36 | 0.63 | 75.0 | No Change | 1 | Confirmed |
| 3220 | Pentafluoroethane (R125) | 66.015 | 36 | 0.72 | 0.87 | 20.8 | 35 | 1 | Confirmed |
| 3339 | R407B | 74.284 | 38 | 0.93 | 0.93 | 0.0 | 33 | 1 | Confirmed |
| 3338 | R407A | 81.864 | 36 | 0.94 | 0.94 | 0.0 | 32 | 1 | Confirmed |
| 3340 | R407C | 86.021 | 35 | 0.95 | 0.95 | 0.0 | 30 | 1 | Confirmed |
| 1077 | Propylene | 92.42 | 30 | 0.43 | 0.43 | 0.0 | 27 | 1 | Confirmed |
| 1018 | Chlorodifluoromethane (R22) | 96.145 | 29 | 1.03 | 1.03 | 0.0 | 27 | 1 | Confirmed |
| 1978 | Propane | 96.675 | 25 | 0.42 | 0.43 | 2.4 | 23 | 1 | Confirmed |
| 1053 | Hydrogen sulphide | 100.45 | 55 | 0.67 | 0.67 | 0.0 | 48 | 1 | Confirmed |
| 3296 | Heptafluoropropane (R227ea) | 101.65 | 15 | 1.2 | 1.21 | 0.8 | 13 | 1 | Confirmed |
| 3159 | 1,1,1,2-Tetrafluoroethane (R134a) | 101.06 | 22 | 1.04 | 1.05 | 1.0 | 18 | 1 | Confirmed |
| 1028 | Dichlorodifluoromethane (R12) | 111.97 | 18 | 1.15 | 1.15 | 0.0 | 16 | 1 | Confirmed |
| 1030 | 1,1-Difluoroethane (R152a) | 113.26 | 18 | 0.79 | 0.79 | 0.0 | 16 | 1 | Confirmed |
| 1021 | 1-Chloro-1,2,2,2-tetrafluoroethane (R124) | 122.28 | 12 | 1.2 | 1.2 | 0.0 | 11 | 1 | Confirmed |
| 1027 | Cyclopropane | 125.15 | 20 | 0.53 | 0.55 | 3.8 | 18 | 1 | Confirmed |
| 1005 | Ammonia, anhydrous | 132.25 | 33 | 0.53 | 0.54 | 1.9 | 29 | 1 | Confirmed |
| 1969 | Isobutane | 134.67 | 10 | 0.49 | 0.49 | 0.0 | 10 (9) | 1 | Confirmed |
| 2517 | 1-Chloro-1,1-difluoroethane (R142b) | 137.11 | 10 | 0.99 | 0.99 | 0.0 | 10 (9) | 1 | Confirmed |
| 1958 | 1,2-Dichloro-1,1,2,2-tetrafluoroethane (R114) | 145.68 | 10 | 1.3 | 1.3 | 0.0 | 10 (6) | 1 | Confirmed |
| 1011 | Butane | 151.98 | 10 | 0.51 | 0.52 | 2.0 | 10 (7) | 1 | Confirmed |
| 1079 | Sulphur dioxide | 157.49 | 14 | 1.23 | 1.23 | 0.0 | 12 | 1 | Confirmed |
| 2204 | Carbonyl Sulphide | 105.65 | 26 | 0.84 | 0.87 | 3.6 | 30 | 1 | Confirmed |
| 2044 | 2,2-Dimethylpropane | 160.65 | 10 | 0.53 | 0.53 | 0.0 | 10 (5) | 1 | Confirmed |

# Text boxes

STSTE

Secretariat