| UNITED NATIONS | E |
| --- | --- |

|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2006/43 27 March 2006 ENGLISH Original: ENGLISH AND FRENCH |
| --- | --- | --- |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

One-hundred-and-thirty-ninth session

Geneva, 20-23 June 2006

Item 4.2.6. of the provisional agenda

## PROPOSAL FOR SUPPLEMENT 2 TO THE 10 SERIES OF AMENDMENTS

## TO REGULATION No. 13

(Braking)

# Submitted by the Working Party on Brakes and Running Gear (GRRF)

Note:  The text reproduced below was adopted by GRRF at its fifty-ninth session (ECE/TRANS/WP.29/GRRF/59, paras. 5 and 6) and is submitted for consideration to WP.29 and AC.1.  It is based on the text of ECE/TRANS/WP.29/GRRF/2006/5 and ECE/TRANS/WP.29/GRRF/2006/6, not amended, and on ECE/TRANS/WP.29/GRRF/2004/19/Rev.2, as amended by paragraph 6 of the report.

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user. Documents are also available via the INTERNET: http://www.unece.org/trans/main/welcwp29.htm

Paragraph 5.2.2.13., amend to read:

"5.2.2.13.	Trailers of category O3 shall be equipped with an anti-lock braking system in accordance with the requirements of annex 13 to this Regulation.  Trailers of category O4 shall be equipped with an anti-lock braking system in accordance with the category A requirements of annex 13 to this Regulation."

Annex 19,

Add a new paragraph 5.1.2., to read:

"5.1.2.	Tests carried out on trailers of category O4 will be deemed to cover the requirements for trailers of O3 category."

Paragraph 5.4.1.2.1., amend to read:

"5.4.1.2.1.	Axle loading – the trailer(s) to be tested shall be loaded so that the axle load is 2500 kg +/- 200 kg or 35 per cent +/- 200 kg of the permissible static axle load whichever is the lower."

Paragraph 5.4.1.2.2., amend to read:

"5.4.1.2.2.	It shall be ensured that "full cycling" of the anti-lock braking system can be achieved throughout the dynamic tests defined in paragraph 6.1.3. of annex 13 to this Regulation."

Annex 19 –appendix 5,

Paragraph 2.5., amend to read:

"2.5.	Scope of application with respect to suspension type:

Air suspension:	Any type of balanced "trailing arm" air suspension

Other suspensions:	to be defined by manufacturer, model and type (balanced/unbalanced)."

- - - - -