| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2006/99 14 July 2006 ENGLISH Original: ENGLISH AND FRENCH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

One-hundred-and-fortieth session

Geneva, 14-17 November 2006

Item 4.2.21. of the provisional agenda

PROPOSAL FOR SUPPLEMENT 9 TO REGULATION No. 43

(Safety glazing)

Submitted by the Working Party on General Safety Provisions (GRSG)

Note:	The text reproduced below was adopted by GRSG at its ninetieth session. It is based on document ECE/TRANS/WP.29/GRSG/2006/16, not amended. It is submitted to WP.29 and to AC.1 for consideration (ECE/TRANS/WP.29/GRSG/69, paras. 47 and 49).

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user. Documents are also available via the INTERNET: http://www.unece.org/trans/main/welcwp29.htm

Paragraphs 1. and 1.1., insert a reference to a new footnote 1/, the corresponding footnote 1/ and amend to read:

"1.	SCOPE

This Regulation applies to:

-	safety glazing materials intended for installation as windscreens or other panes, 		or as partitioning, on vehicles of category L, M, N, O, and T 1/;

-	vehicles of category M, N and O with regard to the installation of these materials;

in both cases, to the exclusion of glazing for lighting and light-signalling devices and 	instrument panels, of special bullet-proof glazing and of double-windows.

__________________

1/	As defined in Annex 7 to the Consolidated Resolution on the Construction of Vehicles (R.E.3), (document TRANS/WP.29/78/Rev.1/Amend.2 as last amended by Amend.4)."

Paragraph 5.4.1., the reference to footnote 1/ and footnote 1/, renumber as footnote 2/ and amend to read:

"2/	1 for Germany, …, 47 for South Africa, 48 for New Zealand, 49 for Cyprus, 50 for Malta, 51 for the Republic of Korea, 52 for Malaysia and 53 for Thailand.  Subsequent numbers …"

Paragraph 5.5.1., the reference to footnote 2/ and footnote 2/, renumber as footnote 3/.

Paragraph 5.11.1., the reference to footnote 3/ and footnote 3/, renumber as footnote 4/ and amend to read:

"4/	See footnote 2/ of para. 5.4.1."

- - - - -