#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2007/13

# ST/SG/AC.10/C.4/2007/3

12 April 2007

Original: ENGLISH

## COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

## HARMONIZED SYSTEM OF CLASSIFICATION

## AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the	Sub-Committee of Experts on the Globally

# Transport of Dangerous Goods	Harmonized System of Classification and

# Labelling of Chemicals

# Thirty-first session

# Geneva, 2-6 July 2007	Thirteenth session

# Item 10(b) of the provisional agenda	Geneva, 9-11 July 2007

# Item 2(a) of the provisional agenda

UPDATING OF THE GLOBALLY HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS (GHS)

Physical hazards

Amendments to Chapter 2.1 of the GHS (Explosives)

Transmitted by the Sporting Arms and Ammunition Manufacturers Institute (SAAMI)

#### Introduction

# 1.	During the eleventh session, the Sporting Arms and Ammunition Manufacturers Institute (SAAMI) asked that the Sub-Committee of Experts on the GHS reconsiders its decision of the eighth session where the GHS pictogram for 1.4 explosives was changed to an exploding bomb on the basis of  proposal  ST/SG/AC.10/C.4/2004/12. SAAMI’s proposal was submitted to the GHS Subcommittee as ST/SG/AC.10/C.4/2006/7 and, since it involves physical hazards, also to the TDG Subcommittee as ST/SG/AC.10/C.3/2006/61.

2.	The proposal asserted that, for many reasons, an exploding bomb pictogram hazard is not appropriate for 1.4S sporting ammunition. In this regard, the pictogram constitutes an excessive warning, and is hence detrimental to safety. Therefore, the proposal asked that the 1.4 symbol be realigned with the transport label to remove the exploding bomb, or alternatively, that certain sporting ammunition products be labelled without the exploding bomb pictogram.

3.	However, some experts in the explosives working group were concerned about 1.4S products which may be more dangerous than sporting ammunition. They believed that the exploding bomb pictogram was appropriate for certain other 1.4S products. Therefore they opposed a return for Division 1.4 to the transport label with no exploding bomb pictogram. Other experts supported the removal of the exploding bomb for 1.4S, but wanted a more general solution , and not one specific to certain sporting ammunition products. Therefore, SAAMI was invited to submit a revised proposal to address these concerns in July 2007.

4.	Regarding products which warrant an exploding bomb pictogram, it is a matter of debate of whether they should be in 1.4S. The explosives working group is studying this issue separately, and if a tool is implemented to remove these products from 1.4S, such as the proposed 6(d) test, then there is no reason to keep an exploding bomb pictogram on the remaining products.

5.	1.4S products are recognizably different in hazard than other 1.4 divisions, part of the criteria being that fire fighters and emergency responders are not significantly endangered in the immediate vicinity of a fire. In many different instances in the UN Model Regulations, 1.4S products are singled out for exceptions. Therefore there is justification to continue this trend and assign a less stringent GHS pictogram to 1.4S products than other 1.4 divisions.

6.	A separate pictogram for 1.4S could be implemented by amending the GHS Explosives Table in Annex 1 of the GHS as follows. This is very similar to Table 2.1.2, which could be similarly amended. Changes are highlighted:

## Proposal

- Implement the changes to the GHS Explosives Table in Annex 1 as shown above.

- Implement the same changes to Table 2.1.2, i.e. a new column for 1.4S indicating a 1.4S transport pictogram as the GHS pictogram for 1.4S materials.

# Text boxes

STSTE

Secretariat