# UN/SCETDG/31/INF.26

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Thirty-first session

Geneva, 2-6 July 2007

Item 6 of the provisional agenda

MISCELLANEOUS PROPOSALS OF AMENDMENTS TO THE MODEL REGULATIONS ON THE TRANSPORT OF DANGEROUS GOODS

Proposed revision of Chapter 2.9

Transmitted by the Expert from the United Kingdom

Introduction

- In the process of revising the Chapter 2.9 Class 9 text in the IMDG Code it was observed by the expert from the United Kingdom that this chapter is presented in a more user-friendly way in RID/ADR/ADN than either the Model Regulations or the Code. As a repository for substances and articles that do not fit readily into the other eight Classes of dangerous goods, further user guidance would seem appropriate. This paper proposes an updated and more complete section describing the assignment of substances and articles to Class 9.

- The text for the next edition of the IMDG Code will be finalized at the International Maritime Organization’s DSC 12 and the Editorial and Technical Group in September 2007 and it this intention of the United Kingdom to submit a similar proposal for that session in order to maximize modal harmonization.

Existing text is shown by underlining.

“CHAPTER 2.9

CLASS 9 - MISCELLANEOUS DANGEROUS SUBSTANCES, ARTICLES AND ENVIRONMENTALLY HAZARDOUS SUBSTANCES (AQUATIC ENVIRONMENT)

### 2.9.1	Definitions

2.9.1.1	Class 9 substances and articles (miscellaneous dangerous substances and articles) are substances and articles which, during transport present a danger not covered by other classes.

2.9.1.2	Genetically modified micro-organisms (GMMOs) and genetically modified organisms (GMOs) are micro-organisms and organisms in which genetic material has been purposely altered through genetic engineering in a way that does not occur naturally.

### 2.9.2	Assignment to Class 9

The substances and articles of Class 9 are subdivided as follows:

Substances which, on inhalation as fine dust, may endanger health

2212	BLUE ASBESTOS (crocidolite) or

2212	BROWN ASBESTOS (amosite, mysorite)

2590	WHITE ASBESTOS (chrysotile, actinolite, anthophyllite, tremolite)

Substances evolving flammable vapour

2211	POLYMERIC BEADS, EXPANDABLE, evolving flammable vapour

3314	PLASTICS MOULDING COMPOUND in dough, sheet or extruded rope form evolving flammable vapour

Lithium and lithium ion batteries

3090	LITHIUM METAL BATTERIES (including lithium alloy batteries)

3091	LITHIUM METAL BATTERIES CONTAINED IN EQUIPMENT or 3091 LITHIUM METAL BATTERIES PACKED WITH EQUIPMENT

3480	LITHIUM ION BATTERIES (including lithium ion polymer batteries)

3481	LITHIUM ION BATTERIES CONTAINED IN EQUIPMENT or LITHIUM ION BATTERIES PACKED WITH EQUIPMENT (including lithium ion polymer batteries)

Live-saving appliances

2990	LIFE-SAVING APPLIANCES, SELF-INFLATING

3072	LIFE-SAVING APPLIANCES NOT SELF-INFLATING containing dangerous goods as equipment

3268	AIR BAG INFLATORS or 3268 AIR BAG MODULES or 3268 SEAT-BELT PRETENSIONERS

Other substances or articles presenting a danger during transport, but not meeting the definitions of another class

1841	ACETALDEHYDE AMMONIA

1845	CARBON DIOXIDE, SOLID (DRY ICE)

1931	ZINC DITHIONITE (ZINC HYDROSULPHITE)

1941	DIBROMODIFLUOROMETHANE

1990	BENZALDEHYDE

2071	AMMONIUM NITRATE BASED FERTILISER

2216	FISHMEAL (FISH MEAL SCRAP), STABILIZED

2807	MAGNETIZED MATERIAL

2969	CASTOR BEANS, or CASTOR MEAL, or CASTOR POMACE, or

2969	CASTOR FLAKE

3166	ENGINE, INTERNAL COMBUSTION or VEHICLE FLAMMABLE GAS POWERED or VEHICLE, FLAMMABLE LIQUID POWERED

3171	BATTERY-POWERED VEHICLE or BATTTERY-POWERED EQUIPMENT

3316	CHEMICAL KIT, or

3316	FIRST AID KIT

3334	AVIATION REGULATED LIQUID, N.O.S.

3335	AVIATION REGULATED SOLID, N.O.S.

3359	FUMIGATED UNIT

3363	DANGEROUS GOODS IN MACHINERY or DANGEROUS GOODS IN APPARATUS

Substances and apparatus which, in the event of fire, may form dioxins

This group of substances and articles includes:

2315	POLYCHLORINATED BIPHENYLS, LIQUID

3432	POLYCHLORINATED BIPHENYLS, SOLID

3151	POLYHALOGENATED BIPHENYLS, LIQUID or POLYHALOGENATED TERPHENYLS, LIQUID

3152	POLYHALOGENATED BIPHENYLS, SOLID or POLYHALOGENATED TERPHENYLS, SOLID

Elevated temperature substances

(a)	Liquid

3257	ELEVATED TEMPERATURE LIQUID, N.O.S., at or above 100 °C and below its flash-point (including molten metal, molten salts, etc.)

(b)	Solid

3258	ELEVATED TEMPERATURE SOLID, N.O.S., at or above 240 °C

Environmentally hazardous substances (aquatic environment)

(a)	Liquid

3077	ENVIRONMENTALLY HAZARDOUS SUBSTANCE, LIQUID, N.O.S

(b)	Solid

3082	ENVIRONMENTALLY HAZARDOUS SUBSTANCE, SOLID, N.O.S.

GMMOs and GMOs

3245	GENETICALLY MODIFIED MICRO-ORGANISMS or GENETICALLY MODIFIED ORGANISMS

GMMOs and GMOs which do not meet the definition of infectious substances (see 2.6.3) but which are capable of altering animals, plants or microbiological substances in a way not normally the result of natural reproduction. They shall be assigned to UN 3245. GMMOs or GMOs are not subject to these Regulations when authorized for use by the competent authorities of the countries of origin, transit and destination.

____________