REGULATION No. 48

(Installation of lighting and light-signalling devices)

Requirements for light-signalling lamps

A.	PROPOSAL

6.19.7.

…

The daytime running lamp on the relevant side of the vehicle may be automatically switched OFF during the entire period (both on and off cycle) of activation of the direction-indicator lamp function or warning lamp function.

If the daytime running lamp and the direction indicator lamp are reciprocally incorporated, the electrical connections shall be such that the daytime running lamp on the relevant side of the vehicle is automatically switched OFF during the entire period (both on and off cycle) of activation of the direction-indicator lamp function or warning lamp function.

# B.	JUSTIFICATION

The proposal is intended to ensure conspicuity of front direction-indicator lamps if they are located close to daytime running lamps, by amending the existing provisions, which are already applicable to dipped-beam headlamps and/or front fog lamps.