Proposal for draft amendments to GLOBAL TECHNICAL REGULATION (gtr No. 4) on world-wide harmonized heavy-duty certification (WHDC)

UNIFORM PROVISIONS CONCERNING THE TEST PROCEDURE FOR COMPRESSION-IGNITION (C.I.) AND POSITIVE-IGNITION (P.I.) ENGINES FUELLED WITH NATURAL GAS (NG) OR LIQUEFIED PETROLEUM GAS (LPG) WITH REGARD TO THE EMISSION OF POLLUTANTS

Ref. Documents: ECE/TRANS/WP.29/GRPE/2006/17 dt. 27 March 2006

A.	PROPOSAL

The current paragraph 3.1.12.:

"3.1.12.	"high speed (nhi)" means the highest engine speed where 70 per cent of the declared maximum power occurs."

amend to read:

"3.1.12.	"high speed (nhi)" means the highest engine speed where 70 per cent of the declared maximum power occurs.  In case of gas engines where determination of nhi is not possible due a sudden drop of power, nhi will be replaced with rated speed."

B.	JUSTIFICATION

It may not be possible to determine nhi for “gas engines” because, after the max power point, there is a sudden power drop to zero due to immediate fuel cut-off and ignition cut-off.  Currently in India we are using rated speed as nhi for gas engines.  Hence the above text has been incorporated so that in case of gas or other engines where determination of nhi is not possible, rated speed could be used in place of nhi

- - - - -