# UN/SCETDG/34/INF.57

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the 
Transport of Dangerous Goods

# Thirty-fourth session

Geneva, 1-9 December 2008

# Item 3 of the provisional agenda

PERFORMANCE OF PACKAGINGS INCLUDING IBCS

Proposed new test based on Doc 2008/100.

Add a new sentence in 6.5.2.2.4 to read as follows:

“The inner receptacle of composite IBCs manufactured after 1 January 2011 shall bear the markings as specified in 6.5.2.1.1. (b), (c), (d) where this date is that of the manufacture of the plastics inner receptacle, (e) and (f). The UN packaging symbol shall not be applied. The marking shall be durable, legible and placed in a location so as to be readily visible when placed in the outer casing. Except for the date, it shall be applied in the sequence shown.

The date of the manufacture of the plastics inner receptacle may alternatively be marked on it adjacent to the remainder of the marking.

An example of an appropriate marking method is:”

_________________