| Transmitted by the expert from the Russian Federation | Informal document No. GRPE-56-01 (56th GRPE, 3-6 June 2008, agenda item 2(b)) |
| --- | --- |

Gasoline engine WHDC validation study

On the request WHDC working group during 55 GRPE session the validation study of WHDC cycles with gasoline engine was carried out.

Engine tested:

Engine type – V 8, four stroke, positive ignition, 4.67 l capacity;

Fuel – petrol;

Fuel feed- carburetor type with electronic control of air/fuel ratio;

Emissions control – 3-way catalytic converter.

Conclusion

Validation study with WHTC and WHSC cycles was carried out.  ETC and ESC tests were also carried out for comparison.

The engine tested could not meet the validation criteria of the GTR completely both in WHTC and ETC cycles. Nevertheless the compliance with the statistics criteria with the WHTC is obviously better than for ETC.  Suggested reason for engine not conforming the statistics criteria is that the engine initially was meant to comply mainly with the stationary (ESC) modes.

As for load/speed distribution the pattern mainly the same as one for the diesel engines determined early.  WHTC cover wider range of the engine map than ETC.  As a whole both WHTC and WHSC cycles are more appropriate than ETC and ESC ones.

Emissions, g/kWt.h

|  | CO | CH | NOx |
| --- | --- | --- | --- |
| WHTC | 0,78 | 0,15 | 2,19 |
| WHSC | 4,73 | 0,20 | 4,42 |
| ETC | 1,17 | 0,24 | 2,12 |
| ESC | 7,77 | 0,18 | 2,62 |

Driveability WHTC

|  | Speed Torque Power limit actual limit actual limit actual Standard error of estimate (SEE) of Y on X max 100 min-1 25,38 35,36 27,6 6,4 5,8 Slope of the regression line, m 0,95-1,03 1,006 0,83-1,03 0,71 0,89-1,03 0,76 Coefficient of determination, r2 min 0,97 0,995 min 0,85 0,77 min 0,91 0,81 Y intercept of the regression line, b ±50 min-1 -13,1 20 23,1 4 3,78 |
| --- | --- |

Driveability ETC

|  | Speed Torque Power limit actual limit actual limit actual Standard error of estimate (SEE) of Y on X max 100 min-1 28,37 35,36 32,2 6,4 7,30 Slope of the regression line, m 0,95-1,03 0,999 0,83-1,03 0,74 0,89-1,03 0,762 Coefficient of determination, r2 min 0,97 0,995 min 0,85 0,79 min 0,91 0,81 Y intercept of the regression line, b ±50 min-1 0,708 20 21,92 4 4,42 |
| --- | --- |