Regulation No. 13-H (Passenger Car Braking)

Proposal on the transitional provisions for amendments to Regulation No. 13-H

regarding Brake Assist Systems (BAS)

Proposal

In ECE/TRANS/WP.29/GRRF/2008/15,

Paragraphs 12.4. and 12.5., should be deleted (the 2 options).

Insert new amendments to paragraphs 12.2. and 12.3., to read:

"12.2.	As from 1 November 2011, Contracting Parties applying this Regulation may refuse to grant national or regional type approval if the vehicle type does not meet the requirements of this Regulation as amended by Supplements 7 and 8 to this Regulation, and is not fitted with an Electronic Stability Control System and a Brake Assist System meeting the requirements of Annexes 9 and 10 to this Regulation.

12.3.	As from 1 November 2013, Contracting Parties applying this Regulation may refuse first national registration of a vehicle which does not meet the requirements of this Regulation as amended by Supplements 7 and 8, and is not fitted with an Electronic Stability Control System and a Brake Assist System meeting the requirements of Annexes 9 and 10 to this Regulation."

- - - - -