| UNITED NATIONS |  | ST |
| --- | --- | --- |
|  | Secretariat | Distr. GENERAL ST/SG/AC.10/C.3/2009/28 5 August 2009 Original: ENGLISH |

COMMITTEE OF EXPERTS ON THE TRANSPORT OF
DANGEROUS GOODS AND ON THE GLOBALLY
HARMONIZED SYSTEM OF CLASSIFICATION
AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the 
Transport of Dangerous Goods

# Thirty-sixth session
Geneva, 30 November – 9 December 2009

Item 10 of the provisional agenda

ISSUES RELATING TO THE GLOBALLY HARMONIZED SYSTEM

OF CLASSIFICATION AND LABELLING OF CHEMICALS (GHS)

Criteria to assign packing groups to corrosive substances

# Transmitted by the expert from Spain

Introduction

1.	In order to prepare a document for the thirty-sixth session, the expert from Spain submitted a proposal in an informal document (INF.14) at the thirty-fifth session of the Sub-Committee in June 2009. The result was that the Sub-Committee considered that this proposal could be discussed at the thirty-sixth session in the more general context of corrosivity criteria (see ST/SG/AC.10/C.3/70, para. 83).

2.	In brief, paragraph 2.8.2.5 contains the criteria for assigning packing groups to corrosive substances. In order to clarify this text, a table is proposed. This table would be similar to the already existing one in 2.3.2.6, for the hazard grouping based on flammability.

Proposal

3.	Add, after 2.8.2.5, a table summarizing the criteria of paragraphs (a), (b) and (c) as follows:

| Packing Group | Exposure time | Observation time | Corrosion rate on steel/aluminium |
| --- | --- | --- | --- |
| I | ≤ 3 min | ≤ 60 min | - |
| II | > 3 min ≤ 60 min | ≤ 14 d | - |
| III | > 60 min ≤ 4 h | ≤ 14 d | > 6.25 mm a year at a test temperature of 55ºC |

_________________

# Footnotes

In accordance with the programme of work of the Sub-Committee for 2009-2010 approved by the Committee at its fourth session (refer to ST/SG/AC.10/C.3/68, para. 118 (i) and ST/SG/AC.10/36, para. 14).