# UN/SCETDG/35/INF.27/Add.1/Corr.1

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Thirty-fifth session

Geneva, 22 - 26 June 2009

Item 5 of the provisional agenda

MISCELLANEOUS PROPOSALS OF AMENDMENTS TO THE MODEL

REGULATIONS ON THE TRANSPORT OF DANGEROUS GOODS

Definition of Intermediate Bulk Containers (IBCs)

Supplement to ST/SG/AC.10/C.3/2009/27

Corrigendum

Transmitted by the International Dangerous Goods and

Containers Association (IDGCA)

# The following pages 3 and 4 should be inserted

FSUE "NIIparashutostroeniya"

# Flight-Test Complex

# General

1.1. Object of tests is a special-purpose flexible container for transportation of bulk dangerous products МК-14-10 having the following characteristics:

Number of sling clamping elements	- 8 pcs

Container height	- 250 cm

Container diameter	- 240 cm

Conventional volume	- 13.0 m³

Safe working load	- 14.0 t

1.2. Kind of testing:

-  stacking

-  break

-  impact at free fall from the height of 0.8 m

-  tipping from the height of 0.8 m

-  lifting to vertical position.

1.3. Test performing is based on letter No.61 of May 21, 2009 from CJSC "Noviye Tekhnologii v Perevozkakh", Moscow, Maly Gnezdnikovsky pereulok, 12, bldg 4.

1.5. The object for testing was delivered on 25.05.2009.

1.6. Tests were performed within the period from 25.05.2009 till 26.05.2009.

# 2. Equipment and measuring means

# 2.1. Equipment:

- gravity drop crane test bench КСК-40

- a truck loader

- a loading frame.

# 2.2. Measuring means:

- an indicating spring dynamometer of ДПУ-50-2 type, GOST 9409

- a measure tape under GOST 7502-98, scale interval – 1 mm.

3. Documents

Tests were performed according to requirements of Part 6 of typical rules "Recommendations on the Transport of Dangerous Goods" (ST/SG/AC/10.1) and international standard ISO 21898 "Packing – Flexible Intermediate Bulk Containers (FIBC) for Safe Bulk Cargoes".

4. Testing procedure

Operations on container preparation for various kinds of tests as well as their performing are stated in Program No.016 – 017 of structural tests of special-purpose flexible container МК-14-10.

____________