# UN/SCETDG/35/INF.53

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Thirty-fifth session

Geneva, 22-26 June 2009

Item 2 of the provisional agenda

# EXPLOSIVE AND RELATED MATTERS

# Amendment to document ST/SG/AC.10/C.3/2009/10: Information required on the Dangerous Goods Transport document when transporting fireworks

Transmitted by the experts from Germany and the United Kingdom

1.	This proposal contains an amendment to the proposal in paragraph 10 of ST/SG/AC.10/C.3/2009/10. UN 0337 was unintentionally left out in the listing of the UN Nos requiring a certification about the proper classification. Furthermore, the information required on the transport document can be limited to the classification reference number itself, taking into account comments regarding the space on the transport document and the possible impact on the use of electronic documents with data fields.

The proposal should read as follows:

# 2	Amend 5.4.1.6 to include a new paragraph:

# "5.4.1.6.2 	When fireworks of UN Nos. 0333, 0334, 0335, 0336 and 0337 are transported, the transport document shall include a confirmation that the goods are properly classified.

As a confirmation a unique classification reference(s) number issued by the competent authority shall be included in the transport document. The classification reference number(s) shall contain a serial number, the name or sign of that competent authority and the competent authority’s state, indicated by the distinguishing sign for motor vehicles in international traffic.".

# 3	Renumber existing 5.4.1.6.2 as 5.4.1.6.3.

_____________