# UN/SCETDG/36/INF.51

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Thirty-sixth session

Geneva, 30 November – 9 December 2009

Item 3 of the provisional agenda

LISTING, CLASSIFICATION AND PACKING

Classification of nitroglycerin solution in alcohol

Consequential amendments by Belgium with respect to INF 10 by IATA

1.	Belgium agrees with the proposal set forth in INF 10 by IATA and proposes the following consequential amendments.

Proposal

2. 	Belgium proposes the addition of special provision YYY to be assigned against UN 3064 as follows:

| UN No. | Name and description | Class or division | Subsi-diary risk | UN packing group | Special provisions | Limited and excepted quantities | Packagings and IBCs | Portable tanks and bulk containers |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | Packing instructions | Special packing provisions | Instruc- tions | Special provisions |
| (1) | (2) | (3) | (4) | (5) | (6) | (7a) | (7b) | (8) | (9) | (10) | (11) |
|  | 3.1.2 | 2.0 | 2.0 | 2.0.1.3 | 3.3 | 3.4 | 3.5 | 4.1.4 | 4.1.4 | 4.2.5 /4.3.2 | 4.2.5 |
| 3064 | NITROGLYCERIN SOLUTION IN ALCOHOL with more than 1% but not more than 5% nitroglycerin | 3 |  | II | YYY | 0 | E0 | P300 |  |  |  |

YYY	Nitroglycerin solution in alcohol with more than 1% but not more than 5% nitroglycerin shall be classified in Class 1 and assigned to UN 0143 if not in compliance with all the requirements of packing instruction P300.

_______________