# UN/SCETDG/36/INF.56

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Thirty-sixth session

Geneva, 30 November – 9 December 2009

Item 5 of the provisional agenda

# MISCELLANEOUS PROPOSALS OF AMENDMENTS TO THE MODEL REGULATIONS ON THE TRANSPORT OF DANGEROUS GOODS

# Application of hazard label for environmentally hazardous substances

Transmitted by the United Kingdom

Introduction

1.	Following plenary discussions of the following papers on ST/SG/AC.10/C.3/2009/33 (IATA), INF. 25 (IATA), INF. 27 (Sweden) on the subject of the Application of hazard label for environmentally hazardous substances the chairman asked the UK to present their alternative text.

The following proposal reflects the UK text.

Proposal

2.	Insert the underlined text after mark in paragraph 5.2.1.6.1

5.2.1.6.1	Packages containing environmentally hazardous substances meeting the criteria of 2.9.3 (UN Nos. 3077 and 3082) shall be durably marked with the environmentally hazardous substance mark “in addition to the labelling requirements of 5.2.2.1.2” with the exception of single packagings and combination packagings containing inner packagings with:

# ______________