# UN/SCETDG/36/INF.59

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Thirty-sixth session

Geneva, 30 November – 9 December 2009

Item 5 of the provisional agenda

# MISCELLANEOUS PROPOSALS OF AMENDMENTS TO THE MODEL REGULATIONS ON THE TRANSPORT OF DANGEROUS GOODS

Application of hazard label for environmentally hazardous substances

Transmitted by the International Air Transport Association (IATA)

Introduction

1.	Following plenary discussion on some text to clarify that the applicable labelling requirements apply in addition to the application of the environmentally hazardous substances mark a revised proposal has been developed to reflect the preferred text.

Proposal

2. 	The Sub-Committee is invited to add the following note under the existing paragraph 5.2.1.6.3 as follows:

5.2.1.6.3 	The environmentally hazardous substance mark shall be as shown in Figure 5.2.2. For packagings, the dimensions shall be 100 mm × 100 mm, except in the case of packages of such dimensions that they can only bear smaller marks. For transport units (see 5.3.2.3.1), the minimum dimensions shall be 250 mm × 250 mm.

NOTE: 	The labelling provisions of 5.2.2 apply in addition to any requirement for packages to bear the environmentally hazardous substance mark.

_______________