| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2009/23 17 December 2008 Original: ENGLISH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

One-hundred-and-forty-seventh session

Geneva, 10 - 13 March 2009

Item 4.2.19 of the provisional agenda

1958 AGREEMENT

Consideration of draft amendments to existing Regulations

Proposal for Supplement 10 to the 01 series of amendments to Regulation No. 53

(Installation of lighting and light-signaling devices on L3 vehicles)

Submitted by the Working Party on Lighting and Light-Signalling (GRE) (/

The text reproduced below was adopted by GRE via e-mail consultation of GRE experts following the decision of WP.29 and AC.1 at their November 2008 sessions (ECE/TRANS/WP.29/1070, para. 65).  The proposal is based on a document without symbol distributed during WP.29 at its one-hundred-and-forty-sixth session (informal document No. WP.29-146-19).  It is submitted to WP.29 and AC.1 for consideration.

Insert new paragraphs 2.22. and 2.23., to read:

"2.22. 	"Gross vehicle mass" or "maximum mass" means the technically permissible maximum laden mass as declared by the manufacturer.

2.23. 	"Laden" means so loaded as to attain the gross vehicle mass as defined in paragraph 2.22."

Paragraphs 6.1.1.1. and 6.1.1.2., amend to read:

"6.1.1.1.	For motorcycles having a cylinder capacity ≤ 125 cm3

One or two of approved type according to:

(a)	Class B, C, D or E of Regulation No. 113;

(b)	Regulation No. 112;

(c)	Regulation No. 1;

(d)	Regulation No. 8;

(e)	Regulation No. 20;

(f)	Regulation No. 57;

(g)	Regulation No. 72;

(h)	Regulation No. 98.

6.1.1.2.	For motorcycles having a cylinder capacity > 125 cm3

One or two of approved type according to:

(a)	Class B, D or E of Regulation No. 113;

(b)	Regulation No. 112;

(c)	Regulation No. 1;

(d)	Regulation No. 8;

(e)	Regulation No. 20;

(f)	Regulation No. 72;

(g)	Regulation No. 98.

Two of approved type according to:

(h)	Class C of Regulation No. 113."

Paragraphs 6.2.1.1. and 6.2.1.2., amend to read:

"6.2.1.1.	For motorcycles having a cylinder capacity ≤ 125 cm3

One or two of approved type according to:

(a)	Class B, C, D or E of Regulation No. 113;

(b)	Regulation No. 112;

(c)	Regulation No. 1;

(d)	Regulation No. 8;

(e)	Regulation No. 20;

(f)	Regulation No. 57;

(g)	Regulation No. 72;

(h)	Regulation No. 98.

6.2.1.2.	For motorcycles having a cylinder capacity > 125 cm3

One or two of approved type according to:

(a)	Class B, D or E of Regulation No. 113;

(b)	Regulation No. 112;

(c)	Regulation No. 1;

(d)	Regulation No. 8;

(e)	Regulation No. 20;

(f)	Regulation No. 72;

(g)	Regulation No. 98.

Two of approved type according to:

(h)	Class C of draft Regulation No. 113."

Insert new paragraphs 6.2.5.3. and 6.2.5.4., to read (including a reference to new footnote 4/ and the insertion of a new footnote 4/):

"6.2.5.3.	For passing beam headlamps with a light source having an objective luminous flux which exceeds 2,000 lumen, the vertical inclination of the passing beam headlamp shall remain between -0.5 and -2.5 per cent. A headlamp levelling device may be used to satisfy the requirements of this paragraph but its operation shall be automatic. 4/

6.2.5.4.	The requirement in paragraph 6.2.5.3. shall be tested on the vehicle in the following conditions:

Condition A (rider alone):

A mass of 75 kg ± 1 kg, simulating the rider, shall be placed on the vehicle in such a way as to reproduce the axle loads declared by the manufacturer for this loading condition.

The vertical inclination (initial aiming) of the passing beam headlamp shall be set, following the manufacturer’s instructions, between -1.0 and -1.5 per cent.

Condition B (fully laden motorcycle):

masses, simulating the manufacturer's maximum total mass, shall be placed on the vehicle in such a way as to reproduce the axle loads declared by the manufacturer for this loading condition.

Before making the measurements, the vehicle shall be rocked 3 times up and down and then moved backwards and forwards for at least a complete wheel revolution."

________________

4/ 	However, until 60 months after the date of entry into force of supplement 10 to the 01 series of amendments this operation may be manual without the use of tools. In such case the manufacturer shall provide in the vehicle owners' manual instruction regarding such manual headlamp levelling."

Paragraph 6.2.7., amend to read:

"6.2.7.	Electrical connections

The control for changing over to the passing beam(s) shall switch off the driving beam(s) simultaneously.

Passing beam headlamps with a light source approved in accordance with Regulation No. 99 shall remain switched on when the driving-beam is illuminated."

Paragraphs 11.1. to 11.3., amend to read:

"11.1.	As from the official date of entry into force of Supplement 10 to the 01 series of amendments, no Contracting Party applying this Regulation shall refuse to grant approvals under this Regulation as amended by Supplement 10 to the 01 series of amendments.

11.2.	As from 60 months after the date of entry into force mentioned in paragraph 11.1. above, Contracting Parties applying this Regulation shall grant approvals only if the vehicle type with regard to the number and mode of installation of the lighting and light-signalling devices corresponds to the requirements of the Supplement 10 to the 01 series of amendments to this Regulation.

11.3.	Existing approvals granted under this Regulation before the date mentioned in paragraph 11.2. above shall remain valid.  In the case of vehicles first registered more than 84 months after the date of entry into force mentioned in paragraph 11.1. above Contracting Parties applying this Regulation may refuse the vehicle type with regard to the number and mode of installation of the lighting and light-signalling devices which do not meet the requirements of the Supplement 10 to the 01 series of amendments to this Regulation."

Annex 1, Communication form,

Insert new items 11. to 11.2., to read (including the reference to footnote 3/ and footnote 3/):

"11. 	Masses as declared by the manufacturer (3/)

11.1. 	mass in running order:

Total mass: 	kg

Mass on the front wheel: 		kg

Mass on the rear wheel: 	kg

11.2.	Gross vehicle mass:

Total mass:	kg

Mass on the front wheel: 	kg

Mass on the rear wheel: 	kg

____________________

3/ 	These sections only need to be completed if the test according to paragraph 6.2.5.4. is performed."

Items 11. to 17. (former), renumber as items 12. to 18.

- - - - -

# Footnotes

(/ In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.