| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2009/69 9 April 2009 ENGLISH Original: ENGLISH AND FRENCH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

One-hundred-and-forty-eighth session

Geneva, 23 - 26 June 2009

Item 4.2.22 of the provisional agenda

1958 AGREEMENT

Consideration of draft amendments to existing Regulations

Proposal for Supplement 3 to Regulation No. 108

(Retreated pneumatic tyres for motor vehicles)

Submitted by the Working Party on Brakes and Running Gear (/

The text reproduced below was adopted by the Working Party on Brakes and Running Gear (GRRF) at its sixty-fifth session.  It is based on ECE/TRANS/WP.29/2008/4, as reproduced in Annex II of the report.  It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration (ECE/TRANS/WP.29/GRRF/65, para. 50).

Paragraph 1., amend to read (including the addition of footnote **/):

"1.	SCOPE

This Regulation covers the production of retreaded tyres designed primarily for vehicles of category M1, N1, O1 and O2. */ **/.  However, it does not apply to the production of:

1.1.	Retreaded tyres with a speed capability below 120 km/h or above 300 km/h;

1.2.	Tyres originally produced without speed symbols and load indices;

1.3.	Tyres originally produced without type approval and without either an "E" or "e" mark;

1.4.	Tyres designed for the equipment of cars produced prior to 1939;

1.5.	Tyres designed exclusively for competition or off road use and marked accordingly;

1.6.	Tyres designated as "T type" temporary use spares.

_______________

*/	As defined in Annex 7 to the Consolidated Resolution on the Construction of Vehicles R.E.3 (document TRANS/WP.29/78/Rev.1 as last amended by Amend. 4).

**/	This Regulation defines requirements for tyres as a component.  It does not limit their installation on any categories of vehicles."

- - - - -

# Footnotes

(/ In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.