| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2009/76 9 April 2009 Original: ENGLISH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

One-hundred-and-forty-eighth session

Geneva, 23 - 26 June 2009

Item 4.2.24 of the provisional agenda

1958 AGREEMENT

Consideration of draft amendments to existing Regulations

Proposal for the 01 series of amendments to Regulation No. 101

(CO2 emissions/fuel consumption)

Submitted by the Working Party on Pollution and Energy (/

The text reproduced below was prepared by the expert from the European Commission to align the requirements of the Regulation with those of European Union Directives 715/2007/EC and 692/2008/EC.  The Working Party on Pollution and Energy (GRPE) had agreed, at its fifty-seventh session, to submit this proposal for consideration to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1), subject to a final review by GRPE at its June 2009 session (ECE/TRANS/WP.29/GRPE/57, para. 39).

Paragraph 5.2.4., amend to read (and keeping footnote 3/ unchanged):

"5.2.4.	For the purpose of the calculation mentioned in paragraph 5.2.3., the fuel consumption shall be expressed in appropriate units and the following fuel characteristics shall be used:

(a)	density: measured on the test fuel according to ISO 3675 or an equivalent method. For petrol, diesel, biodiesel and ethanol (E85) the density measured at 15 ºC will be used; for LPG and natural gas/biomethane a reference density will be used, as follows:

0.538 kg/litre for LPG

0.654 kg/m3 for NG 3/

(b)	hydrogen-carbon ratio:  fixed values will be used which are:

C1H1,89O0,016 for petrol,

C1H1,86O0,005 for diesel,

C1H2,525 for LPG (liquefied petroleum gas),

CH4 for NG (natural gas) and biomethane,

C1H2,74O0,385 for ethanol (E85)."

Paragraph 9.3.1.1.2.4., amend to read:

"9.3.1.1.2.4.	The reference fuels described in Annexes 10 and 10a of Regulation No. 83 shall be used for this test."

Annex 6

Paragraph 1.3.5., amend to read:

"1.3.5.	The tyres shall be of a type specified as original equipment by the vehicle manufacturer inflated to the pressure recommended for the test load and speeds.  The pressures shall be indicated in the test report.

The choice of tyres shall be based on the rolling resistance.  The tyres with the highest rolling resistance shall be chosen, measured according to ISO 28580.

If there are more than three tyre rolling resistances, the tyre with the second highest rolling resistance shall be chosen.

The rolling resistance characteristics of the tyres fitted to production vehicles shall reflect those of the tyres used for type-approval."

Paragraph 1.4.3., amend to read:

"1.4.3.	The fuel consumption, expressed in litres per 100 km (in the case of petrol, LPG, ethanol (E85) and diesel) or in m3 per 100 km (in the case of NG/biomethane) is calculated by means of the following formulae:

(a)	for vehicles with a positive ignition engine fuelled with petrol (E5):

FC = (0.118/D) ∙ [(0.848 ∙ HC) + (0.429 ∙ CO) + (0.273 ∙ CO2)]

(b)	for vehicles with a positive ignition engine fuelled with LPG:

FCnorm = (0.1212 / 0.538) · [(0.825 · HC) + (0.429 · CO) + (0.273 · CO2)]

If the composition of the fuel used for the test differs from the composition that is assumed for the calculation of the normalized consumption, on the manufacturer's request a correction factor cf may be applied, as follows:

FCnorm = (0.1212 / 0.538) · (cf) · [(0.825 · HC) + (0.429 · CO) + (0.273 · CO2)]

The correction factor cf, which may be applied, is determined as follows:

cf = 0.825 + 0.0693 · nactual

where:

nactual = the actual H/C ratio of the fuel used

(c)	for vehicles with a positive ignition engine fuelled with NG/biomethane:

Fcnorm = (0.1336 / 0.654) · [(0.749 · HC) + (0.429 · CO) + (0.273 · CO2)]

(d)	for vehicles with a compression ignition engine fuelled with diesel (B5):

FC = (0.116/D) ∙ [(0.861 ∙ HC) + (0.429 ∙ CO) + (0.273 ∙ CO2)]

(e)	for vehicles with a positive ignition engine fuelled with ethanol (E85):

FC = (0.1742/D) ∙ [(0.574 ∙ HC) + (0.429 ∙ CO) + (0.273 ∙ CO2)]

In these formulae:

FC	=	the fuel consumption in litre per 100 km (in the case of petrol, LPG, diesel or biodiesel) or in m3 per 100 km (in the case of natural gas)

HC	=	the measured emission of hydrocarbons in g/km

CO	=	the measured emission of carbon monoxide in g/km

CO2	=	the measured emission of carbon dioxide in g/km

D	=	the density of the test fuel.

In the case of gaseous fuels this is the density at 15 °C."

- - - - -

# Footnotes

(/ In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.