REGULATION No. 48

(Installation of lighting and light-signalling devices)

Clarifications on installation requirements

Proposal for draft Supplement 5 to the 03 series of amendments to Regulation No. 48

Submitted by the expert from Germany (/

A.	PROPOSAL

6.21. 		CONSPICUITY MARKINGS

6.21.1. 	Presence

6.21.1.1. 	Prohibited: on vehicles of categories M 1 and O 1 .

6.21.1.2. 	Mandatory:

6.21.1.2.1. 	to the rear:

full contour marking on vehicles exceeding  2, 100  mm in width of the following categories:

- N 2  with a maximum mass exceeding  7. 5  tonnes and N 3 (with the exception of chassis-cabs, incomplete vehicles and tractors for semi-trailers)

- O 3 and O 4 (with the exception of incomplete vehicles)

6.21.1.2.2.	to the side:

6.21.1.2.2.1.	partial contour marking on vehicles exceeding 6,000 mm in length (including the drawbar for trailers) of the following categories:

(a)	N2 with a maximum mass exceeding 7.5 tonnes and N3 (with the exception of chassis-cabs incomplete vehicles and tractors for semi-trailers)

(b)	O3 and O4. (with the exception of incomplete vehicles)"

Paragraph 6.21.1.2.3., amend to read:

"6.21.1.2.3.	A line marking may be installed instead of the mandatory contour marking if the shape, structure, design or operational requirements of the vehicle make it impossible to install the mandatory contour marking.

Insert new paragraph 6.21.1.2.4. to read:

6.21.1.2.4.	 “If the exterior surfaces of the bodywork are partially constituted of flexible material, this line marking shall be installed on (a) rigid part(s) of the vehicle. The remaining portion of conspicuity markings may be fitted on the flexible material. However, if the exterior surfaces of the bodywork are fully constituted of flexible material, requirements of paragraph 6.21. shall be met."

Insert new paragraphs 6.21.1.2.5. , to read:

“6.21.1.2.5.	In cases where the manufacturer, after verification by the Technical Service, can prove to the satisfaction of the authority responsible for type approval that it is impossible, due to the operational requirements which may require special shape, structure or design of the vehicle, to comply with the requirements contained in paragraphs 6.21.2. to 6.21.7.5., then partial fulfilment of some of these requirements is acceptable. This is conditional upon a portion of the requirements being met where possible, and the application of conspicuity markings that partially meet requirements maximised on the vehicle structure. This may include fitting of additional brackets or plates containing material compliant with Regulation 104 where structure is available to ensure clear and uniform signalling compatible with the objective of conspicuity.

Where partial fulfillment is deemed acceptable, retro-reflective devices like retro-reflectors of class IV of Regulation No. 3 or brackets containing retro-reflecting material compliant with photometric requirements of Class C of Regulation 104 may substitute part of the required conspicuity markings.

In this case, at least one of these retroreflective devices shall be installed per 1500 mm

The necessary information shall be indicated in the communication form.”

______________

6.21.1.3. 	Optional:

6.21.1.3.1. 	on all other categories of vehicles, not otherwise specified in paragraphs  6. 21. 1. 1. and  6. 21. 1. 2. above, including the cab of tractor units for semi-trailers and the cab of chassis-cabs.

6.21.1.3.2.	partial or full contour marking may be applied instead of mandatory line markings, and full contour marking may be applied instead of mandatory partial contour marking.

6.21.2.	 Number

According to the presence.

Paragraph 6.21.3., amend to read:

"6.21.3.	Arrangement

The conspicuity markings shall be as close as practicable to horizontal and vertical, compatible with the shape, structure, design and operational requirements of the vehicle; if this is not possible, the full or partial contour markings, when fitted, shall follow as close as practicable the contour of the outer shape of the vehicle.

Furthermore, the conspicuity markings shall be spaced as evenly as possible over the horizontal dimensions of the vehicle such that the total length and/or width of the vehicle can be identified."

6.21.4. 	Position

6.21.4.1. 	Width

6.21.4.1.1. 	The conspicuity marking shall be as close as practicable to the edge of the vehicle.

6.21.4.1.2. 	The cumulative horizontal length of the conspicuity marking elements, as mounted on the vehicle, shall equate to at least  80  per  cent of the overall width of the vehicle, excluding any horizontal overlap of individual elements.

6.21.4.2. 	Length

6.21.4.2.1. 	The conspicuity marking shall be as close as practicable to the ends of the vehicle and reach to within  600  mm of each end of the vehicle (or cab in the

case of tractor units for semi-trailers).

6.21.4.2.1.1. 	for motor vehicles, each end of the vehicle, or in the case of tractors for semi-trailers the each end of the cab;

6.21.4.2.1.2.	for trailers, each end of the vehicle (excluding the drawbar).

6.21.4.2.2. 	The cumulative horizontal length of the conspicuity marking elements, as mounted on the vehicle, excluding any horizontal overlap of individual elements, shall equate to at least  80  per  cent of:

6.21.4.2.2.1. 	for motor vehicles, the length of the vehicle excluding the cab, or in the case of tractors for semi-trailers, if fitted, the length of the cab;

6.21.4.2.2.2. 	for trailers, the length of the vehicle (excluding the drawbar).

6.21.4.3. 	Height

Paragraph 6.21.4.3.1. to 6.21.4.3.2., amend to read:

"6.21.4.3.1.	Line markings and contour markings lower element(s)

As low as practicable within the range:

Minimum:		not less than 250 mm above the ground.

Maximum:		not more than 1,500 mm above the ground.

However, a maximum mounting height of 2,500 mm may be accepted where the shape, structure, design or operational conditions of the vehicle prevent compliance with the maximum value of 1,500 mm or, if necessary, to fulfil the requirements of paragraphs 6.21.4.1.2., 6.21.4.1.3., 6.21.4.2.2. and 6.21.4.2.3., or the horizontal positioning of the line marking or the lower element(s) of the contour marking.

The necessary justification for installation of conspicuity material higher than 1500 mm shall be indicated in the communication form."

6.21.4.3.2.	Contour markings upper element(s)

As high as practicable, but within 400 mm of the upper extremity of the vehicle."

Paragraphs 6.21.5. to 6.21.5.2.2., amend to read:

"6.21.5.	Visibility

The conspicuity marking shall be considered visible, if at least 80 per cent of the illuminating surface of the installed marking is visible when viewed by an observer positioned at any point within the observation planes defined below.

6.21.5.1.	for rear conspicuity markings (see Annex 11, Figure 1) the observation plane is perpendicular to the longitudinal axis of the vehicle situated  25 m from the extreme end of the vehicle and bounded by:

6.21.5.1.1.	in height, by two horizontal planes 1 m and 3.0 m respectively above the ground,

6.21.5.1.2.	in width, by two vertical planes which form an angle of 4° outwards from the vehicle's median longitudinal plane and which pass through the intersection of the vertical planes parallel to the vehicle's median longitudinal plane delimiting the vehicle's overall width, and the plane perpendicular to the longitudinal axis of the vehicle that delimits the end of the vehicle.

6.21.5.2.	for side conspicuity markings (see Annex 11, figure 2) the observation plane is parallel to the longitudinal median plane of the vehicles situated 25 m   from the extreme outer edge of the vehicle and bounded by:

6.21.5.2.1.	in height, by two horizontal planes 1.0 m and 1.5 m respectively above the ground,

6.21.5.2.2.	in width, by two vertical planes which form an angle of 4° outwards from a plane perpendicular to the vehicle's longitudinal axis and which pass through the intersection of the vertical planes perpendicular to the vehicle's longitudinal axis delimiting the vehicle's overall length and the extreme outer edge of the vehicle."

6.21.6. 	Orientation

Paragraphs 6.21.6.1. to 6.21.6.2., amend to read:

"6.21.6.1.	To the side:

As close as practicable to being parallel to the median longitudinal plane of the vehicle, compatible with the shape, structure, design and operation requirements of the vehicle; if this is not possible, it shall follow as close as practicable the contour of the outer shape of the vehicle.

6.21.6.2.	To the rear:

As close as practicable to being parallel to the transverse plane of the vehicle, compatible with the shape, structure, design and operation requirements of the vehicle, if this is not possible, it shall follow as close as practicable the contour of the outer shape of the vehicle."

"6.21.7.1. 	Conspicuity markings shall be considered continuous if the distance between adjacent elements are as small as possible and do not exceed 50 per cent of the shortest adjacent element length. However, if the manufacturer can prove to the satisfaction of the authority responsible for type approval that it is impossible to respect the value of 50 per cent, the distance between adjacent elements may be larger than 50 per cent of the shortest adjacent element, and it shall be as small as possible and not exceed 1000 mm."

6.21.7. 	Other requirements

6.21.7.1. 	Conspicuity markings shall be considered continuous if the distance between adjacent elements are as small as possible and do not exceed  50  per cent of

the shortest adjacent element length.

Paragraph 6.21.7.2., amend to read:

"6.21.7.2.	In the case of a partial contour marking, each upper corner shall be described by two lines at 90°, to each other and each at least 250 mm in length; if this is not possible, the marking shall follow as close as practicable the contour of the outer shape of the vehicle."

6.21.7.3. 	The distance between the conspicuity marking fitted to the rear of a vehicle and each mandatory stop lamp should be greater than  200  mm.

6.21.7.4. 	Where rear marking plates conforming to the 01 series of amendments to

Regulation No. 70 are installed these may be considered, at the discretion of the

manufacturer, as part of the conspicuity marking to the rear, for the purposes of

calculating the length of the conspicuity marking and its proximity to the side of

the vehicle.

6.21.7.5. 	The locations on the vehicle designated for conspicuity markings shall allow for

the installation of markings of at least 60 mm in width.

Annex 1,

Insert a new paragraph 9.24.4., to read:

"9.24.4. Exemption  regarding conspicuity marking	Rear yes/no 2/

according to paragraph 6.21.1.2.5. 	Comments:

Side yes/no 2/

Insert a new paragraph 10.7., to read:

Comments: 	"

"10.7.		Comments regarding conspicuity marking (according to paragraphs  6.21.1.2.5., and 6.21.4.3.1. of this Regulation)………………………..."

Insert a new paragraph 10.8., to read:

"10.8.		Comments regarding conspicuity marking (Incomplete vehicle or Complete Vehicles according to paragraphs 6.21.1.2.1. and 6.21.1.2.1.1.:

Incomplete vehicles: 	yes/no

Complete vehicles:	yes/no

Completed vehicles:	yes/no"

Annex 11, amend to read:

Annex 11

VISIBILITY OF CONSPICUITY MARKINGS TO THE REAR AND

SIDE OF A VEHICLE

(see paragraph 6.21.5. of this Regulation)

Figure 2

B.	JUSTIFICATION

Background

The provisions concerning conspicuity markings, including:

(a)	Definitions in paragraph 2.7.17.

(b)	New paragraph 6.21., and

(c)	Transitional provisions

were introduced into Regulation No. 48 by the 03 series of amendments which entered into  force on 10 October 2006.  They are applicable to:

(a)	new vehicle type approval from 10 October 2007, and

(b)	as an option by Contracting Parties, to national/regional vehicle type approval from 10 October 2009.

Existing approvals cease to be valid on 10 October 2011.

At present, vehicles for which conspicuity marking is mandatory, either as full contour marking or partial contour marking, are, as a rule, first registered in the territory of Contracting Parties on the basis of national type approval. Mandatory compliance with Regulation No. 48 provisions regarding conspicuity marking is not required for the time being.

The directives of the European Community (EC) regarding Whole Vehicle Type Approval (WVTA) in their most recent version are intended to extend the application of the relevant technical requirements (including those on lighting and light-signalling in Regulation No. 48) to:

(a) 	all categories of vehicles, and also

(b)	to single vehicle approval.

As from 10 July 2011, EU Member States will issue certificates of conformity for new vehicles regarding lighting installation only if the vehicle complies with Regulation No. 48 requirements. In addition, such requirements may also be introduced by other Contracting Parties.

Motor vehicles and trailers for the transport of goods are normally built with closed bodywork which permits the installation of conspicuity markings without problems. However, the increasing diversification of the road transport market requires more and more vehicles whose bodywork is designed to cover dedicated transport purposes. A few examples are:

(a)	Tanker vehicles

(b)	Vehicles/chassis for container transport

(c)	Vehicles with flexible bodywork (curtain-sider)

(d)	Vehicles for the transport of concrete

(e)	Vehicles for special loads, such as timber, cables, etc.

(f)	Large capacity tipper vehicles

(g)	Vehicles for the transport of substances with high temperature, e.g. bitumen

(h)	Low bed trailers

In such cases, it is often not possible to install conspicuity markings to the full extent of the requirements or in such a way that their performance is maintained during normal vehicle operation. Examples of typical constructions are given in the Annex below.

In order to ensure consistent application of the Regulation, it is considered necessary to amend the provisions of paragraph 6.21. in such a way that they cover as many special vehicle configurations as possible, taking into account the objectives of traffic safety and the practical constraints of vehicle design.

The proposal is intended to find:

(a)	a long-term solution;

(b)	a description of the exceptions which are clearly readable and resulting in uniform use (interpretations) of the specifications

(c)	a hierarchic process given by a stepwise description of the decision procedure to be followed by the authorities. In any case the results must be recorded in the communication form.

- - - - -

# Footnotes

(/  In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.

# Text boxes

25 m

25 m

observation plane

Observation plane plane plane

### Figure 1

Observation plane

4°

4°

4°

4°