UN/SCETDG/37/INF.59

Committee of Experts on the Transport of Dangerous Goods and on the Globally Harmonized System of Classification and Labelling of Chemicals Sub-Committee of Experts on the Transport of Dangerous Goods 18 June 2010 Thirty-seventh session Geneva, 21–30 June 2010 Item 3 of the provisional agenda Listing, classification and packing

Special provision 272

Transmitted by the Expert from Germany

1	SP 272 states that “This substance shall not be transported under the provisions of class 4.1 unless specially authorized by the competent authority (see UN 0143).” SP 272 is assigned to:

UN 3319 NITROGLYCERIN MIXTURE, DESENZITIZED, SOLID, N.O.S with more than 2% but not more than 10 % nitroglycerin, by mass; and

UN 3344 PENTAERYTHRITE TETRANITRATE (PENTAERYTHRITOL TETRANITRATE; PETN) MIXTURE, DESENSZITED, SOLID, N.O.S. with more than 10% but not more than 20 % PETN, by mass.

2	The reference to UN 0143 does not apply to UN 3344. The corresponding entry for UN 3344 would be UN 0150.

Thus, there are two options for a possible correction of SP 272:

Either a reference to UN 0150 should be included, or

The reference to UN 0143 should be deleted.

3	The first option seems preferable to avoid further amendments. Germany is willing to prepare a formal proposal for the next meeting, taking into consideration the preference of the Experts of the Sub-Committee.