UN/SCETDG/37/INF.67

Committee of Experts on the Transport of Dangerous Goods and on the Globally Harmonized System of Classification and Labelling of Chemicals Sub-Committee of Experts on the Transport of Dangerous Goods 23 June 2010 Thirty-seventh session Geneva, 21–30 June 2010 Item 5 of the provisional agenda Miscellaneous proposals of amendments to the Model Regulations on the Transport of Dangerous Goods

Aerosols (UN 1950) – Maximum volume of the liquid phase at 50°C

Transmitted by the expert from the European Aerosol Federation (FEA)

Introduction

1.	The latest modification of the Aerosol Dispensers Directive 75/324/EEC (Directive 2008/47/EC – Annex § 2.4) includes a more stringent requirement for the maximum volume of the liquid phase at 50°C which must not exceed 90% of the net capacity of the aerosol container, instead of 95% in the previous version.

2.	FEA proposes to update the existing requirements in 6.2.4.2.1.1 and 6.2.4.2.2.2.

3.	The Sub-Committee is invited to discuss the proposed amendments. If the Sub-Committee agrees to the proposal, FEA is willing to submit a working document for the December session.

Proposal

4.	Amend the first sentence of existing 6.2.4.2.1.1 to read (new text in bold underline):

The temperature of the water bath and the duration of the test shall be such that the internal pressure reaches that which would be reached at 55°C (50°C if the liquid phase does not exceed 90% of the capacity of the aerosol dispenser at 50°C).

25	Amend the first sentence of existing 6.2.4.2.2.2 to read (new text in bold underline):

The temperature of the water bath and the duration of the test shall be such that the internal pressure reaches that which would be reached at 55°C (50°C if the liquid phase does not exceed 90% of the capacity of the aerosol dispenser at 50°C).