| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2010/9/Corr.1 15 January 2010 ENGLISH ONLY |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

One-hundred-and-fiftieth session

Geneva, 9-12 March 2010

Item 4.2.5 of the provisional agenda

1958 AGREEMENT

Consideration of draft amendments to existing Regulations

Proposal for Supplement 17 to the 02 series of amendments to Regulation No. 7

(Front and rear position side lamps)

Submitted by the Working Party on Lighting and Light-Signalling (/

Corrigendum

Page 5, the table

Replace the existing table by the following one

|  | Minimum luminous intensity in cd | Maximum luminous intensity in cd when used as |
| --- | --- | --- |
|  |  | Single lamp | Lamp (single) marked "D" paragraph (4.2.2.6.) |
| 6.1.1. Front position lamps, front end-outline marker lamp A or AM | 4 | 140 | 70 |
| 6.1.2. Front position lamps incorporated in a headlamp | 4 | 140 | - |
| 6.1.3. Rear position lamps, rear end-outline marker lamp 6.1.3.1. R, R1 or RM1 (steady) | 4 | 17 | 8.5 |
| 6.1.3.1. R2 or RM2 (variable) | 4 | 42 | 21 |
| 6.1.4. Stop-lamps 6.1.4.1. S1 (steady) | 60 | 260 | 130 |
| 6.1.4.2. S2 (variable) | 60 | 730 | 365 |
| 6.1.4.3. S3 (steady) | 25 | 110 | 55 |
| 6.1.4.4. S4 (variable) | 25 | 160 | 80 |

- - - - -

# Footnotes

(/ In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.