| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2010/51 22 December 2009 Original: ENGLISH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

One-hundred-and-fiftieth session

Geneva, 9-12 March 2010

Item 4.2.46 of the provisional agenda

1958 AGREEMENT

Consideration of draft amendments to existing Regulations

Proposal for Corrigendum 1 to Supplement 2 to the 05 series of amendments to Regulation No. 49 (Emissions of C.I. and P.I. (LPG and NG) engines)

Submitted by the secretary of the informal group

Worldwide harmonized Heavy Duty Certification (WHDC) (/

The text reproduced below was prepared to modify paragraphs 7.6.3. (hot soak period) and 8.6.3. (calculation of specific emissions) for solving the options on hot soak period and cold start weighting factor in amendment 1 to gtr No. 4 (document ECE/TRANS/WP.29/2009/121).  Other modifications are clarifications to the text and corrections of errors in document ECE/TRANS/WP.29/2009/114, and are aligned with the modifications proposed in document ECE/TRANS/WP.29/2010/48 for amendment 2 to gtr No. 4. The modifications to the text of ECE/TRANS/WP.29/2009/114 are marked in bold characters or strikethrough.  The World Forum agreed to prepare the corresponding document to be submitted to a vote either at the March or  the June 2010 session of WP.29, after consideration by the Working Party on Pollution and Energy (GRPE) at its January 2010 session.

Annex 4B,

Paragraph 3.2., insert new symbols and correct the following symbols, to read:

| "Symbol | Unit | Term |
| --- | --- | --- |
| a1 | - | Slope of the regression |
| a0 | - | y intercept of the regression |
| cgas | ppm/Vol per cent | Concentration on the gaseous components |
| er ep | g/kWh | Specific emission during regeneration |
| kr | - | Regeneration factor |
| kr,u | - | Upward regeneration adjustment factor |
| kr,d | - | Downward regeneration adjustment factor |
| mb mf,d | mg | Particulate sample mass of the dilution air collected |
| mf | mg | Particulate sampling filter mass |
| mp mf | mg | Particulate sample mass collected |
| Md | g/mol | Molar mass of the dilution air |
| Mf | Nm | Torque absorbed by auxiliaries/equipment to be fitted |
| Mr | Nm | Torque absorbed by auxiliaries/equipment to be removed |
| nr | - | Number of measurements with during regeneration |
| Pf | kW | Power absorbed by auxiliaries/equipment to be fitted |
| Pr | kW | Power absorbed by auxiliaries/equipment to be removed |
| r2 | - | Coefficient of determination |
| s |  | Standard deviation |
| u | - | Ratio between the densities (or molar masses) of the gas components and the exhaust gas divided by 1000" |

Paragraph 6.3.5., amend to read:

"6.3.5.	Engine cycle work

The calculation of reference and actual cycle work (see paragraphs 7.4.8. and 7.8.6.) shall be based upon engine power according to paragraph 6.3.1.  In this case, Pf Pa and Pr Pb of equation 4 are zero, and P equals Pm.

If auxiliaries/equipment are installed according to paragraphs 6.3.2. and/or 6.3.3., the power absorbed by them shall be used to correct each instantaneous cycle power value Pm,i, as follows:

(4)

where:

Pm,i	is the measured engine power, kW

Pf,i	is the power absorbed by auxiliaries/equipment to be fitted, kW

Pr,i	is the power absorbed by auxiliaries/equipment to be removed, kW"

Paragraph 6.6.2., amend to read:

"6.6.2.	Periodic regeneration

…

With reference to the specific emission calculations in paragraph 8.6.3., the regeneration adjustment factors shall be applied, as follows:

(e)	for a test without regeneration, kr,u shall be multiplied with or be added to, respectively, the specific emission e in equations 69, 70a or 70b,

(f)	for a test with regeneration, kr,d shall be multiplied with or be added to be subtracted from, respectively, the specific emission e in equations 69 70a or 70b.

At the request of the manufacturer …"

Paragraph 7.3., the flowchart, the last box, amend the line "Data collection and evaluation" to read:

"Data collection and evaluation				paragraph 7.6.6./7.7.4."

Paragraph 7.4.7., amend to read:

"7.4.7.	Denormalization of engine torque

… shall be denormalized, using the mapping curve determined according to paragraph 7.4.3., as follows:

(10)

where:

Mnorm,i	is the normalized torque, per cent

Mmax,i	is the maximum torque from the mapping curve, Nm

Mf,i	is the torque absorbed by auxiliaries/equipment to be fitted, Nm

Mr,i	is the torque absorbed by auxiliaries/equipment to be removed, Nm

If auxiliaries/equipment are fitted in accordance with paragraph 6.3.1. and Annex 7, Mf Ma and Mr Mb are zero.

…"

Paragraph 7.6.3., amend to read:

"7.6.3.	Hot soak period

Immediately upon completion of the cold start test, the engine shall be conditioned for the hot start test using a 10 ± 1 minutes hot soak period soaked for 5 ( 1 minutes."

Paragraph 7.8.4., amend to read:

"7.8.4.	Drift verification

…

The following provisions apply for analyzer drift:

(a)	The pre-test zero and span and post-test zero and span responses may be directly inserted into equation 66 applied to the drift calculation provisions of paragraph 8.6.1. without determining the drift;

(b)	If the drift difference between the pre-test and post-test results is less than 1 per cent of full scale, the measured concentrations may be used uncorrected or may be corrected for drift according to paragraph 8.6.1.;

(c)	If the drift difference between the pre-test and post-test results is equal to or greater than 1 per cent of full scale, the test shall be voided or the measured concentrations shall be corrected for drift according to paragraph 8.6.1."

Paragraph 7.8.7., amend to read:

"7.8.7.	Validation statistics of the test cycle

Linear regressions of the actual values (nact, Mact, Pact) on the reference values (nref, Mref, Pref) shall be performed for speed, torque and power for both the WHTC and the WHSC.

To minimize the biasing effect of the time lag between the actual and reference cycle values, the entire engine speed and torque actual signal sequence may be advanced or delayed in time with respect to the reference speed and torque sequence.  If the actual signals are shifted, both speed and torque shall be shifted by the same amount in the same direction.

The method of least squares shall be used, with the best-fit equation having the form:

y  =  a1x + a0	(11)

where:

y 		is the actual value of speed (min-1), torque (Nm), or power (kW)

a1		is the slope of the regression line

x		is the reference value of speed (min-1), torque (Nm), or power (kW)

a0		is the y intercept of the regression line

The standard error …"

Paragraph 8.4.2.3., amend to read:

"…

where:

ugas 		is the ratio between density of respective value of the exhaust component and density of exhaust gas from table 5

…"

Paragraph 8.4.2.4., amend to read:

"…

where:

ugas 		is calculated from equation 38 or 39 the instantaneous density ratio of exhaust component and exhaust gas

…"

Paragraph 8.5.2.3.1., amend to read:

"…

where:

ugas 		is the ratio between density of respective value of the exhaust component and density of exhaust gas from table 6

…"

Paragraph 8.6.3., amend to read:

"8.6.3.	Calculation of the specific emissions

The specific emissions egas or ePM (g/kWh) shall be calculated for each individual component in the following ways depending on the type of test cycle.

For the WHSC, hot WHTC, or cold WHTC, the following equation formula shall be applied:

(69)

where:

m	is the mass emission of the component, g/test

Wact	is the actual cycle work as determined according to paragraph 7.8.6., kWh

For the WHTC, the final test result shall be a weighted average from cold start test and hot start test according to the following equation by using either of the following options:

(70)

(70b)

The option shall be selected by the Contracting Parties.

where:

mcold		is the mass emission of the component on the cold start test, g/test

mhot		is the mass emission of the component on the hot start test, g/test

Wact,cold	is the actual cycle work on the cold start test, kWh

Wact,hot	is the actual cycle work on the hot start test, kWh

If periodic regeneration in accordance with paragraph 6.6.2 applies, the regeneration adjustment factors kr,u or kr,d shall be multiplied with or be added to, respectively, the specific emissions result e as determined in equations 69 and 70."

Paragraphs 3.1.10., 3.1.20., 3.2., 7.5.6., 7.6.6., 7.7.4, 8.1.2., 8.1.3., 8.4.3.1., 8.4.3.2.2., 8.5.2.3.1., 8.5.2.3.2., 8.5.2.3.3., 8.5.3.1., 9.2. table 7, 9.3.11., 9.4.6.3., A.3.1.3., A.3.2.1., A.3.2.2., A.3.2.3., A.3.2.4., A.3.2.5., replace: dilution air by diluent.

- - - - -

# Footnotes

(/ In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.