Regulation No. 117 (Tyre rolling noise and wet grip adhesion)

Proposal for amendments to ECE/TRANS/WP.29/2010/63

The text reproduced below was prepared by the expert from ETRTO to amend the note 9 page 6 of document ECE/TRANS/WP.29/2010/63 agreed at the last WP29 of June 2010.

Text deleted is shown by strikethrough and new text in bold font

A	PROPOSAL

σm can be estimated by measuring n times (where n ≥ 53) the whole procedure described section 4 of Annex 6 to this Regulation, for at least five the p alignment tyres (where p ≥ 5), assuming that the variances of the p alignment (where p ≥ 5) at least five tyres are homogeneous, as follows:

(corrected)

Where:

i	= either 1 or 5 corresponding to each of the tyres is the counter from 1 to p for the number of alignment tyres

j	= is the counter from 1 to n for the number of repetitions of each measurement for a given tyre

n	= is the number of repetitions of tyre measurements (n ≥ 3)

p    = is the number of alignment tyres (p ≥ 5).

B	JUSTIFICATION

This formula was extrapolated from ISO 28580, introducing a number of
alignment tyres greater or equal to 5. However, there was a confusion
between the number n of measurement repetitions (n greater or equal to 3)
and the number of tyres (greater or equal to 5). This confusion was made
both in the text : "measuring n times (where n >= 5)" and in the first
formula, giving the value of "sigma m" from the individual values "sigma
m,i" obtained for each alignment tyre. In addition "i" index, for the
tyres, was restricted to the values of 1 and 5, not taking into
consideration all the 5 or more alignment tyres. To bring a remedy to this
and correct the formula giving the value of "sigma m", it is proposed to
set "i" as a counter varying from 1 to "p", where "p" is introduced as the
number of alignment tyres.

- - - - -