Proposal for a modification of the Vienna Convention,

(Regarding inconsistencies between the Convention and

the technical Regulations on vehicles)

Article 1 (Definitions)

Subparagraph (u) is amended as follows:

“Articulated vehicle” means:

- A combination of vehicles comprising either a motor vehicle and a semi-trailer coupled to the motor vehicle, provided that no transport of persons is operated in the semi-trailer,

- Or a motor vehicle made up of at least two rigid sections which articulate relative to one another and in which free movement of persons is possible».

Article 13 (speed and distance between vehicles)

A new paragraph 1.a is added; it has to be read:

« 1.a 	Driving assistance systems with an influence on the way the vehicle is driven, namely in order to enhance the roadholding or the respect of a safety distance between vehicles, shall not be considered contrary to the principles mentioned in paragraphs 1 et 5 of this Article and mentioned in paragraph 5 of Article 8 as well, provided that:

-  either these systems can be switched off at any time,

-  or they only optimise at technical level some functions which operating depends only on the driver,

-  or they operate in case of emergency when the driver lost or is about to loose the control of the vehicle».

Article 32 (Rules of the use of lamps)

-	In paragraph 4 (English version only), the words «front fog maps» are replaced by «front fog lamps».

-    The second sentence of paragraph 7 is changed as follows:

«In this case, rear position lamps may be used together with the front lamps».

-   Paragraph 12 is changed as follows:

«Reversing lamps may be used only when the vehicle is reversing or about to reverse; optional additional reversing lamps may remain illuminated during slow forward manoeuvres».

# Annex 1 to the Convention

Paragraph 2

-	Subparagraph (a), in the English version the word “indicator” has to be replaced by “gauges”;

-	Subparagraph (c) is changed as follows:

« (c)	Rear view mirrors/devices for indirect vision so designed as to yield backwards under moderate pressure so that they no longer project beyond the permissible maximum width».

-	Subparagraph (d) is changed as follows:

« (d)	Side direction-indicators, marker lamps, position lamps and parking lamps provided that such projection does not exceed a few centimetres».

-	In paragraph 2two new items (f) and (g) are added :

« (f)	Service-door lighting,

(g)	Exterior courtesy lamp».

Annex 5 (Technical provisions regarding vehicles and trailers)

- 	Annex 5 is completed by paragraph 1.a as follows:

« 1.a Vehicles that have been type approved in conformity with the Regulations annexed to the « Agreement concerning the adoption of uniform technical prescriptions for wheeled vehicles, equipment and parts which can be fitted and/or be used on wheeled vehicles and the conditions for reciprocal recognition of approvals granted on the basis of these prescriptions”, done at Geneva on 20 March 1958, including the Amendments, are deemed to be in conformity with this Annex, provided that the above mentioned Regulations are not contrary to the principles defined in paragraph 5 of Article 8, to paragraphs 1 and 1.a of Article 13 and to Article 32 of the Convention».

- 	In chapter I, D (Braking of motorcycles), a new subparagraph (b) is added:

Previous subparagraph (b) becomes subparagraph (c).

- Chapter II (Vehicle lighting and light-signalling devices), the following paragraphs are changed as follows:

- Chapter III (Other requirements), paragraph 47is changed as follows:

Appendix to Annex 5 is replaced by the following provisions

## APPENDIX