|  | United Nations | ECE/TRANS/WP.29/GRSP/2010/34 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 16 September 2010 Original: English English and French only |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

Working Party on Passive Safety

Forty-eighth session

Geneva, 7–10 December 2010

Item 10 of the provisional agenda

Regulation No. 16 (Safety-belts)

Proposal for Supplement 2 to the 06 series of amendments

Submitted by the experts from Belgium and Germany*

The text reproduced below was prepared by the experts from Belgium and Germany in order to introduce prescriptions for side-facing seats in vehicles of category M3 (Class II, III and B). The text supersedes ECE/TRANS/WP.29/GRSP/2010/25. The modifications to the current text of the Regulation are marked in bold for new or strikethrough for deleted characters.

I.	Proposal

Insert a new paragraph 1.6., to read:

“1.6.	At the request of the manufacturer, it also applies to safety-belts designated for installation on side-facing seats in vehicles of categories M2 (Class II, III or B) and M3 (Class II, III or B).1”

Insert new paragraphs 2.18.2. to 2.18.4., to read:

“2.18.2.	“Forward-facing seat” means a seat which can be used whilst the vehicle is in motion and which faces towards the front of the vehicle in such a manner that the vertical plane of symmetry of the seat forms an angle of less than + 10° or - 10° with the vertical plane of symmetry of the vehicle.

2.18.3.	“Rearward-facing seat” means a seat which can be used whilst the vehicle is in motion and which faces towards the rear of the vehicle in such a manner that the vertical plane of symmetry of the seat forms an angle of less than + 10° or – 10° with the vertical plane of symmetry of the vehicle.

2.18.4.	“Side-facing seat” means a seat which can be used whilst the vehicle is in motion and which faces towards the side of the vehicle in such a manner that the vertical plane of symmetry of the seat forms an angle of 90° (+ 10°) with the vertical plane of symmetry of the vehicle.”

Annex 16, the table, insert a new column “side-facing”, to read:

| “Annex 16 Minimum requirements for Safety-belts and Retractors |
| --- |
| Vehicle Category | Forward facing seating positions | Rear facing Seating positions | Side-facing |
|  | Outboard seating positions | Centre seating position |  |  |
|  | Front | Other than front | Front | Other than front |  |  |
| M1 | … | … | … | … | … |  |
| M2 < 3.5 t | … | … | … | … | … |  |
| M2 > 3.5 t | … | … | … | … | … |  |
| M3 | … | … | … | … | … | Br3,Br4m and Br4Nm |
| N1 | … | … | … | … | … |  |
|  | … | … | … | … | … |  |
| N2 | … | … | … | … | … |  |
| N3 | … | … | … | … | … |  |

…”

II.	Justification

1.	This proposal introduces the necessary requirements to take into account the installation of side-facing seats under certain conditions.

2.	As the proposal does not influence requirements, test procedures, etc. there is no need to distinguish between safety-belts approved before the date of entry force of Supplement 1 to the 06 series of amendments to Regulation No. 16 and those approved after that date.

3.	Consequently there are no transitional provisions defined.

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2006–2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.