Explanation of the proposal for Supplement 3 to the 07 series of amendments to Regulation No. 14 (Safety belt anchorages) submitted by the experts from Germany*

The presentation below was prepared by the expert from Germany regarding the marking of ISOFIX top tether to explain the intention and the content of the proposal to amend the text of paragraph 5.2.4.5. of Regulation No. 14 as proposed in document ECE/TRANS/WP.29/GRSP/2010/30 to be amended by Informal document GRSP-48-15. Pictures were taken from the informal document GRSP-41-18 presented by Consumers International at the 41st session of GRSP in May 2007.

# The problem:

# The proposal:

# Option 1

(a)	Designing all such anchorages in the ISOFIX top tether anchorage zone as ISOFIX top tether anchorages

# The proposal:

# Option 2

(b)	Marking only the ISOFIX top tether anchorages using one of the symbols, or its mirror image, as set out in figure 13 of Annex 9; or

# The proposal:

# Option 3

(c)	Marking such anchorages not in accordance with (a) or (b) above with a clear indication  that these anchorages should not be used in combination with any ISOFIX anchorages system.