|  | United Nations | ST/SG/AC.10/C.3/2011/29–ST/SG/AC.10/C.4/2011/5 |
| --- | --- | --- |
|  | Secretariat | Distr.: General 5 September 2011 Original: English |

Committee of Experts on the Transport of Dangerous Goods
and on the Globally Harmonized System of Classification
and Labelling of Chemicals

| Sub-Committee of Experts on the Transport of Dangerous Goods | Sub-Committee of Experts on the Globally Harmonized System of Classification and Labelling of Chemicals |
| --- | --- |
| Fortieth session | Twenty-second session |
| Geneva, 28 November – 7 December 2011 Item 2 (c) of the provisional agenda Listing, classification and packing: miscellaneous | Geneva, 7 – 9 December 2011 Item 2 (a) of the provisional agenda Updating of the Globally Harmonized System of Classification and Labelling of Chemicals (GHS): physical hazards |

Amendments to the classification flow chart/decision logic for self-reactive substances and organic peroxides

Transmitted by the International Council of Chemical Associations (ICCA)

I.	Introduction

1.	Over the last years the classification flow chart/decision logic for self-reactive substances and organic substances was discussed in the International Group of experts on explosion risks of Unstable Substances, working group of Energetic and Oxidising Substances (IGUS-EOS) for several times.

2.	Apart from a minor change that was introduced in the second part of both flowcharts in the ninth edition of the Recommendations (1995), these flow charts have remained unchanged since their first introduction more than 25 years ago. At the time of introduction of the flow chart, nearly all substances were transported and handled in packagings. However, over time the transport and handling in intermediate bulk containers (IBCs) and tanks became more and more common practise. It was felt in the discussion in IGUS-EOS that this should have some consequences for the classification flow chart.

3.	Further, it was observed that various issues that determine the classification of substances or mixtures are addressed in the text of the Model Regulations and the Globally Harmonized System of Classification and Labelling of Chemicals (GHS), however are not incorporated in the flow chart. These aspects can easily be overlooked by users not so familiar with the detailed text. As they are part of the classification procedure, it is more appropriate to include them in the classification flow charts for both self-reactive substances and organic peroxides. These flow charts are identical.

4.	It was agreed during the last IGUS-EOS meeting that ICCA would prepare a proposal to both subcommittees on TDG and GHS.

II.	Background to the proposal

A.	Aspects not changing the classification principles

5.	The following aspects are addressed in the text of the Model Regulations and GHS but are not incorporated in the classification flow charts:

(a)	No type G classification possible if the Self-Accelerating Decomposition Temperature (SADT) of  the substance is < 60 ºC in a 50 kg packaging (see Model Regulations 2.4.2.3.3.2 (g) , 2.5.3.3.2 (g) and GHS 2.8.2.2 (g), 2.15.2.2 (g));

(b)	No type G classification possible when a diluent is used with a boiling point < 150 ºC (see Model Regulations 2.4.2.3.3.2 (g) , 2.5.3.3.2 (g) and GHS 2.8.2.2 (g), 2.15.2.2 (g)).

6.	In the proposed amended flow chart these two aspects are addressed in the new boxes 14 and 17 respectively. The introduction of these boxes will not lead to a change in the existing classification principles.

B.	Aspects changing the classification principles for Type G substances and mixtures

7.	In addition, in IGUS-EOS there was a discussion on the requirements for exemption (i.e. Type G in the flow charts). It was felt that for solid materials the existing requirements need not to be changed (there are to our knowledge no type G solids transported in IBCs or tanks). For liquids however, when transported or handled in IBCs or tanks, Type F classification seems to be the most appropriate solution for the following two reasons:

(a)	Despite the type G properties, for liquids adequate pressure relief requirements may be needed when transported and handled in IBCs or tanks (for Type G there are no requirements at all);

(b)	The requirement for type G substances or mixture is an SADT < 60 ºC in a 50 kg packaging. However, the substance or mixture in an IBC or tank will have a lower SADT compared to the SADT in a 50 kg packaging. When classified as Type F, the actual SADT of the substance in IBC or tank has to be chosen for the determination of control- and emergency temperatures, when required according to the criterion for temperature control.

8.	In the proposed amended flow chart these two aspects are addressed in the new boxes 15 and 16 and the wording in exit F (in flow chart Model Regulations).

III.	Proposals

A.	Proposal alternative 1

9.	Based on the background given in sub-sections 2.1 (no change in classification principles) and 2.2 (change in classification principles for Type G substances) the following is proposed (changes in grey shading):

(a)	In the Model Regulations replace Figures 2.4.1 and 2.5.1 by the following new scheme:

Figure 2.4.1: Flow chart scheme for self-reactive substances
Figure 2.5.1: Flow chart scheme for organic peroxides

Figure 2.4.1: Flow chart scheme for self-reactive substances (cont'd)

Figure 2.5.1: Flow chart scheme for organic peroxides (cont'd)

(b)	In GHS replace Figures 2.8 and 2.15 by the following new decision logic:

Decision logic 2.8 for self-reactive substances and mixtures
	Decision logic 2.15 for organic peroxides

Decision logic 2.8 for self-reactive substances and mixtures (cont'd)
Decision logic 2.15 for organic peroxides (cont'd)

(Note: the grey shaded wording in boxes 10 and 13 are just corrections.)

B.		Proposal alternative 2

10.	Based on the background given in sub-section 2.1 (no change in classification principles), it is proposed to take proposal alternative 1 with the deletion of boxes 15 and 16 and deleting the grey shaded wording in exit F of the proposed flow chart scheme in paragraph 9 (a) (i.e. proposal for the Model Regulations).

IV.	Consequential amendments

11.	If alternative 1 or alternative 2 proposal is adopted, the following flow chart is to be amended accordingly:

–	In the Manual of Tests and Criteria the flow chart given in Figure 20.1 (a)

12.	If alternative 1 proposal is adopted:

(a)	In the Model Regulations add to 2.4.2.3.3.2 (g) , 2.5.3.3.2 (g) the following sentence: when the formulation is a liquid to be transported in IBCs or tanks it should be defined as self-reactive substance type F;

(b)	In the Model Regulations add to 2.5.3.3.2 (g) the following sentence: when the formulation is a liquid to be transported in IBCs or tanks it should be defined as organic peroxide type F;

(c)	In GHS add to 2.8.2.2 (g) the following sentence: when the substance or mixture is a liquid to be handled in IBCs or tanks it should be defined as self-reactive substance type F;

(d)	In GHS add to 2.15.2.2 (g) the following sentence: when the substance or mixture is a liquid to be handled in IBCs or tanks it should be defined as organic peroxide type F.

# Footnotes

In accordance with the programme of work of the Sub-Committee for 2011-2012 approved by the Committee at its fifth session (refer to ST/SG/AC.10/C.3/76, para. 116 and ST/SG/AC.10/38, para. 16).

# Text boxes

What is 
the effect of heating it

under defined

confinement

?

Is the

organic peroxide/
self-reactive substance

to be considered for transport 
in IBCs or tanks,

or for exemption
 ?

17.2 No

17.1 Yes

16.1 Yes

16.2 No

15.2 No

15.1 Yes

Box 17

Box 16

Box 15

Box 14

14.2 No

14.1 Yes

Is 
a diluent with a 
boling point of 
< 150 °C  used 
?

Is it to be
considered for transport in IBCs or tanks?

Is it a solid ?

Is the SADT < 60 ºC
in a 50 kg package
?

SHALL BE CONSIDERED FOR EXEMPTION

ACCEPTED FOR TRANSPORT IN PACKAGES OF NOT MORE THAN 400KG/450 LITRES

What is its 
explosive power
?

Exit E

Box 12

Box 13

Box 11

13.2 None

13.1 Low

12.3 None

12.2 Low

12.1 Not low

11.2 No

11.1 Yes

Exit G

Exit F

from box 9

MAY BE CONSIDERED FOR TRANSPORT IN IBCS OR TANKS IF ADEQUATE PRESSURE RELIEF CAN BE PROVIDED UNDER THE CONDITIONS SPECIFIED BY THE COMPETENT AUTHORITY. OTHERWISE: ACCEPTED FOR TRANSPORT IN PACKAGES OF NOT MORE THAN 400KG/450 LITRES

SUBSTANCE/MIXTURE

Box 1
Test A

Type D

Type C

Type B

Type A

Box 9
Test E

Box 8
Test E

Box 7
Test E

Box 6
Test D

Box 3

Test C

Box 5
Test C

Box 4
Test C

Box 2
Test B

?

confinement

of heating it under defined

What is the effect

?

confinement

of heating it under defined

What is the effect

?

confinement

of heating it under defined

What is the effect

?

a deflagration

Can it propagate

?

a deflagration

Can it propagate

8.4 None

8.3 Low

8.2 Medium

?

in package

deflagrate rapidly

Does it

?

a deflagration

Can it propagate

?

detonate as packaged

Can it

2.2 No

2.1 Yes

Violent

8.1

Yes, rapidly

3.1

3.3 No

3.2 Yes, slowly

4.3 No

4.2 Yes, slowly

Yes, rapidly

4.1

?

explode as packaged

Can it

10.2 No

Box 10
Test G

10.1 Yes

9.4 None

9.3 Low

Violent

9.1

Medium

9.2

Violent

7.1

7.4 None

7.3 Low

7.2 Medium

6.2 No

6.1 Yes

5.3 No

5.2 Yes, slowly

Yes, rapidly

5.1

?

a detonation

Does it propagate

1.3 No

1.2 Partial

1.1 Yes

go to box 11

from box 9

Box 11

11.2 No

11.1 Yes

?

exemption

be considered for

than 400 kg/450 l or to

Packaged

Box 13
Test E

confinement

of heating it under defined

What is the effect

?

in packages of more

Type E

Type G

Type F

?

400 kg/450 l

Packaged in

packages of more than

Box 14
Test H

Box 12
Test F

17.2 No

16.2 No

15.2 No

14.2 No

13.2 None

14.1 Yes

16.1 Yes

15.1 Yes

17.1 Yes

Box 17

Box 16

Box 15

13.1 Low

12.3 None

Is it a solid

12.2 Low

12.1 Not low

?

explosive power

What is its

Is the SADT < 60 ºC

?

in a 50 kg package

?

Is a diluent with

< 150 ºC used

a boiling point of

?

ACCEPTED FOR TRANSPORT IN PACKAGES OF NOT MORE THAN 25 KG NET MASS WITH “EXPLOSIVE” SUBSIDIARY RISK LABEL

ACCEPTED FOR TRANSPORT IN PACKAGES OF NOT MORE THAN 50 KG NET MASS

ACCEPTED FOR TRANSPORT IN PACKAGES OF NOT MORE THAN 50 KG NET MASS

NOT ACCEPTED FOR TRANSPORT IN THAT PACKAGING

Can it

explode as packaged

for transport

?

What is 
the effect of heating it

under defined

confinement

?

What is the

effect of heating it

under defined

confinement

?

What is 
the effect of heating it

under defined 
confinement

?

Does it

deflagrate rapidly

in package

?

Can it

detonate as packaged

for transport

?

Does it
propagate a
detonation?

Can it

propagate a

deflagration

?

Can it

propagate a

deflagration

?

Can it

propagate a

deflagration

?

8.4 No

8.3 Low

8.2 Medium

2.2 No

Box 2

2.1 Yes

Violent

8.1

Box 8

Yes, rapidly

3.1

3.3 No

3.2 Yes, slowly

Box 3

4.3 No

4.2 Yes, slowly

Box 4

Yes, rapidly

4.1

10.2 No

Box 10

10.1 Yes

9.4 No

9.3 Low

Violent

9.1

Box 9

Medium

9.2

Violent

7.1

Box 7

7.4 No

7.3 Low

7.2 Medium

6.2 No

Box 6

6.1 Yes

5.3 No

5.2 Yes, slowly

Box 5

Yes, rapidly

5.1

1.3 No

1.2 Partial

Box 1

1.1 Yes

Exit D

Exit C

Exit B

Exit A

go to box 11

SELF-REACTIVE SUBSTANCE / ORGANIC  PEROXIDE