UN/SCETDG/39/INF.10

Committee of Experts on the Transport of Dangerous Goods and on the Globally Harmonized System of Classification and Labelling of Chemicals Sub-Committee of Experts on the Transport of Dangerous Goods 6 June 2011 Thirty-ninth session Geneva,20 – 24 June 2011 Item 5 (d) of the provisional agenda Miscellaneous proposals of amendments to the Model Regulations on the Transport of Dangerous Goods: miscellaneous

Assignment of Bulk Container Codes

Transmitted by the expert from Germany

Introduction

1.	Germany presented a proposal on the revision of some bulk container instructions to the 15th session of the IMO Sub-Committee on Dangerous Goods, Solid Cargoes and Containers (Document DSC 15/3/4, content reproduced as annex to this document). A review of the assignment of BK Codes in the UN Model Regulations and in the IMDG Code had shown, that the assignment is not fully harmonized. Several proposals for amendments were made, taking into consideration if the substances are allowed to be transported in cargo holds of bulk carriers under the IMSBC Code as well as if they are permitted to be carried in bulk by European road regulations (ADR).

2.	Having considered document DSC 15/3/4, noting the multimodal dimension of the proposed amendments, DSC 15 invited the delegation of Germany to submit a similar proposal to the TDG Sub-Committee for consideration an action, as appropriate.

3. 	Based on the approach presented in the annexed document, taking into consideration  the current discussion in the Joint meeting on the revision of the system of bulk codes in RID/ADR/AND (see documents ECE/TRANS/WP.15./AC.1/2011/15 and ECE/TRANS/WP.15./AC.1/2011/15) the Sub-Committee is invited to discuss the possible amendments below.

Proposal

4.	For some those entries to which BK 2 has been assigned in the IMDG Code and which may be transported in bulk according to ADR as well as according to the IMSBC Code,  BK Codes should be allocated in the UN Model Regulations, too. This would affect some substances of class 4.2 packing group III (UN Nos. 1363, 1386, 2217 and 2793) and some substances of class 4.3 packing group III (UN 1398 and 1435). For the latter, it should be considered if transport in bulk should be limited to BK 2. This would be aligned with the existing provisions of European land transport which require hermetically sealed openings (see ECE/TRANS/WP.15./AC.1/2011/15).

5.	It is to question whether bulk container codes are appropriate for substances of class 6.1 packing group II and III. If not BK 2 should be deleted for UN 3243. Furthermore, the annexed DSC Submission proposes that BK codes should not be assigned to substances with a subsidiary risk of 6.1. If the Sub-Committee follows that approach, BK 2 should be deleted for UN 1408. Consequently, the provisions for UN 1395, 1446 and 1469 should be harmonized in the IMDG Code with UN Model Regulations and BK 2 should be deleted in the IMDG-Code.

6.	Furthermore, the Sub-Committee is invited to discuss a rationalized approach. Currently, BK Codes are assigned to some substances of class:

	4.1, packing group II and III,

	4.2 packing group III,

	4.3 packing group II and III,

	4.3, subsidiary risk 6.1, packing group III,

	5.1, packing group II and III,

	6.1, packing group II,

	6.2,

	8, packing group II and

	9 packing group II and III.

7.	Apart from the class and the packing group further aspects should be taken into account, for example the shape of the transported material.

8.	Based on the outcome of the discussion, the expert from Germany is willing to submit a formal proposal for the next meeting.

Annex

| Sub-Committee of dangerous goods, Solid cargoes and containers 15th session Agenda item 3 | DSC 15/3/4 01 June 2011 Original: ENGLISH |
| --- | --- |

Amendments to the IMDG Code and Supplements, including harmonization of the IMDG Code with the UN Recommendations on the Transport of Dangerous Goods

Revision of bulk container instructions for UN 1402, UN 1395, UN 1446, UN 1469,
UN 2211 and UN 3314

submitted by Germany

| SUMMARY |
| --- |
| Executive summary: | This document proposes amendments to the bulk container instructions for UN 1402, UN 1395, UN 1446, UN 1469, UN 2211 and UN 3314 in order to harmonize them with the relevant provisons of UN Model Regulations |
| Strategic direction: | 5.2 |
| High-level action: | 5.2.3 |
| Planned output: | 5.2.3.1 |
| Action to be taken: | Paragraph 13 |
| Related documents: | none |

Background

1.	Authorities in Germany received an inquiry of a shipping line, seeking advice whether the transport of UN 1402 Calcium carbide, packing group I, is permitted in bulk containers. There was an offer from a shipper to carry such cargo and the dangerous goods list of the IMDG Code shows "BK2" under the respective entry. But there were doubts, whether it is really intended by the Code to permit packing group I substances in bulk containers. The Authority recommended not to accept this cargo for shipment, as the involved hazard appeared not to be acceptable.

2.	The IMDG Code permits UN 1402 packing group II in bulk containers only when the provisons of SP 951 are complied with, i.e "bulk container shall be hermetically sealed and under a nitrogen blanket". However, this special provision is not assigned to the entry of UN 1402 packing group I.

3.	Further investigation showed that the assignment of BK 2 codes to certain UN numbers in the IMDG Code is not consistent with the UN Model Regulations. In some of these cases however, the IMSBC Code permits the transport of the relevant substances in the cargo holds of bulkcarriers. A list of all UN numbers concerned is shown in the annex to this document.

Discussion

4.	Germany is of the opinion that the assisgnemnt of bulk container instructions in the UN Model Regulations and in the IMDG Code should be harmonized as far as possible. It is recognized that the regulations for sea transport are more restrictive and only closed bulk containers are accepted. But it should not be the case that the IMDG Code permits the use of bulk containers where the Model Regulations do not.

5.	For UN 1363, UN 1386, UN 1398, UN 1435, UN 2217 and UN 2793 the Model Regulations do not provide a bulk container instruction. The IMDG Code however assigns "BK2". These commodities are permitted in the cargo holds of bulk carriers under the IMSBC Code and they are also permitted under certain conditions to be carried in bulk by European road regulations (ADR). Therefore it is considered appropriate to amend the Model Regulations and to permit the use of closed bulk containers for these commodities both for the sea and for the land mode of transport.

6.	For UN 2211 and UN 3314 the Model Regulations do not provide a bulk container instruction. The IMDG Code however assigns "BK2". These commodities are not permitted in the cargo holds of bulk carriers under the IMSBC Code. They are permitted to be carried in bulk by European road regulations (ADR), but only under the condition that the containers are sufficiently ventilated. Therefore it is considered appropriate to maintain the bulk container instruction "BK2" in the IMDG Code, but to add a special provision that only ventilated bulk containers are permitted.

7.	For UN 1395, UN 1446 and UN 1469 the Model Regulations do not provide a bulk container instruction. The IMDG Code however assigns "BK2". These commodities have a subsidiary risk of class 6.1, therefore it seems not appropriate to permit the transport in bulk containers, which do not provide a proper confinement for toxic substances. In this context it should be noted that chapter 4.3 of the IMDG Code (use of bulk containers) does not consider at all the specific hazards of substances with toxic properties. As well, European road regulations do not permit the bulk transport of these commodities due to the toxic subsidiary risk. Notwithstanding these considerations, the IMSBC Code permits the shipment of these substances in the cargo holds of bulk carriers, however there are specific safety measures required, such as gastightness of bulkheads, detectors for quantitative measurements of gas concentrations, face masks for the crew etc. As this equipment is not generally available on a ship carrying cargo transport units and as the product information provided to the crew of such ships does not contain all those details that are contained in the cargo information for bulk carriers, these cargoes should be not permitted in bulk containers under the IMDG Code, and the Code should be harmonized with the Model Regulations.

8.	For UN 1402 packing group I, shipment in bulk containers shall be prohibited for safety reasons. The entry "BK2" in the dangerous goods list of the IMDG Code for this commodity is obviously an error and should be corrected by the next Errata & Corrigenda. For UN 1402 packing group II, special provison 951 of the IMDG Code applies and shipment in bulk containers is only permitted if the container is hermetically sealed and if the cargo is under a nitrogen blanket. However, the fact that a container is hermetically sealed should be tested and approved. As chapter 6.9 of the IMDG Code does not contain any provsions for hermetically sealed bulk containers, it seems appropriate to transport this cargo in tanks only. As the tank instruction "T3" and the tank provision "TP33" are already assigned for this entry, the bulk container instruction should be deleted.

Proposals

9.	In the dangerous goods list for UN 1402 packing group I the entry "BK2" should be deleted. This should be communicated by the next Errata & Corrigenda.

10.	In the dangerous goods list for UN 1402 packing group II and for UN 1395, UN 1446 and UN 1469 the entry "BK2" should be deleted.

11.	A special provision SP 9XX should be assigned to UN 2211 and UN 3314:

"SP 9XX If transported in closed bulk containers the containers shall be sufficiently ventilated to prevent the build-up of an explosive atmosphere in the containers."

12.	The Sub-Committee is asked to express the opinion, that the UN Model regulations should permit the use of closed bulk containers for UN 1363, UN 1386, UN 1398, UN 1435, UN 2217 and UN 2793 and to permit the use of open or closed bulk containers for UN 2211 and UN 3314, the latter only provided that closed bulk containers are sufficiently ventilated.

Action requested of the Sub-Committee

13.	The Sub-Committee is invited to consider the discussions above and proposals set forth in paragraph 9 to 12 and take action as appropriate.

Annex

Bulk container instructions in the UN Model Regulations and in the IMDG Code and respective provisions in the IMSBC Code

| UN Number | UN Model Regulations | IMDG Code | IMSBC Code | Proper Shipping Name |
| --- | --- | --- | --- | --- |
| 1334 | BK 1 BK 2 | BK 2 | Not permitted | Naphthalene |
| 1350 | BK 1 BK 2 | BK 2 | Permitted | Sulphur |
| 1363 | BK not assigned | BK 2 | Permitted | Copra |
| 1376 | BK 2 | BK 2 | Permitted | Iron oxide spent |
| 1386 | BK not assigned | BK 2 | Permitted | Seed cake, containing vegetable oil |
| 1395 | BK not assigned | BK 2 | Permitted | Aluminium ferrosilicon powder |
| 1398 | BK not assigned | BK 2 | Permitted | Aluminium silicon powder uncoated |
| 1402 | BK not assigned | BK 2 | Not permitted | Calcium carbide |
| 1408 | BK 2 | BK 2 | Permitted | Ferrosilicon |
| 1435 | BK not assigned | BK 2 | Permitted | Zinc ashes |
| 1438 | BK 1 BK 2 | BK 2 | Permitted | Aluminium nitrate |
| 1446 | BK not assigned | BK 2 | Permitted | Barium nitrate |
| 1454 | BK 1 BK 2 | BK 2 | Permitted | Calcium nitrate |
| 1469 | BK not assigned | BK 2 | Permitted | Lead nitrate |
| 1474 | BK 1 BK 2 | BK 2 | Permitted | Magnesium nitrate |
| 1486 | BK 1 BK 2 | BK 2 | Permitted | Potassium nitrate |
| 1495 | BK 1 BK 2 | BK 2 | Not permitted | Sodium chlorate |
| 1498 | BK 1 BK 2 | BK 2 | Permitted | Sodium nitrate |
| 1499 | BK 1 BK 2 | BK 2 | Permitted | Sodium nitrate and potassium nitrate mixture |
| 1910 | Regulated only by air | Not regulated | Permitted | Calcium oxide (Lime) In IMSBC Code MHB |
| 1942 | BK 1 BK 2 | BK 2 | Permitted | Ammonium nitrate |
| 2067 | BK 1 BK 2 | BK 2 | Permitted | Ammonium nitrate based fertilizer A |
| 2071 | Regulated by air and sea | BK 2 | Permitted | Ammonium nitrate based fertilizer B |

| UN Number | UN Model Regulations | IMDG Code | IMSBC Code | Proper Shipping Name |
| --- | --- | --- | --- | --- |
| 2211 | BK not assigned | BK 2 | Not permitted | Polystyrene beads |
| 2213 | BK 1 BK 2 | BK 2 | Not permitted | Paraformaldehyde |
| 2216 | regulated only by sea | BK 2 | Permitted | Fish meal, stabilized |
| 2217 | BK not assigned | BK 2 | Permitted | Seed cake, oil extracted |
| 2793 | BK not assigned | BK 2 | Permitted | Ferrous metal borings |
| 2814 | BK 1 BK 2 | BK 2 | Not permitted | Infectious substances affecting humans |
| 2900 | BK 1 BK 2 | BK 2 | Not permitted | Infectious substances affecting animals only |
| 2912 | - | - | Permitted | Radioactive material LSA I |
| 2913 | - | - | Permitted | Radioactive material SCO I |
| 2950 | BK 2 | BK 2 | Not permitted | Magnesium granulate, coated |
| 2969 | BK 1 BK 2 | BK 2 | Permitted | Castor beans |
| 3170 | BK 1 BK 2 | BK 2 | Permitted | Aluminium smelting by-products |
| 3175 | BK 1 BK 2 | BK 2 | Not permitted | Solids containing flammable liquid |
| 3243 | BK 1 BK 2 | BK 2 | Not permitted | Solid containing toxic liquid |
| 3244 | BK 1 BK 2 | BK 2 | Not permitted | Solid containing corrosive liquid |
| 3291 | BK 2 | BK 2 | Not permitted | Clinical waste |
| 3314 | BK not assigned | BK 2 | Not permitted | Plastics moulding compound |
| 3373 | BK 1 BK 2 | BK 2 | Not permitted | Biological substance category B |
| 3377 | BK 1 BK 2 | BK 2 | Not permitted | Sodiumperborate monohydrate |
| 3378 | BK 1 BK 2 | BK 2 | Not permitted | Sodium carbonate peroxyhydrate |

# Footnotes

Document DSC 15/3/4 contained some editorial mistakes, therefore the annex reproduces the original submission of Germany.