|  | United Nations | ECE/TRANS/WP.29/2011/5 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 23 December 2010 English Original: English and French |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

153rd session

Geneva, 8–11 March 2011

Item 4.6.3 of the provisional agenda

1958 Agreement – Consideration of draft amendments

to existing Regulations submitted by GRRF

Proposal for Supplement 12 to Regulation No. 13-H (Brakes of M1 and N1 vehicles)

Submitted by the Working Party on Brakes and Running Gear*

The text reproduced below was adopted by the Working Party on Brakes and Running Gear (GRRF) at its sixty-eighth session to align the provisions in Regulation No. 13-H with those in Regulation No. 90 regarding the information necessary for the type approval to identify the original replacement discs and drums. It is based on ECE/TRANS/WP.29/GRRF/2009/25, as amended by Annex II to the report (ECE/TRANS/WP.29/GRRF/68, para. 21). It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration.

Insert a new paragraph 2.24., to read:

"2.24.	"Identification Code" identifies the brake discs or brake drums covered by the braking system approval according to this regulation. It contains at least the manufacturer's trade name or trademark and an identification number."

Insert new paragraphs 12.8. to 12.10., to read:

"12.8.	As from the official date of entry into force of the Supplement 12 to the original version of this Regulation, no Contracting Party applying this Regulation shall refuse to grant approval under this Regulation as amended by Supplement 12 to the original version of this Regulation.

12.9.	Contracting Parties applying this Regulation shall continue to grant approvals to those types of vehicles which comply with the requirements of this Regulation as amended by Supplement 11 to the original version of this Regulation during the 12 month period which follows the date of entry into force of supplement 12 to the original version of this Regulation.

12.10.	Contracting Parties applying this Regulation shall not refuse to grant extensions of approval according to this Regulation as amended by Supplement 11 to the original version of this Regulation."

Annex 1, items 7. to 7.2., amend to read:

"7.	Make and type of brake linings, discs and drums:

7.1.	Brake linings

7.1.1.	Brake linings tested to all relevant prescriptions of Annex 3

7.1.2.	Alternative brake linings tested in Annex 7

7.2.	Brake disc and drums

7.2.1.	Identification code of brake discs covered by the braking system approval

7.2.2.	Identification code of brake drums covered by the braking system approval

"

Annex 1, Appendix 1, items 2. to 2.2., amend to read:

"2.	Make and type of brake linings, discs and drums:

2.1.	Brake linings

2.1.1.	Brake linings tested to all relevant prescriptions of Annex 3

2.1.2.	Alternative brake linings tested in Annex 7

2.2.	Brake disc and drums

2.2.1.	Identification code of brake discs covered by the braking system approval

2.2.2.	Identification code of brake drums covered by the braking system approval
	"

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2006–2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.