|  | United Nations | ECE/TRANS/WP.29/2011/13 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 17 December 2010 English Original: English and French |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

153rd session

Geneva, 8–11 March 2011

Item 4.7.7 of the provisional agenda

1958 Agreement – Consideration of draft amendments

to existing Regulations submitted by GRE

Proposal for Supplement 13 to the 01 series of amendments to Regulation No. 53 (Installation of lighting on L3 vehicles)

Submitted by the Working Party on Lighting and Light-Signalling (GRE)*

The text reproduced below was adopted by the Working Party on Lighting and Light-Signalling (GRE) at its sixty-fourth session. It is based on ECE/TRANS/WP.29/GRE/2009/67, as amended by Annex XIII to the report, and on ECE/TRANS/WP.29/GRE/2010/25, as amended by Annex XIV to the report. It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration (ECE/TRANS/WP.29/GRE/64, paras. 40 and 41).

Paragraph 5.13., amend to read:

"5.13. 		Colours of the lights

The colours of the lights referred to in this Regulation shall be as follows:

driving beam headlamp: 			white

passing beam headlamp:			white

direction-indicator lamp: 			amber

stop lamp: 					red

rear-registration plate lamp: 		white

front position lamp: 				white or amber

rear position lamp: 				red

rear retro-reflector, non-triangular: 		red

side retro-reflector, non-triangular: 	amber at the front

amber or red at the rear

vehicle-hazard warning signal: 		amber

front fog lamp : 				white or selective yellow

rear fog lamp : 				red"

Paragraph 6.3.7., amend to read:

"6.3.7. 	May not be "reciprocally incorporated" with any other lamp, except amber front position lamp."

Paragraph 6.4.7., amend to read:

"6.4.7. 	 "Tell-tale"

Tell-tale optional; where fitted, this tell-tale shall be a tell-tale consisting of a non-flashing warning light which comes on in the event of the malfunctioning of the stop lamps."

Paragraphs 6.6.1., amend to read:

"6.6.1. 	Number

One or two	if coloured white

or

Two (one per side)		if coloured amber"

Paragraphs 6.6.7., amend to read:

"6.6.7. 	Other requirements

When the front position lamp is reciprocally incorporated in the front direction indicator lamp, the electrical connection shall be such that the position lamp on the same side as the direction indicator lamp is switched off when the direction indicator lamp is flashing."

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2006–2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.