|  | United Nations | ECE/TRANS/WP.29/2011/19 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 21 December 2010 English Original: English and French |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

153rd session

Geneva, 8–11 March 2011

Item 4.10.3 of the provisional agenda

1958 Agreement – Consideration of draft Corrigenda

to existing Regulations submitted by GRE

Proposal for Corrigendum 1 to Supplement 15 to the 02 series of amendments to Regulation No. 7 (Front and rear position lamps, stop lamps and end-outline marker lamps)

Submitted by the Working Party on Lighting and Light-Signalling*

The text reproduced below was adopted by the Working Party on Lighting and Light-Signalling (GRE) at its sixty-fourth session. It is based on ECE/TRANS/WP.29/GRE/2010/30, not amended. It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration (ECE/TRANS/WP.29/GRE/64, para. 25).

Paragraph 6.1.7.2., amend to read:

"6.1.7.2.	The lamp shall comply with the minimum intensity required in the table of standard light distribution in space as shown in Annex 4 when any one light source has failed. However, for lamps designed for only two light sources, 50 per cent of the minimum intensity in the axis of reference of the lamp shall be considered sufficient, provided that a note in the communication form states that the lamp is only for use on a vehicle fitted with an operating tell-tale which indicates when any one of these two light sources has failed."

Paragraph 6.1.8., shall be deleted.

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2006–2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.