|  | United Nations | ECE/TRANS/WP.29/2011/24 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 21 December 2010 English Original: English and French |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

153rd session

Geneva, 8–11 March 2011

Item 4.10.8 of the provisional agenda

1958 Agreement – Consideration of draft Corrigenda

to existing Regulations submitted by GRE

Proposal for Corrigendum 1 to Supplement 36 to the 03 series of amendments to Regulation No. 37 (Filament lamps)

Submitted by the Working Party on Lighting and Light-Signalling*

The text reproduced below was adopted by the Working Party on Lighting and Light-Signalling (GRE) at its sixty-fourth session. It is based on informal document GRE-64-29 as reproduced in Annex II to the report. It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration (ECE/TRANS/WP.29/GRE/64, para. 8).

Annex 1, sheet H16/3, correct to read:

"…

| … | … | … | … |
| --- | --- | --- | --- |
| Objective values | Watts | 26 max. | 26 max. |
|  | Luminous flux | 500 + 10% / -15% |  |
| Reference luminous flux: 370 lm at approximately 12 V |
| Reference luminous flux: 500 lm at approximately 13.2 V |
| Reference luminous flux: 550 lm at approximately 13.5 V |

"

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2006–2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.