|  | United Nations | ECE/TRANS/WP.29/2011/91 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 3 May 2011 English only |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

154th session

Geneva, 21–24 June 2011

Item 4.16.3 of the provisional agenda

1958 Agreement – Consideration of draft Regulations

Proposal for amendments to ECE/TRANS/WP.29/2011/78 (Proposal for a new Regulation on Lane Departure Warning System)

Submitted by the representative of Italy*

The text reproduced below was prepared by the representative of Italy to replace in the draft Regulation on Lane Departure Warning System, the information on visible lane marking applicable in Italy. It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration.

Proposal

Annex 3, Table 1, the section concerning Italy should be replaced by the following:

"Table 1

| PATTERN | COUNTRY | WIDTH |
| --- | --- | --- |
| Left edge lane marking | Centre line | Right edge lane marking |  | Left edge lane marking | Centre line | Right edge lane marking |
|  | Definition of lane width for the purpose of this Regulation |  |
|  | ITALY Secondary and Local |  |
|  | ITALY Motorway |  |
|  | ITALY Main |  |

"

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.

# Text boxes

15 cm

25 cm

3 m

25 cm

12 or 15 cm

10 or 12 cm

12 or 15 cm

4.5 m

Lane width

Lane width

15 cm

3 m

4.5 m

7.5 m

4.5 m

25 cm

25 cm