|  | United Nations | ECE/TRANS/WP.29/GRE/2011/26 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 14 January 2011 Original: English English and French only |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

Working Party on Lighting and Light-Signalling

Sixty-fifth session

Geneva, 28–31 March 2011

Item 4(a) of the provisional agenda

Regulation No. 48 (Installation of lighting and

light-signalling devices)

Proposal for Supplement 8 to the 04 series of amendments

Submitted by the expert from the Netherlands*

The text reproduced below was prepared by the expert from the Netherlands, to ensure that the Working Party on Lighting and Light-Signalling (GRE) will not inadvertently make any future changes to the colour allowed for front positions lamps, which are installed on vehicles covered by this Regulation. The modifications to the existing text of the Regulation are marked in bold for new or strikethrough for deleted characters.

I.	Proposal

Paragraph 5.15., insert a reference to footnote8 and a new footnote8 and amend to read:

"5.15.		The colours … following:

Main-beam headlamp:			White

…

Rear registration plate lamp:		White

Front position lamp:				White

Rear position lamp:				Red

…

Rear retro-reflector, triangular:		Red

Front retro-reflector, non-triangular:	Identical to incident light9

Side retro-reflector, non-triangular:	….

…

Conspicuity marking:	White to the front;

White or yellow to the side;

Red or yellow to the rear10

…"

Paragraph 6.2.4.2., the reference to footnote 10 and footnote 10, renumber as footnote11

Paragraph 6.2.9., the reference to footnote 11 and footnote 11, renumber as footnote12

Paragraph 6.3.4.2., the reference to footnote 12 and footnote 12, renumber as footnote13

Paragraphs 6.3.5., 6.3.6.1.1. and 6.5.8., the reference to footnote 13 and footnote13, renumber as footnote14

Paragraph 6.19., the reference to footnote14 and footnote 14, renumber as footnote15

Paragraph 6.19.7.3., the reference to footnote15 and footnote 15, renumber as footnote16

Paragraphs 6.21.4.1.3. and 6.21.4.2.3., the reference to footnote 16 and footnote16, renumber as footnote17

Paragraph 6.22.4.1.2., the reference to footnote17 and footnote17, renumber as footnote18

Paragraph 6.22.7.4.3., the reference to footnote18 and footnote18, renumber as footnote19

Paragraph 6.22.7.4.5., the reference to footnote19 and footnote19, renumber as footnote20

Paragraph 6.22.9.1., the reference to footnote20 and footnote20, renumber as footnote21

II.	Justification

1.	This proposal is aimed to ensure that GRE will not inadvertently make any future changes to the color allowed for front positions lamps, which are installed on vehicles covered by this Regulation (categories M, N and O). Only the color white is allowed, whilst amber front position lamps are exclusively reserved for use on motorcycles.

2.	During the sixty-fourth session of GRE, following the decision to allow amber front position lamps on motorcycles (Regulation No. 53), it was agreed that the option of the amber front position lamp would not be accepted for Regulation No. 48 (see ECE/TRANS/WP.29/GRE/64, para. 40).

3.	The expert from the Netherlands appreciates the fact that the Secretariat has mentioned this agreement in the official report. However, he is of the opinion that it would be even better to mention it, by means of a footnote, in Regulation No. 48 as well. Thus, it will serve as permanent reminder, also to future generations of GRE experts.

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2006–2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.

Only the colour white is allowed for the light emitted by front position lamps installed on vehicles covered by this Regulation. Front position lamps emitting light of the colour amber are only allowed to be installed on vehicles covered by Regulation No. 53 (motorcycles)."