|  | United Nations | ECE/TRANS/WP.29/GRE/2011/38 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 22 July 2011 Original: English English and French only |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

Working Party on Lighting and Light-Signalling

Sixty-sixth session

Geneva, 4-6 October 2011

Item 5(d) of the provisional agenda

Collective amendments - Regulation Nos. 98 and 123

Proposal for collective amendments to Regulations Nos. 98 and 123

Submitted by the expert from the Working Party "Brussels 1952"*

The text reproduced below was prepared by the expert from the Working Party "Brussels 1952" (GTB) to simplify the photometric test requirements. The modifications to the existing text of the Regulation are marked in bold for new or strikethrough for deleted characters.

- Proposal

Proposal for Supplement 3 to the 01 series of Regulation No. 98

The table in Paragraph 6.2.5., delete line 1

Proposal for Supplement 3 to the 01 series of Regulation No. 123

Annex 3, Table 1, amend to read:

"

|  | Position /deg | passing beam |
| --- | --- | --- |
| tabled requirements expressed in cd | horizontal | vertical | class C | class V | class E | class W |
|  | No | Element | at/ | from | to |  | at |  | min | max | min | max | min | max | min | max |
| Part A | 1 | B50L 4/ | L | 3.43 |  |  | U | 0.57 | 50 4/ | 350 |  | 50 | 350 |  | 50 | 625 | 8/ | 50 | 625 |  |
|  | 2 | HV 4/ | V |  |  |  | H |  | 50 4/ | 625 |  | 50 | 625 |  | 50 |  |  | 50 |  |  |
|  | 3 | BR 4/ | R | 2.5 |  |  | U | 1 | 50 4/ | 1750 |  | 50 | 880 |  | 50 | 1750 |  | 50 | 2650 |  |
|  | 8a | S50, S50LL, S50RR S50 + S50LL + S50RR 5/ |  |  |  |  | U | 4 | 63 190 7/ |  |  |  |  |  | 63 190 7 |  |  | 63 190 7 |  |  |
|  | 9a | S100, S100LL, S100RR S100 + S100LL + S100RR 5/ |  |  |  |  | U | 2 | 125 375 7/ |  |  |  |  |  | 125 375 7/ |  |  | 125 375 7/ |  |  |
|  | 18 | Emax 3/ |  |  |  |  |  |  | 16900 | 44100 |  | 8400 | 44100 |  | 16900 | 79300 | 8/ | 29530 | 70500 | 2/ |
| Part B (bending modes): Table 1 Part A applies, however with the lines Nos. 1, 2, 7, 13 and 18 being replaced by those listed hereunder |
| Part B | 1 | B50L 4/ | L | 3.43 |  |  | U | 0.57 | 50 4/ | 530 |  |  | 530 |  |  |  |  |  | 790 |  |
|  | 2 | HV 4/ |  |  |  |  |  |  | 50 4/ | 880 |  |  | 880 |  |  |  |  |  |  |  |
|  | 18 | Emax 6/ |  |  |  |  |  |  | 10100 | 44100 |  | 5100 | 44100 |  | 10100 | 79300 | 8/ | 20300 | 70500 | 2/ |

"

Annex 5., paragraph 1.2.1.1., amend to read:

"1.2.1.1.	For the following values of the passing beam and its modes, the maximum unfavourable deviation may be respectively:

(a)	maximum values at point B50L 170 cd equivalent 20 per cent and 255 cd equivalent 30 per cent;

(b)	maximum values at zone III, HV and segment BLL: 255 cd equivalent 20 per cent and 380 cd equivalent 30 per cent;

(c)	maximum values at segments E, F1, F2 and F3: 170 cd equivalent 20 per cent and 255 cd equivalent 30 per cent;

(d)	minimum values at BR, P, S 50, S 50LL, S 50RR, S 100, S 100LL, S 100RR, at the groups S 50 + S 50LL + S 50RR and S 100 + S 100LL + S 100RR, and those required by footnote 4/ of Table 1 in Annex 3 of this Regulation (B50L, HV, BR, BRR, BLL): half of the required value equivalent 20 per cent and three quarter of the required value equivalent 30 per cent."

Annex 7., paragraph 1.2.1.1., amend to read:

"1.2.1.1.	For the following values of the passing beam and its modes, the maximum unfavourable deviation may be respectively:

(a)	maximum values at point B50L 170 cd equivalent 20 per cent and 255 cd equivalent 30 per cent;

(b)	maximum values at zone III, HV and segment BLL: 255 cd equivalent 20 per cent and 380 cd equivalent 30 per cent;

(c)	maximum values at segments E, F1, F2 and F3: 170 cd equivalent 20 per cent and 255 cd equivalent 30 per cent;

(d)	minimum values at BR, P, S 50, S 50LL, S 50RR, S 100, S 100LL, S 100RR, at the groups S 50 + S 50LL + S 50RR and S 100 + S 100LL + S 100RR, and those required by footnote 4/ of Table 1 in Annex 3 of this Regulation (B50L, HV, BR, BRR, BLL): half of the required value equivalent 20 per cent and three quarter of the required value equivalent 30 per cent."

- Justification

This collective amendment simplifies the photometric testing procedures by:

(a)	Removing the HV test point from Regulations Nos. 98 and 123 because it is already included in the measurement of Zone III. This approach is already adopted in Regulation No. 112.

(b)	Grouping the overhead sign test points in Regulation 123 following the approach already adopted in Regulations Nos. 112 and 123.

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106, ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.